## Slide 1: The Air and Water Connection of Mercury in Watersheds Presentation for ORSANCO Technical Committee
Martin Risch Research Hydrologist
February 9, 2016

## Slide 2
Overview
Mercury in the air and water
Mercury in the Ohio River
Wet and dry deposition of atmospheric Hg
Stream Hg loads and yields
The air and water connection of mercury in watersheds—a case study from Indiana
Hg mass balance for the Ohio River watershed

## Slide 3: The Mercury (Hg) Problem
Human activities release Hg to air and water.
Some inorganic Hg is microbially converted to organic methylmercury (MeHg), which accumulates in aquatic and terrestrial food chains.
MeHg enters humans and wildlife through dietary exposure, typically from fish consumption.
MeHg is a potent neurotoxin, with potential harm to cardiovascular and endocrine systems. Effects are documented in young and adult humans.
MeHg at very low levels poses a health risk, especially to the young and unborn.

## Slide 4
Nearly all fish tissue samples have detectable Hg, assumed to be mostly MeHg.
Fish-consumption advisories for Hg affect people who fish -- in Indiana 1 of 6 residents, 1 of 2 adults.
Sport fishing, commercial fishing, and subsistence fishing bring freshwater and marine fish MeHg into family diets.
Hg water-quality criteria protecting wildlife are frequently exceeded.
Fish communities, and aquatic and terrestrial wildlife show adverse effects from MeHg.

## Slide 5: Mercury is a Global Issue
Biannual International Conference on Hg as a Global Pollutant – scientific consensus on Hg issues
Minamata Convention on Hg – global treaty to protect human health & environment, 128 signing nations in 2013, United Nations Env. Program
Development of Hg monitoring network in SE Asia
USEPA Mercury and Air Toxics Standards rule will reduce Hg emissions from power plants; additional rules affect other Hg emissions sources
Mix of upward and downward trends in regional Hg wet deposition in US

## Slide 6: Hg is a Local Issue-- the Ohio River
126
607
721
846
918
ORSANCO Historic Hg monitoring site
2010 Hg Recon monitoring site & downstream mile mark
607
118
USGS and ORSANCO Hg Recon, 2010
Seasonal streamflow-integrated samples for low-level Hg and MeHg at 6 sites

## Slide 7: 2010 Hg concentrations were low, when compared to historic Hg data from Ohio River and Indiana streams
Concentrations (ng/L) | Ohio River recon 2010 (n = 18) | Indiana streams1 2001-2006 (n=411) | Ohio River2 2007-2009 (n=90)
Hg minimum | 0.87 | 0.24 | <1.5
Hg maximum | 13.0 | 28.2 | 50.8
Hg median | 1.41 | 2.32 | 3.63
MeHg minimum | <0.04 | <0.04 | no data
MeHg maximum | 0.13 | 0.66 | no data
MeHg median | 0.04 | 0.10 | no data
1 Risch and others, 2010.
2 ORSANCO written commun., 2010; 5 of the 6 sites sampled in 2010 w/o mile 118 site

## Slide 8: Ohio River Hg & MeHg mostly particulate, related to streamflow & suspended sediment, such that when streamflow is > 200,000 cfs, suspended sediment is > 200 mg/L, Hg can be > 12 ng/L criteria. Instantaneous stream Hg loads varied by location and season.
45 to 414 kg/hr
1 to 49 kg/hr
0.5 to 5 kg/hr
upstream
downstream

## Slide 9: The Hg cycle in terrestrial and aquatic ecosystems

## Slide 10: The Air- Water- Fish Mercury Connection– a case study from Indiana Watersheds
Interpretation of available baseline data from 5-6 yrs of Hg monitoring, using streamflow, precipitation, Hg sources, and land cover
Fish Hg Water Hg Air Hg
Wastewater Emissions
26 watersheds: spatial and statistical analysis - Hg & MeHg concentrations in water; stream Hg loads; atmospheric Hg loads; Hg in fish - correlations with Hg sources & land cover
Land Cover

## Slide 11: Mercury Monitoring
STREAMS Seasonal sampling 4 times /yr at 26 stream gages/bridges, 5 years Integrated stream-width & stream-depth isokinetic method; trace-metals protocols
PRECIPITATION
Weekly samples at 5 MDN sites, 6 years Automated collector & raingage
Low-level Hg supplies, central laboratory
Hg concentration X precipitation = Hg wet deposition

## Slide 12
26 Watersheds:
152 to 74,293 km2
Drain 80% of Indiana
22% area outside IN
5 major river systems
6 sites downstream from dams and lakes
Monitoring data:
411 stream samples
2,162 wet-deposition samples from 9 NADP MDN sites
1,731 fish samples--
358 rivers, 59 lakes;
83% state locations

## Slide 13
Stream Hg Concentrations
Statistically: High Hg
90th percentile
high median and maximum
High MeHg:
90th percentile
high median and maximum
High Fish Hg
> 300 ug/kg
90th percentile
high median and maximum

## Slide 14
5-year average annual stream Hg yields per watershed range 0.72 to 45.2 ug/m2
median 4.21 ug/m2
Annual stream Hg loads calculated with streamflow regression model LOADEST (Runkel and others, 2004) using 5 years of streamflow and Hg concentration data at sites not downstream from reservoirs; Hg load = g/year stream Hg yield = stream Hg load/drainage area
Next: the air Hg connection

## Slide 15
Atmospheric Mercury Species and Fate

## Slide 16
x
=
Precipitation-weighted average annual Hg concentration map
Hg concentration data for 5 Indiana & 4 nearby NADP MDN sites
Average annual precipitation map from 151 NWS Coop sites (127 in Indiana)
Concentration X Precipitation
Hg wet deposition load (mass per area per time)

## Slide 17
Comparison:
Average annual atmospheric Hg wet deposition loads per watershed range 9.6 to 14.8 mg/m2;
median 11.3 mg/m2
Average annual stream Hg yields per watershed range 0.72 to 45.2 mg/m2;
median 4.21 mg/m2
Hg wet-deposition map for 26 watersheds

## Slide 18
Concentration from 9 MDN sites
Precipitation from 151 NWS Coop sites
Mercury wet-deposition map for Indiana, 2006
Effect from area of high precipitation
Area of high precipitation
Area of high Hg concentration
Effect from area of high Hg concentration

## Slide 19
Total atmospheric Hg deposition =
Atmospheric wet Hg + dry Hg deposition
Dry Hg deposition calculations
Seasonal median daily air Hg concentrations at monitoring sites in IN (Risch and others, 2007)
Reactive gaseous Hg, particulate bound Hg, gaseous elemental Hg (GEM)
Vertical deposition velocity for 3 Hg species (Seigneur and others, 2004) with GEM in forest and non-forest
Air Hg concentration x vertical deposition velocity x number of days = seasonal dry Hg deposition rate
Annual Hg dry deposition = sum of seasonal rates
Added 5.6 to 13.6 mg/m2 per year dry Hg to wet Hg

## Slide 20
Ratios of average annual stream Hg yield per watershed to average annual atmospheric Hg wet deposition load –
Generally, more atmospheric Hg wet deposition loading than stream Hg yield
Urbanized watersheds had more stream Hg yield than could be attributed to atmospheric Hg wet deposition

## Slide 21
Three conditions inferred from ratio of stream Hg yield to atmospheric Hg load per watershed
Stream Hg yields less than atmospheric Hg loads; excess Hg retained in the landscape or re-emitted to the air; other Hg inputs are minor part of stream Hg yield
Stream Hg yields generally equal to atmospheric Hg loads; other Hg inputs offset atmospheric Hg retained in landscape or re-emitted to the air
Stream Hg yields greater than atmospheric Hg loads; other Hg inputs (point sources) contribute more Hg than any atmospheric Hg retained in landscape or re-emitted to air
Next: Hg sources

## Slide 22: Positive statistical correlations of moderate strength (Kendall’s tau 0.4 to 0.5, high is 0.7) where 50% of variation in dependent variable is explained by independent variable
Average annual stream Hg load & average annual atmospheric Hg load
Average stream Hg concentrations & annual Hg emissions, number emission sources
Average stream Hg concentrations & number of outfalls, number of major > 1 MGD facilities
Average annual stream Hg yield & percentage of urban land cover
Average stream Hg concentrations & percentage of forest land cover

## Slide 23
64 POTW’s with Hg in 510 samples
4,144 permitted outfalls, including 1, 044 major facilities (> 1 MGD)

## Slide 24
Annual Hg emissions & number of stationary sources per watershed
Percentage land cover types per watershed grouped from 20 land cover classes

## Slide 25
Hg Mass Balance (Inflow = Outflow) Inflow Hg Atmospheric Hg directly to water + Atmospheric Hg indirectly reaches water + Hg in discharges to the water
= Outflow Hg
Ohio River Watershed
Can be calculated with methods developed by USGS

## Slide 26
Wet Hg deposition – National Atmospheric Deposition Program (NADP) Mercury Deposition Network
Air Hg concentrations for dry Hg deposition – NADP Atmospheric Mercury Network
Inferential model of vertical deposition velocity for each Hg species, by land cover (NADP, 2016; Zhang and others, 2012)
Litterfall Hg Deposition – NADP Litterfall Mercury Network
Precipitation data – National Weather Service, Midwest Climate Data Center
Sources of information for total (wet and dry) atmospheric Hg loads to watersheds and forest landscapes (2007-2014)

## Slide 27
7-Year Mean Annual Hg Wet Deposition*
2000-2010
*Risch et al, 2012
37 Hg-monitoring sites from 3 networks
1,541 precipitation gages in 2 networks

## Slide 28
Hydrologic model - Water Availability Tool for Environmental Resources (WATER)
Uses topographic and soil properties, with a regionally calibrated hillslope-hydrology model (TOPMODEL)
Uses impervious-surface model (TR-55), and climatic model to uniformly estimate streamflow for tributary watersheds
Calculate Hg in runoff by hydrologic response units of forested, agricultural, and developed land cover using published release rates
Methods to compute release of atmospheric Hg from landscape to streams and watersheds – estimates of stream Hg yield of atmospheric Hg

## Slide 29
Annual atmospheric Hg loading by 12-digit hydrologic unit
Direct atmospheric Hg deposition to Ohio River
Uniform estimates for streamflow by 12-digit hydrologic unit
Release of atmospheric Hg to precipitation runoff according to land cover = Hg indirectly reaches tributaries
Stream Hg loads/yield of atmospheric Hg
Initial interpretations for selected tributary watersheds to show the high-low ranges of Hg deposition, Hg stream yield, streamflow, and landscape factors
Interpretations of Hg mass balance for Ohio River watershed and tributaries

## Slide 30: Acknowledgments
Risch, M.R., Baker, N.T., Fowler, K.K., Egler, A.L., and Lampe, D.C., 2010, Mercury in Indiana watersheds: U.S. Geological Survey Professional Paper 1780 http://pubs.usgs.gov/pp/pp1780/
Indiana Department of Environmental Management Office of Air Quality, Office of Water Quality
National Atmospheric Deposition Program http://nadp.sws.uiuc.edu/
Thank you!
mrrisch@usgs.gov