## Slide 1: Hg Trib Monitoring Agenda Item 8b ORSANCO Technical Committee Meeting 210, February 9-10, 2016
Methyl Mercury and Total Mercury

## Slide 2: Project Goals
Estimate annual mass load of mercury and methyl mercury from each Tributary
  Use daily flow data to model loads
Characterize the methylation efficiency of each basin (% methyl mercury )

## Slide 3: 15 Major Ohio River Tributaries
15 Watersheds >1,000 mi2
Capturing 84% of the 203,000 mi2 Ohio River Basin
Notes: Not monitored: Cache, Salt, Tradewater, Anderson, Blue, Eagle Ck, Kiniconnick, Mud, Guyandotte, Hocking, Little Muskingum, Little Kanawha, Wheeling Ck

## Slide 4: Methods
12 samples (monthly for one year) on each tributary
Collection Method:
  Single Vertical at the Centroid of Flow (VCF method)
  Ultra-clean Method 1669 (USEPA) Protocols
  Boat or bridge-based samples

## Slide 5: Sample Locations
Sample locations chosen for maximum drainage capture and proximity to USGS stream gauges

## Slide 6: Sample Locations

## Slide 7: Quality Assurance
Concern that lower reaches of tributaries are possibly impacted by Ohio River high water events
  Backwatering
    slow flows
    reduce solids
    Mixing water
Survey boat and necessary equipment unable to access higher reaches of the Beaver, Big Sandy, and Licking Rivers
Example: Beaver River mile 2, downstream of first dam
  Unable to launch above dam
  Procedure:
    Test SpCond above the Beaver Falls Dam
    Test SpCond at sample site to demonstrate no Ohio River influence at surface, middle, and bottom depths.
  Collect sample upstream of Dam (from bridge) if influence found

## Slide 8: Project Schedule
Currently conducting 4th events in February 2016
Final (Event 12) samples will be collected October 2016