## Slide 1: Source Water Protection Efforts Organics Detection System & Spill Notification
Technical Committee Meeting,
February 10-11, 2016
Covington, KY

## Slide 2: 2015 Organics Detection System (ODS)
15 active ODS sites screening river water for volatile organic compounds (VOC’s)
  30 routine, calibrated contaminants
  Qualitative monitoring via 7 GC/MS units
  Nearly 15,000 river water samples analyzed in 2015 calendar year
  91% program efficiency for daily sample analysis, comparable to prior years
  2015 ODS monitoring did not find presence of any “unusual” volatile contaminants
  2015 ODS monitoring did not find contaminants at/above actionable threshold (2 ppb)
Notes: 9% differential due to a combination of lab renovations, reduced lab hours at some sites (either M-F or no overnight operations) and instrument repair
“unusual” as in not our calibrated list of target analytes.
-PQL 2ppb (operator calls) actionable as in increased monitroing confirmation of sample at GCMS, notification to downstream users

## Slide 3: 2016 Organics Detection System (ODS)
Pittsburgh (Allegheny River) ODS site will be re-activated, increasing number of operable sites to 16
Install 2 new computer systems to maintain compatibility with GCMS software upgrades
  Oldest GCMS (DSQII) units are vendor obsolete, efforts being made to maintain system-wide compatibility for communications network
Continue discussions with lower river utility interested in cooperative partnership with ORSANCO and the ODS (Henderson, KY)
Continue annual ODS site assessments at each location
  Maintain & foster lines of communication with ODS operators
  Inspect instrumentation, optimize analytical parameters and tweak system performance
Notes: DSQII on market since 2006. Vendor support through 2018 pending availability of parts.

## Slide 4: 2016 Organics Detection System (ODS)
  Maintain efficient field service repair turnaround times
  Increased field service workload due to in house coverage of all purge and trap, SAM units and Autosamplers, GC FID units, process GC units, computer hardware, some software, some website maintenance. (Coverage expired 12/31/15)
  Maintain appropriate supply inventory
  Active ODS Website for Utilities and Public
    Process GC online
    Driver for GCMS data currently under α-testing
  STAG Grant closeout
  ODS renovation grant (PRG345) terminates as of September 30, 2016
  ORSANCO 2nd Quarter FY17 all program costs shift back to PRG125 (state funded)
Notes: GCMS maintenance agreements only for GCMS portion of the system. Skeletonized the maintenance agreements to conserve operating costs
Alpha testing to identify and correct compatibility issues and glitches. Next step is to pull data from ODS GCMS site

## Slide 5: Spill Notification and Response Efforts
In 2015 ORSANCO technical staff reviewed 619 spill reports from the National Response Center (NRC)
  Covers 75 counties on the Ohio River and Industrialized Tributaries
Of those 227 ( 36.6%) were potential risks to Ohio River water quality
  1/3 of NRC reports listed “Unknown Oil” as the most frequently recorded spilled substance.
  Diesel was the second most commonly listed material on NRC Spill reports received.
  Quantities ranged from (min) to (max) in 2015

## Slide 6: 2016 Spill Notification and Response Efforts
Technical staff will continue 24 hour, weekly rotation of “Spills Duty”, reviewing NRC reports and other relevant sources of information and providing notification to DW utilities and other stakeholders as appropriate
Source Water protection staff will continue to review and summarize spill report data to gain insight into impacts on river quality
Improvements to Spills tracking database and reviewing technology advancements to improve/ program will continue

## Slide 7: Other
Continue providing input to Joint GCWW-NKY Water Source Water Protection Plan
Validation and “groundtruthing” of RSMS Hydrologic Model using ODS process GC data

## Slide 8: Comments/Questions?