## Slide 1: Beyond Microbeads: Microplastics in 29 Great Lakes Tributaries
Quantifying and characterizing the contribution of plastics from streams to lakes
Austin Baldwin, Steve Corsi, Pete Lenaker, Michelle Lutz - USGS Wisconsin Water Science Center
Sherri Mason - State University of New York at Fredonia
Manitowoc River, WI
Preliminary Results
ORSANCO Commission Meeting
February 10, 2016 – Covington, KY

## Slide 2
Great Lakes microplastics study
(Eriksen et al. 2013, Marine Pollution Bulletin)
Among first freshwater studies
Alarming numbers of plastic microbeads in some samples
Sherri Mason

## Slide 3
plastic particles less than 5mm in diameter
More than just microbeads!
Microplastics

## Slide 4: Sources to the environment
Cosmetics and personal care products
  Exfoliation
Soaps, scrubs, toothpastesa-d
Several hundred thousand per tubee
  Film formation, viscosity control
  Deodorants, sunscreen, lipstick,
    eye shadow, shaving cream,…d
  1 - 50 µm in diameter
- Pass through WWTPs, into streamsf
5gyres.org
newscientist.com
a. Gregory 1996; b. Barnes et al. 2009; c. Fendall and Sewell 2009; d. UNEP 2015; e. 5-Gyres Institute; f. McCormick et al. 2014

## Slide 5: Sources to the environment
Fibers from synthetic
clothing, textiles
  Up to 1,900/ garment/washing a
  Some pass through WWTPs, most capturedb-d
patagonia.com
Photo: Sherri Mason
a. Browne et al. 2011; b. Habib et al. 1998; c. Zubris and Richards 2005; d. Gasperi et al. 2015

## Slide 6: Sources to the environment
Mechanical and photodegradation of litter (“secondary” microplastics)
bags, bottles, nets, styrofoam, wrappers, cigarette butts, etca,b
a. Browne et al. 2007; b. Cole et al. 2011

## Slide 7: Sources to the environment
Preproduction pellets and powdersa
Pellets for bead blasting (boat hulls, engine parts)b
Overland sludge applicationc
Medical uses (drug delivery)d
Pheromone flakes
  3-layered PVC laminate, 2/ft2 e
Atmospheric deposition
  29-280 particles/m2/day f
sermopel.com
charlotteobserver.com
extension.iastate.edu
a. Mato et al. 2001; b. Gregory 1996; c. Zubris and Richards 2005; d. Browne et al. 2007;
e. MN Poll. Control Agency 2014; f. Gasperi et al. 2015

## Slide 8: Why should we care?

## Slide 9: Ingestion
Observed in >100 species (marine mammals, birds, fish, turtles, and invertebratesa-e)
  Plastics found in 82% of Lake Superior Lake Herring in 2013f
  Mussels in Nova Scotia: 126-178 microplastics/organismj
Bioaccumulation and trophic transfer up food chaing,h
a. Thompson et al. 2004; b. Teuten et al. 2009; c. Tourinho et al. 2010; d. Lavers et al. 2014; e. Derraik 2002;
f. S. Mason, personal comm.; g. Farrell and Nelson, 2013; h. Setala et al. 2014; i. Wright 2013;
j. Mathalon and Hill 2014

## Slide 10
Hazards poorly understood:
  Oysters exposed to microplastics: significant reductions in egg cells, slower-moving sperm, and fewer, slower-growing offspringa
  obstruction of digestive system, clogging of feeding appendages, nutritional deprivation, migration into the circulatory system, reduced immune response, and deathb,c,e,I
  some organisms are able to pass some sizes and shapes of microplasticsk
a. Sussarellu et al. 2016; b. Teuten et al. 2009; c. Tourinho et al. 2010; e. Derraik 2002; f. S. Mason, personal comm.; g. Farrell and Nelson, 2013; h. Setala et al. 2014; i. Wright 2013; k. Canniff and Hoang 2015
Ingestion

## Slide 11: Vectors for Contaminants
Flame retardants
Alkyl phenols
Antimicrobials
(triclosan)
Antioxidants (BPA)
Plasticizers
(phthalates)
Styrenes
PCBs
PAHs
DDT
Metals
Pathogens
Plastic additives
Sorption & accumulation
Barnes et al. 2009; Browne et al. 2007; Mato et al. 2001; Teuten et al. 2009;
Lavers et al. 2014; Betts 2008; McCormick et al. 2014

## Slide 12: Regulation Microbead-Free Waters Act of 2015 (goes into effect July 2017)
  Preempts state bans
  Prohibits “rinse-off cosmetics” containing plastic microbeads
    “…any solid plastic particle…used to exfoliate or cleanse the human body”
      Includes exfoliating soaps and toothpastes
      Excludes use as bulking agent/viscosity control in sunscreen, lotion, makeup, etc.
  No “biodegradable” loophole

## Slide 13: Regulation
  Polystyrene food containers
    Recently banned in NYC, DC, Seattle, San Francisco
  Plastic bags
    Bans/fees:
      International: Australian states, Bangladesh, China, Cameroon, Haiti, India, Ireland, Italy, Ivory Coast, Mali, Northern Ireland, Philippines, Rwanda, South Africa, Tanzania, Wales,…
      US: Hawaii, California (pending); >100 municipalities
    Effective: 20-fold decrease in plastic bag litter since Ireland’s bag tax (2002)

## Slide 14: Regulation
Plastic fibers
  The most abundant and ubiquitous microplastic
  Currently no regulations
  Green chemistry and engineering research
    Textiles which shed fewer fibers
    Washing machines which filter fibers

## Slide 15
Basin land use
GLRI Study 2014
29 tributaries
~22% of total inflow to the Great Lakes
Range of land uses
4 samples/site (2 baseflow, 2 stormflow)
agricultural
urban
natural

## Slide 16: Sample collection

## Slide 17: Sample processing

## Slide 18
Samples shipped to Sherri Mason’s lab at SUNY Fredonia for analysis

## Slide 19: Analytical Methods Sherri Mason’s lab at SUNY Fredonia
Sieved into three size classes:
0.355-0.999mm
1.00-4.749mm
>4.75mm
Floatation in salt water to
separate plastic particles
Digestion of organic
matter using wet
peroxide oxidation
Photos courtesy of
Tim Hoellein

## Slide 20
Bead/pellet
(personal care products,
preproduction pellets)
Fragments
Foam
(styrofoam)
Line
(nets, rope)
Particles counted & categorized
using light microscope
Photo: Sherri Mason

## Slide 21
Film
(bags, wrappers)
Fibers
(clothing,
textiles)
Photo: Sherri Mason

## Slide 22
Film
plant material
Tangle of fibers
Photo: Sherri Mason

## Slide 23: Results Particle sizes (106 samples)
Size range | Count | Percent of total
0.355-0.999mm | 28,110 | 72
1.00-4.749mm | 10,016 | 26
>4.75mm | 860 | 2
All sizes | 38,986 | 100

## Slide 24: Average concentration by tributary
53%
1.4%
34%
Median: 1.9 particles/m3
Max: 32 particles/m3
Fragments, foam, & film are more common in more urban basins
Fibers are ubiquitous

## Slide 25: Plastic particle concentrations vs WWTP effluent

## Slide 26: Concentrations vs streamflow conditions (57 baseflow, 49 stormflow)
*
*
*
* Statistically greater

## Slide 27
Estimated
daily loads
corresponding
to individual samples
0.2 – 5.2 Billion
Particles/Day

## Slide 28: Great Lakes vs Tributaries
* from Eriksen et al. 2013
*
*
*
1,950
3,540
10,200
Collected using same methods and mesh size,
and analyzed by the same lab
501,000

## Slide 29
(from Eriksen et al. 2013)
Great Lakes vs Tributaries: Relative abundance of particle types
Collected using same
methods and mesh size,
and analyzed by the same lab
Fragment
Fiber/line
Foam
Film
Pellet/bead

## Slide 30
Polymers and densities (from Driedger et al, ‘15)
0.01 – 0.04 g/cm3 Expanded polystyrene
0.89 – 0.98 Polyethylene
0.85 – 0.92 Polypropylene
1.13 – 1.16 Nylon
1.30 Cellulose acetate
1.38 – 1.41 Polyester
1.38 – 1.41 Polyester
1.38 – 1.41 PVC
(from Eriksen et al. 2013)
Foam
Film
Pellet/bead
Fragment
Fiber/line
Neutral
buoyancy

## Slide 31
Polymers and densities (from Driedger et al, ‘15)
0.01 – 0.04 g/cm3 Expanded polystyrene
0.89 – 0.98 Polyethylene
0.85 – 0.92 Polypropylene
1.13 – 1.16 Nylon
1.30 Cellulose acetate
1.38 – 1.41 Polyester
1.38 – 1.41 Polyester
1.38 – 1.41 PVC
(from Eriksen et al. 2013)
Foam
Film
Pellet/bead
Fragment
Fiber/line
Neutral
buoyancy

## Slide 32: Fibers in deep sea sediment
Woodall et al. 2014
Concentrations in sediment 4x greater than at ocean surface
Average of 13 fibers/50ml sediment

## Slide 33: Summary
Microplastics present in every tributary sample to date (up to 32 particles/m3)
Land use: litter-related particles (fragments, foams, films) more common in more urban watersheds; fibers seem unrelated to land use
Streamflow conditions: litter-related particles (fragments, foams, films) more common in stormflow conditions; fibers seem unrelated to flow conditions
Effluent contribution: no relationship observed, possibly due to large watershed sizes or quality of WWTP data
Tributary concentrations 10-1000 times greater than in Great Lakes
Fibers dominate over other particle types in tributaries (53% of all sampled particles)
  May be settling out in lakes
  Sources beyond WWTP effluent? (Atmospheric deposition? Overland sludge application?)
Beads/pellets rare (<2% of sampled particles)

## Slide 34: Acknowledgments
WI: Paul Reneau, Nic Buer, Ben Siebers, Troy Rutter, Becky Carvin, Ben Torrison, Joe Schuler, Molly Breitmun, Kyle Raimer
MI: Joe Duris, Cyndi Rachol, Rick Jodoin, Julia Giesen
IN: Cheryl Silcox, Ed Dobrowolski, Eric Looper, Andy Gorman, Howard Mills
OH: Stephanie Kula, Stephanie Janosy, Chad Toussant, Brian Mailot
NY: Brett Hayhurst, Ben Fisher
MN: Josh Larson, Russ Buesing, Jeff Copa
SUNY: Rachel Ricotta, Joylyn Kovachev, Katie Donnelly, Evan Miller
Questions?
Austin Baldwin
akbaldwi@usgs.gov

## Slide 36: Plastic particle concentrations vs urban land use