## Slide 1: 210th Technical Committee Meeting Agenda Item 13: Storm Water Abatement Report (informational item)
Steve Braun
sbraun@orsanco.org

## Slide 2: Status of MS4
At the 2012 Tech meeting ORSANCO began tracking progress of MS4 communities
MS4 – Municipal Separate Storm Sewer Systems
Regulation of Stormwater is Intended to reduce pollutants that are carried to waterways via storm sewers from urbanized areas, Industrial and Construction Activities
Carried out in two Phases
  Phase I
  Phase II

## Slide 3: Phase I MS4’s
Began in 1990
Permit needed if:
  Medium to Large Communities serving a population of >100,000
  Industry falls within one of 10 categories
  Construction Sites disturbing more than 5 acres of land
Must have an approved Storm Water Management Plan with 6 minimum controls
Must Conduct analytical Monitoring
Louisville is only Phase I MS4 along Ohio River

## Slide 4: Phase II MS4’s
Began in 1999
Permit needed if:
  Designated a small MS4 in urbanized areas defined by the US Census (>50,000 & Density of 1000 people/sq-mile)
  Construction sites disturbing 1-5 acres of land
Usually a general Permit that can cover multiple nearby MS4 communities (co-permittees)
Have an approved Storm Water Management Plan with 6 minimum controls
Usually does not require monitoring but reduce pollutants to the “Maximum Extent Possible”

## Slide 5: 6 Minimum Controls
Public Education and Outreach
Public Participation/ Involvement
Illicit Discharge Detection and Elimination
Construction Site Runoff Control
Post-Construction Runoff Control
Pollution Prevention/Good Housekeeping

## Slide 6: MS4’s along the Ohio River
69 Permitted MS4 Communities/Counties – could grow as population grows
Only one Phase I community (Louisville)

## Slide 7: MS4 State Details
Indiana
  16 Permittees
  All in compliance
  No changes from previous Year
Illinois
  No MS4 Communities
  No changes from previous year
Kentucky
  11 permittees, some are co-permittees
  4 Cities have at least one of the 6 minimum controls not in compliance
    Greenup County
    City of Flatwoods
    Oldham Co.
    Hardin Co.
  Paducah reached compliance in all 6 in 2015

## Slide 8: MS4 State Details cont.
Ohio
  11 Permittees
  No changes from previous year
  2 cities have at least one of the 6 minimum controls not in compliance
    Belmont Co.
    City of Portsmouth
PA
  20 Permittees
  All in Compliance
  No changes from previous year
WV
  11 Permittees
  Monitoring for TKN, Nitrite, Nitrate, Total Phosphorus and others at main outfall

## Slide 10: Questions? *informational item
Conclusion
Most of the MS4 Communities are in compliance
Very few changes from previous year