## Slide 1: Biological Water Quality
2015 Subcommittee Report

## Slide 2: Macroinvertebrate Program
Incorporated into ALU Assessment
  2 Methods collected at all sites
  Macro Index (ORMIn) est. 2012
  2015 ORMIn refinement
    ↑ Resolution of least & most disturbed sites
    ↑ Index response to disturbance
    Scores generated from Hester Dendy Deep (HDD) samples alone
    Hydrilla highly influences Multi-Habitat (MH) samples
      HDD to much lesser extent
      Will continue MH collection to account for Hydrilla
  Lab has 90 day return (End of February)
    Implications for 305(b)
MH
HDD

## Slide 3: Macroinvertebrate Program
Nutrient Criteria Development
  Continuous DO monitors set with HDDs
    May – October 2015, 30 min intervals
    77% retrieval, lost probes due to tampering
  Paired Abiotic Data Collections (3 rounds)
    ORSANCO funded (Nutrient/Macro Programs)
      Sestonic Nutrients, Chl-a
  USACE Louisville JT Myers co-op
    Funded abiotic collections/macro analysis
    Added BOD to analytes
  2015 Data offloaded, QA/QC ongoing

## Slide 4: 305(b) ALU Assessment Approach
full support
  mORFIn and ORMIn scores are greater than or equal to 20.0
    (i.e. a condition rating of ‘Fair’, ‘Good’, ‘Very Good’, or ‘Excellent’)
partial support
  one of the indices scores ‘Fair’ or better (>20.0)
  the other index scores ‘Poor’ (10.0 - 19.9)
non support
  pool in which both indices score ‘Poor’ (<20.0)
  or in which either or both indices score ‘Very Poor’ (<10.0)

## Slide 5: Blow out figure
2013 Pools

## Slide 6: 2015 Fish Survey Results
3-4 pools surveyed each year
15 random sites per pool (mORFIn scores averaged)
  Collectively represent the condition of the pool
  Biological criterion = avg. score of >=20.0 (Fair or better)
Pool | Macro Condition Rating | Fish Condition Rating | ALU Designation
Montgomery | Fair | Good | Met
Racine | Due Spring ‘16 | Good | Pending
J.T. Myers | Due Spring ’16 | Good | Pending

## Slide 7: Past vs. Present Surveys

## Slide 8: Understanding the Variation
Flows
  Can disrupt recruitment, habitat use, and sampling efficiency
Seasonality
  Fall sampling generally results in higher catch rates than summer
    Primarily influenced by young of year
Invasive Species
  Hydrilla continues to proliferate (above Meldahl L&D)
    ↓Functional habitat
    ↑Hypoxic conditions and dissolved oxygen range
River-wide Species Trends
  River-wide trends in several key mORFIn species (1991 – Present) cloud response to local conditions

## Slide 9: Racine Pool Revisit
 | July | September
mORFIn | 30.9* | 32.3*
# Species Score | 49.8 | 62.6
No. of Species | 40 | 48
# Great River Spp. | 0.0 | 15.56
Mooneye | 0 | 5
River Darter | 0 | 3
% Simple Lithophils | 13.2 | 5.9
% Invertivores | 78.7 | 58.1
Freshwater Drum | 9 | 361
Bluegill | 159 | 432
Orangespotted Sunfish | 5 | 28
Smallmouth Bass | 12 | 44
Spotted Bass | 10 | 57
* Not significantly different (Wilcoxon signed-rank test, p = 0.73)
Young of Year
Individuals

## Slide 10
From 1957 – 2014 (3400 sampling events) = 121 individuals
2015 Montgomery (15 sampling events) = 152 individuals
Notes: Trout perch – moderately intolerant…none in Beaver R, probably coming from lower Allegheny

## Slide 13: Average Pool Conditions
= Avg. Pool Macro Condition
= Avg. Pool Fish Condition
2011 - 2015
2011 - 2015
2010 - 2014
2010 - 2014

## Slide 14: BWQSC Recommendations
Approves use of final Macroinvertebrate Index for 2016 305(b) assessment of the Aquatic Life Use of the Ohio River
Accepts 2015 biological condition rating of ‘Good’ using fish and ‘Fair’ using macroinvertebrates for Montgomery Pool with no caveats
Accepts 2015 biological condition ratings of ‘Good’ using fish for Racine and J.T. Myers pools with no caveats
  Review of macroinvertebrate assessments is pending receipt of data (due in spring 2016)

## Slide 15: BWQSC Recommendations
Target 3 pools for 2016 fish and macroinvertebrate surveys (Willow Island, Greenup and Cannelton)
  Switch to 6 year cycle (3 pools/yr)
  Use available resources to study highest ranked need:
    Determine effects of Hydrilla on biotic indices
    Collect water/sediment chemistry at fish/bug sites
    Conduct revisits to gauge effects of seasonality & flows
    Conduct targeted biological sampling
    Coordinate mussel surveys at fish/bug sites
    Determine upstream extent of Asian Carp reproduction
    Determine impacts of microplastics on aquatic life
Notes: Mention study plans and rough budgets developed for each; plan still needs to be vetted through 305(b) committee.