## Slide 1: Mercury Speciation and Bioavailability In Power Plant Wastewater and Ambient Ohio River Samples: Final Results
Rob Reash
American Electric Power, Columbus, OH
ORSANCO Technical Committee Meeting, October 2017

## Slide 2: Basic Assumption
All (or most) of mercury is available for bioaccumulation. Thus, total Hg should be regulated.
But…..if this were true then fish tissue Hg levels should spike after high flow events.
ORSANCO Hg sampling shows the % MeHg of THg is 2 – 3%.

## Slide 3: Purpose of Study
Assess the operationally-defined bioavailability of Hg in various water sample types.
Evaluate whether treated wastewater contributes to increased Hg bioavailability.
Joint AEP/EPRI study.

## Slide 4: Mercury in Water Samples: Typical Analyses
Total Hg (and dissolved Hg) by EPA Method 1631
MeHg by EPA Method 1630* * Assumption is that the proportion of MeHg to THg represents the bioavailable fraction of all sum mercury species.

## Slide 5: Bioavailable Hg - Not Just MeHg
Bioavailable Hg consists of two components: MeHg and inorganic bioavailable Hg (IB – Hg) that may be readily converted to MeHg. WERF, 2009 * IB – Hg also called “reactive inorganic” Hg or “acid soluble” Hg.

## Slide 6: Thus, the amount of bioavailable Hg is:
(B – Hg)(ng/L) = (MeHg)(ng/L) + (IB – Hg)(ng/L) And, the fraction of bioavailable Hg is:
f (B – Hg) = [(MeHg + IB – Hg)/THg] * 100

## Slide 7: Basic Methodology
Collection and analysis of ambient, wastewater, and mixing zone (simulated) water samples.
Analysis of THg and dissolved Hg by CV-AFS.
Analysis of MeHg by IPC-CV-ICP-MS.
Analysis of acid-labile (IB) Hg by fluorescence
Other variables that influence Hg bioavailability (TSS, TOC, pH, sulfide, sulfate, TDS).

## Slide 8
OHIO
KENTUCKY
WEST VIRGINIA
PENNSYLVANIA
Muskingum
River
Cardinal Plant
(RK 122)
Mitchell
Plant
(RK 180)
Gavin
Plant
(RK 415)
Mountaineer
Plant
(RK 390)
Kanawha
River
Ohio
River
50 km
N

## Slide 9: Water Sample Types
Treated wastewater: > FGD landfill leachate > FGD purge stream w/ fly ash landfill leachate > FGD purge stream w/bottom ash sluice and miscellaneous low-volume streams >FGD purge stream (from 2° clarifier)
Mixing zone > 50:50 mix of wastewater and ambient Ohio R. > Worst-case (unrealistic) mixture
Ambient Ohio River > RM 73, 241, 260

## Slide 10: Results – Median Concentrations
Sample location | THg (ng/L) | Reactive Hg (ng/L) | MeHg (ng/L)
Ambient | 2.3a | 0.08a | 0.034a
Wastewater | 7.1b | 0.84a | 0.088a
Mixing zone | 5.3b | 3.46b | 0.078a

## Slide 11
6
5
4
3
2
1
50
40
30
20
10
% Bioavailable Hg
Ambient
Wastewater
Mixing Zone
Ambient
Wastewater
Mixing Zone
% MeHg
Sample Type

## Slide 12: Study Result Conclusions
Median concentrations of all Hg species were marginally higher in wastewater and mixing zone samples, however the median concentration of THg in wastewater samples was < 12 ng/L.
The median % MeHg was highest in ambient river samples, but this was < 2%. Consistent with ORSANCO monitoring data.
The median % bioavailable Hg ranged from 8% (ambient river) to 29% (mixing zone). Thus, the median bioavailable fraction of THg for all samples was < 30%.

## Slide 13: Recognition of the need to understand bioavailable Hg
Although THg concentration is relevant for any investigation of Hg-contaminated soils and sediments, the fraction available for methylation and, ultimately, for accumulation in the food web is of particular importance…Identification of the particular chemical species is less important than understanding the overall “available” Hg concentration.
G.N. Bigham et al. 2016. Biogeochemical controls on methylmercury in soils and sediments: implications for site management. Integrated Environmental Assessment and Management 13: 249 - 263

## Slide 14: Another persepective
Furthermore, given the difference in concentration distribution and bioavailability of inorganic Hg and MeHg from sediments, it is clear that management decisions based only on total Hg concentration will not result in a correct prediction of sediment Hg and MeHg bioavailability and/or toxicity.
Mason, R.P., and A.L. Lawrence. 1999. Concentration, distribution, and bioavailability of mercury and methylmercury in sediments of Baltimore Harbor and Chesapeake Bay, Maryland, USA. Environmental Toxicology and Chemistry 18: 2438 – 2447.

## Slide 15: Recommdations
ORSANCO and bordering states should allow Hg translator studies for facilities who wish to conduct Hg speciation studies.
Regulating total Hg, while convenient for permitting and reporting purposes, will often incur treatment costs with no promise of environmental benefits (reduced fish tissue Hg levels).