## Slide 1: The 215th Meeting of the ORSANCO Technical Committee Measures to Minimize Effects of Proposed Non-Federal Hydropower Development in the Upper Ohio River Basin Navigation System on Aquatic Resources
Rose Reilly
Rosemary.j.reilly@usace.army.mil
USACE Pittsburgh District
3 October 2017

## Slide 2: FERC Licensed Non-Federal Hydropower Projects
Federal Energy and Regulatory Commission (FERC) Authority: Federal Power Act.
  FERC has the exclusive authority to license most non-federal hydropower projects located on navigable waterways or federal lands, or connected to the interstate electric grid.
US Army Corps of Engineers (Corps) Involvement: Memorandum of Understanding with FERC, 20 July 2016
  “The Corps can allow the development of hydropower by non-Federal entities at suitable projects, provided that the installation and operation of the hydropower facility is found to be compatible with the purposes for which Congress authorized the project and would not be injurious to the public interest, and provided that there is no Federal interest in developing hydropower at the facility.”
  MOU encourages developer into a process that integrates Corps & FERC technical & permit requirements
  Currently no federal interest for development at any Pittsburgh District (District) facility.

## Slide 3: FERC Process
Non-federal applicant applies for Preliminary Permit. Good for 3 years.
FERC issues preliminary permits.
License secure the data & perform the acts required for the material that must accompany an application for license.
District provides standard comments on Permit Application.
Six basic Phases and corresponding District involvement following issuance of the Preliminary Permit.

## Slide 4: FERC Process
  Phase 1:
    Applicant receives permit.
    District typically provides technical information
  Phase 2:
    Applicant submits Pre-Application Document/Notice of Intent (PAD). Agency and public review, focus primarily environmental.
    Applicant files study plan scopes for agency and public review.
    The Applicant or FERC conducts a public scoping meeting
    Applicant evaluates project economics and environmental effects
    FERC prepares Scoping Document for their Environmental Assessment for agency and public review.
    Applicant submits Final License Application, serves as basis for the Environmental Assessment.

## Slide 5: FERC Process
  Phase 3:
    FERC accepts License application.
    Applicant & District begin coordination on Section 408 permission review plan.
    District typically reviews Preliminary Supporting Design Report.
    FERC issues NEPA document for public and agency review. Final Environmental Assessment is basis for License requirements (usually to support Finding of No Significant Impact).
  Phase 4:
    FERC issues license for construction and operation.
    All projects require a Corps approved Section 408 Permission document.
    Licensee begins engineering studies.
    Licensee typically makes initial submission of Section 404/10 Permit application.
    License includes requirements for District/FERC approval of various plans and memorandums of agreement between District and the licensee prior to construction and operation. District typically requires Adaptive Management Plan (AMP) addressing non-degradation requirements prior to commencement of construction.

## Slide 6: FERC Process
  Phase 5: Project Construction.
    District & licensee typically execute Operations MOA that identifies operation details acceptable to the District.
    District inspectors on-site for critical activities.
    Licensee typically conducts real-time water quality monitoring.
    Commissioning of plant involving testing required to document project viability.
  Phase 6: Project Operation.
    Plant operated in accordance with Operations MOA & AMP.
    Licensee continues real-time water quality monitoring (and possibly biological monitoring) conducted throughout license term.

## Slide 7: District Involvement Summary (opportunities to incorporate conditions to protect aquatic resources)
FERC License
  Review and Comment throughout process
  License Construction MOA, District & Licensee
  License Operational MOA, District & Licensee
  Interagency water quality monitoring plan
Section 408 Review (Corps NEPA-like process to assess impacts on Corps facilitates, resources & missions).
District Adaptive Management Plan (components incorporated into all of the above)

## Slide 8: Section 408
Section 14 Rivers and Harbors Act of 1889, codified in 33 U.S.C 408 (Section 408).
  “Authorizes the Secretary of the Army to grant permission to a private, public, tribal, or other federal entity for the temporary or permanent alteration or use of a US Army Corps of Engineers Civil Works project if the Secretary determines that the alteration or use will not be injurious to the public interest and will not impair the usefulness of the project.”
EC 1165-2-216.
  “Policy and Procedural Guidance for Processing Requests to Alter US Army Corps of Engineers Civil Works Projects Pursuant to 33 USC 408”
  “Provides policy & guidance for…processing requests by private, public, tribal, or other federal entities, to make alterations to, or temporarily or permanently occupy or use, any US Army Corps of Engineers (USACE) federally authorized civil works projects.”
EC = Engineering Circular

## Slide 9: District Hydropower Status Navigation Dams
All are Non-Federal
Licensed-Operating - 5
Licensed-Not Operating - 17
Total Permitted - 22

## Slide 10: District Hydropower Status Navigation Dams
[1] , no application for a preliminary permit has been submitted to the knowledge of the District Hydropower Coordinator.
[2] L/D will be removed

## Slide 11: District Hydropower Status Reservoirs
All are Non-Federal
Licensed-Operating - 4
Licensed-Not Operating - 2
Total Permitted - 6

## Slide 12: District Hydropower Status Reservoirs
[1] , no application for a preliminary permit has been submitted to the knowledge of the District Hydropower Coordinator.
[2] Project has been relicensed

## Slide 13: Pittsburgh District Hydropower Status

## Slide 14: Allegheny River Non-Federal Hydropower projects
Four Allegheny River L/Ds retrofitted with run-of-river hydroelectric plants
  L/D 5 (9.5 megawatt, placed in operation 1989)
  L/D 6 (9.5 megawatt, placed in operation 1989)
  L/D 8 (14 megawatt, placed in operation 1990)
  L/D 9 (18 megawatt, placed in operation 1990).
  “Levels of fish mortality (from mechanical injury; pressure affects, including cavitation and decompression; swim bladder rupture; and shear damage) resulting from passage through hydraulic turbines at hydroelectric facilities can be substantial. Adverse affects caused by rack impingement, entrainment, and turbine operations were reported to be relatively low at the hydroelectric facilities on the middle Allegheny River (ERC 1996; Sigma Consultants 1993).”

## Slide 15: Pittsburgh District Hydropower Status - Oct 2017 Licensed-Operating – Allegheny River L/D 6 (1988)

## Slide 16: Pittsburgh District Hydropower Status - Oct 2017 License Application Accepted by FERC - Rye Development

## Slide 17: District Concerns
Cumulative system losses & degradation with construction & operation of stacked hydropower projects in the navigation system. (22 permitted: 17 new & 5 existing).
Loss of aeration provided by dams & lower downstream dissolved oxygen levels.
Loss/ degradation of aquatic life and habitat.
  Tailwaters
    Extensive construction in tailwaters.
    Diversion of as much as 90% of river flow through turbines, flow not evenly distributed across channel.
    Loss of dam tailwater habitat, a limited, unique, & diverse resource. Few darter species are only found in tailwaters (Gilt, Bluebreast, Tippecanoe, and Variegate). Best spawning habitat for larger broadcast spawning species such as Sauger & Walleye.
  Upper pools.
    Crest gates on fixed crest dams & Diversion channels
    Loss of shoreline wetlands and shallow water habitat.

## Slide 18: District Concerns
“Unavoidable impingement and entrainment-related mortality …”1 as fish pass through the turbines.
Individual FERC EAs rather than a system EIS.
  Weak alternative analyses. No consideration of various bypass flows & mitigation alternatives.
  Weak assessment of cumulative impacts.
  Minimized impacts with fewer alternatives than included in FERC’s 1988 Final EIS for hydropower development in the Upper Ohio River Basin
  Environmental issues requiring mitigation in 1988 were determined minor in current EA’s.
  1. Rye Development EA’s

## Slide 19: FERC 1988 Final Environmental Impact Statement for Hydropower Development in the Upper Ohio River Basin2
23 Proposed Projects at navigation dams in 1988 (22 total in 2017).
Proposed mitigation.
  Maintain existing dissolved oxygen (DO) conditions downstream from Projects
    First five Ohio River dams particularly efficient aerators, important for maintaining downstream DO concentrations.
    If DO levels reduced to the state standard of 5.0 mg/l or lower, it would “significantly affect aquatic life”. Sufficient to maintain a DO > 6.5 mg/l.
  Turbine Bypass flows.
    Cease generation at Allegheny L&D No.2, Emsworth, Dashields, Montgomery, New Cumberland, and Pike Island when Ohio River flow at Sewickley drops below 9000 cfs July through October. during the critical season of July through October, & 4000 cfs the rest of the year to provide aeration in the main & backchannel.
  Continuous water quality monitoring.
2. “Hydroelectric Development in the Upper Ohio River Basin, FERC Docket No. EL85-19-114, Ohio, Pennsylvania, West Virginia, Final Environmental Impact Statement, September 1988.

## Slide 21: FERC 1988 Final Environmental Impact Statement for Hydropower Development in the Upper Ohio River Basin (Cont.)
  Protection of wetlands and fish habitat “…important for maintaining the overall biological integrity of the basin”.
    Goal no net loss of in-kind habitat value.
    No development at Allegheny L/D7, Montgomery L/D, and Muskingum L/D3 to avoid significant adverse impacts to wetlands, fish, and recreation. Recreational enhancements proposed could not compensate for losses.
    Regional Resource Agencies “…select, construct, test, & evaluate engineering prototypes of fish guidance systems that may prove effective for minimizing fish entrainment in hydroelectric turbines in the upper Ohio basin.”
  fish impingement and entrainment-related mortality
    “In the absence of well-defined fish passage rates at existing projects, monitoring at new projects will be necessary to determine these rates.”

## Slide 22: Possible Components of the District Adaptive Management Plan (AMP) for the Operation of Non-federal Hydropower projects at Navigation Dams
Adaptive management approach for project operations to maintain existing conditions (water quality, aquatic life, & habitat).
Included in Section 408 Review & in Construction & Operations MOAs required by the FERC License.
  ORSANCO and Resource agency input critical.
  Water Quality (WQ)
    Construction and operations compliance monitoring plans.
    Compliance with non-degradation water quality standards.
      Turbine bypass flows for each hydropower project sufficient to maintain >6.5 mg/l dissolved oxygen downstream.
    Year-round, real-time continuous WQ monitoring upstream and downstream of each project & flow where specified by the District by the USGS, during project construction & operation, funded by licensees.

## Slide 23: Possible AMP Components (cont.)
  Assessment of Aquatic life & habitat
    Biological integrity. Periodic biotic monitoring to document local and cumulative, project related changes on aquatic habitats and communities (fish, benthic macroinvertebrates, & mussels) during construction and throughout the term of the licenses.
        Track mussel bed & tailwater habitat
        Survey for federally listed mussels in the construction footprints and relocate listed mussels
        Multi-method fish surveys (fish netting and electrofishing) surveys
        Periodic fish netting and electrofishing surveys
    Post-construction turbine fish impingement and entrainment studies
        Representative of seasonal and hydrologic conditions, and all species and sizes of fish.
        Modify the trash rack spacing and approach velocities if necessary.
    Fish Passage?
    Creel surveys?

## Slide 24: Possible AMP Components (cont.)
  Turbine Bypass flow
    When discharges are NOT in compliance (fish, water quality, habitat degradation), flow through District’s gates or spillway increased.
    Aeration requirements will be higher during the critical summer low flow season & more bypass flow required.
    District’s discretion whether it releases any flows prior to making flows available to the projects for generation; determines the timing, amount, & location for any bypass flows it deems necessary.
  Navigation System Operation.
    System database and modeling to minimize cumulative impacts.

## Slide 25: Authority for Non-degradation Adaptive Management Approach
Navigation dams project specific purposes.
  Primary: Pass flow and to maintain minimum pool elevations and the navigation channel.
  Secondary: Managing flow to address climate change or for the benefit of aquatic life, water quality, fish passage, or fishing access
Federal Power Act.
  Corps project purposes have priority over hydropower generation.
  All decisions regarding flow belong to the Corps
ER 1110-2-1462. 20 Feb 1991. "Water Quality and Water Control Considerations for Non-Federal Hydropower Development at Corps of Engineers Projects".
ER 200-1-5. "Prevention, Control and Abatement of Environmental Pollution at Federal Facilities".
  USACE Environmental Operating Principles & Implementation Guidance.
Precedent: Non-degradation water quality criteria required in Operations MOAs of existing nonfederal hydropower projects at District facilities.
ER. = Corps Engineering Regulation

## Slide 26: Summary
Hydropower development encouraged as long as existing resources and project purposes are not impacted.
Similar to 1988, FERC permits and/or licenses have recently been issued for almost every District Navigation Dam that doesn’t already have non-federal hydropower.
District utilizes opportunities to recommend conditions to protect purposes and aquatic resources throughout the FERC licensing process for each proposed project & during the Corps’ Section 408 reviews.
District will require an adaptive, system-wide approach for the operation of non-federal hydropower projects at navigation dams, utilizing continuous, real time water quality monitoring and periotic biological sampling & assessment funded by the licensees, and compliance with non-degradation water quality standards. (Adaptive Management Plan).
The District AMP may incorporate some mitigation measures recommended in the FERC 1988 FEIS to minimize cumulative impacts of stacked hydropower development in the navigation system to protect Corps project purposes & resources.
Encourage /welcome input from state and federal resource agencies and ORSANCO in the development of the adaptive management plan for the operation of the hydropower projects in navigation system.
Notes: <number>

## Slide 27
Rose Reilly
Water Resources/ Water Quality
(412) 395 7357
Rosemary.j.reilly@usace.army.mil
Jeff Benedict
Planning, District Hydropower Coordinator
(412) 395 7202
Jeffrey.M.Benedict@usace.army.mil
US Army Corps of Engineers
Pittsburgh District
1000 Liberty Avenue
Pittsburgh, PA 15222