## Slide 1
Report of the
Biological Programs
215th ORSANCO Technical Committee Meeting
Agenda Item 4

## Slide 2: Agenda Item 4a: 2016 Assessments
2012 - Created a multi-metric Ohio River Macro index (ORMIn)
Fish and Bug metrics
  Diversity, abundance, feeding/reproductive guilds,
  pollution tolerance, health, and habits
Compare observed index score of a site to the past performance of sites with similar habitat
Biological Condition Ratings (colors) are assigned based on this relative performance
2003 - Created a multi-metric Ohio River Fish index (ORFIn)
2008 - Modified (mORFIn) to incorporate updated habitat classes and metric scoring methods

## Slide 3: Agenda Item 4a: 2016 Assessments
Willow Island, Greenup, and Cannelton pools
All 2016 Fish Survey results have been approved by the BWQSC
2 of 3 Macro Survey results have been completed, BWQSC approval pending
  Lab complications & field activities precluded timely completion of assessments
    Both avoidable in the future
  Willow Island and Greenup Pools complete
Cannelton Pool Macros
  6 HDs lost due to high flows, can’t assess with 9 sites
  Subcontracting lab processed MH samples with incorrect SOP
    Samples currently being enumerated with same lab
    Index calculations require quantitative data

## Slide 4
Assessment Pending
Assessment Complete
BWQSC Approval Pending
Assessment Complete
BWQSC Approval Pending

## Slide 7: Item 4b: Special Surveys – Hydro Impact Estimate
Involved Parties: Pittsburgh USACE, PADEP, USEPA Wheeling
Goal: Gather abiotic and biotic data for baseline/assessment of hydro impacts
Study Areas (5 total)
    Proposed Facility Existing Facility
    Allegheny L&D 2 Greenup L&D
    Montgomery Embayment Cannelton L&D
    Montgomery L&D
Methods
  Night-time electrofishing (day-time in the embayment)
  Muliti-habitat Kick Macroinvertebrate sampling
  Continuous DO & Temperature loggers
  DO profile at the top of each zone
Analyses
  mORFIn and ORMIn scores
  Abiotic and biotic variables compared to probabilistic results as necessary

## Slide 8: Item 4b: Special Surveys – Direct Tributaries
Interested Parties: PADEP, WVDEP, OEPA, KDOW, IDEM
Goal: Fill in knowledge and assessment gaps between ORSANCO and state agencies
  Lower tributaries are unique habitats
Study Areas: Identified 14 candidate tributaries across 3 pools
Methods
  Instream habitat sampling
  Day-time electrofishing
Analyses
  mORFIn, other fish assemblage measures as necessary

## Slide 9: Item 4b: Special Surveys Ohio Trib Temperature Regimes
Involved Parties : Ohio EPA
Purpose
  Obtain a temperature regime for backwater areas
  Compare with reference condition upstream of Ohio River influence
  Used to determine most appropriate temperature standards
Study area
  6 tributaries within the Meldahl Pool
    Bullskin Creek
    White Oak Creek
    Eagle Creek
    Ohio Brush Creek
    Stout Run
    Turkey Creek
Methods
  Continuous Temperature Pen Loggers were deployed in July
    Retrieval pending OEPA decision later this fall
Analyses – to be completed by Ohio EPA

## Slide 10
West Virginia 604(b) Project Summary
2016-2017
A Study of Contaminants in Edible Fish from the Kanawha and Monongahela Rivers in West Virginia
215th ORSANCO Technical Committee Meeting
Agenda Item 4C

## Slide 11: WV 604(b) Fish Tissue Project
Beginning in spring 2016,ORSANCO biological staff has operated on the Monongahela and Kanawha rivers on behalf of WVDEP.
Kanawha River:
Below Winfield Locks & Dam to the Byrd Pool of the Ohio River (KAN1)
Winfield Locks & Dam to Nitro, WV, river mile ~44.5 (KAN2)
Nitro, WV (river mile ~44.5) to Marmet Locks & Dam (KAN3)
Marmet Locks & Dam to London Locks & Dam (KAN4)
London Locks & Dam to the Kanawha Falls (KAN5)
Monongahela River:
PA/WV border (river mile 91.5) to Hildebrand Locks & Dam (MON1)
Hildebrand Locks & Dam to river mile ~128 (beginning of Monongahela River) (MON2)

## Slide 15: WV 604(b) Fish Tissue Project
Sauger
Walleye
Hybrid Striper or Striper
White Bass
Freshwater Drum
Common Carp
Channel Catfish < 45 cm
Channel Catfish > 45 cm
Flathead Catfish
Crappie
Largemouth Bass
Smallmouth Bass
Twelve species were targeted from each of the seven locations
Species were selected based on what was likely to be encountered and what is thought to be commonly consumed.
Each sample was to contain 3 to 5 fish if possible. Smaller composites (1 to 2 fish) were submitted in the event that 3 to 5 fish composites could not be attained
Targeted sizes followed legal size restrictions for all species.
Notes: Last of the samples will be shipped...today?

## Slide 16: WV 604(b) Fish Tissue Project
74 of 84 targeted samples (271 individuals) were collected and submitted for analysis.

## Slide 17: WV 604(b) Fish Tissue Project
Fillet homogenates were analyzed for lipids content, polychlorinated biphenyls, (PCBs; aroclors), total mercury (TrHg), and methylmercury (MeHg). All fillet samples from locations 1-4 on the Kanawha River were also analyzed for dioxins (all congeners). Carcass homogenates were analyzed for MeHg only and used to determine whole-fish MeHg.

## Slide 18: WV 604(b) Fish Tissue Project
Over the course of the project, total electrofishing time on the Kanawha was ~31.3 hours and ~9.8 hours on the Monongahela.
Expenditures for the project came to within one percent of the total estimated budget. Although not all target species were encountered, more personnel and travel expenses were accrued expending additional effort to fill as many data gaps as possible within the proposed timeframe.
The data resulting from this initiative provides WVDEP a fairly comprehensive snapshot of contaminant concentrations in fish across two of WV’s major waterways.

## Slide 19: WV 604(b) Fish Tissue Project
Despite the extensive travel and sampling effort, ORSANCO staff and seasonal Biologists suffered no lost-time incidents during the execution of this initiative, nor did any participants / interested party incur any substantial liability due to injury, equipment damage or loss.
ORSANCO would like to thank our State partners at WVDEP for the opportunity to conduct this study on their behalf. We would like to acknowledge WVDNR staff for their logistical assistance and field effort.