## Slide 1: 2017 Monitoring Activities: Summer Water Quality Conditions
Technical Committee Meeting
October 3-4, 2017
Agenda Item #3

## Slide 2: 2017 Sampling Sites

## Slide 3: Summer 2017 Monthly Precipitation Relative to Normal
May
June
July
August
September

## Slide 4
Average Monthly Streamflow May – September 2017
Chart: Pittsburgh (ORM 13)
| May | June | July | Aug | Sept
Observed | 55.2522 | 30.7875 | 32.308 | 14.1885 | 8.99
Long-Term | 37.9 | 25.6 | 17.8 | 14.5 | 13.8
Chart: Cincinnati (ORM 471)
| May | June | July | Aug | Sept
Observed | 170.9522 | 99.9167 | 94.064 | 44.8077 | 25.59
Long-Term | 120.2 | 72.1 | 48.1 | 40.2 | 34.8
Chart: Evansville (ORM 791)
| May | June | July | Aug | Sept
Observed | 246.9957 | 132.9583 | 111.8 | 61.5462 | 50.32
Long-Term | 180.4 | 118.8 | 74.4 | 61 | 54.1

## Slide 5
Clean Metals and Bimonthly Sampling

## Slide 6: Metals and Bimonthly Program Parameters
Metals
Mercury
Aluminum
Chromium
Manganese
Nickel
Copper
Zinc
Arsenic
Selenium
Silver
Cadmium
Antimony
Thallium
Lead
Magnesium
Calcium
Iron
Barium
Nutrients, Major Ions
Ammonia Nitrogen
Bromide
Chloride
Hardness
Nitrate-Nitrite Nitrogen
Phenols
Sulfate
Total Dissolved Solids
Total Kjeldahl Nitrogen
Total Organic Carbon
Total Phosphorus
Total Suspended Solids
Cyanide

## Slide 8
MeHg BAF and Tributary Sampling
MeHg BAFs under development at one location: (yellow dot)
  Will be complete in Oct 2017.
Tributary Hg & MeHg Mass Load Development (green and orange Dots)
  Data collection November 2015 to October 2016 (completed)

## Slide 9
Organics Detection System Sites
Notes: Maysville is not on this map

## Slide 10: Organics Detection System
Summary of ODS travel related repairs (non-maintenance agreement) September 1st 2016 to August 31st 2017
  Computer hardware or software related – 204 hours
  Equipment repair and maintenance - 60 hours
  GC calibration, training and service – 36 hours
    Pittsburgh Water, West View Water and Weirton Water have all needed training due to recent staffing changes.
  Inficon process GC related – 50 hours
  Only the GCMS portion of instrumentation is covered by Maintenance Agreements

## Slide 11
Year | # Raw Water Samples | % Utilization
2017 (Jan – Aug) | 3416/16 sites (8 months) | 88%
2016 (Jan – Dec) | 5221/16 sites | 92%
2015 (Jan – Dec) | 4969/15 sites | 91%
2014 (Jan – Dec ) | 5162/16 sites | 88%
2013 (Jan-Dec ) | 4771/15 sites | 87%
2012 (Jan – Dec) | 4589/15 sites | 88 %
2011 (Jan – Dec) | 4228/13 sites | 89 %
Organics Detection System
Performance Operations

## Slide 12: Contact Recreation Sampling

## Slide 13: Contact Recreation Monitoring
Bacteria samples are collected April 1 through October 31.
Samples are collected at an upstream and downstream location in Pittsburgh, Wheeling,
Huntington, Cincinnati, Louisville and Evansville.
Five rounds of sampling are completed monthly for each urban community sampling location and analyzed for E. coli using Colilert Method. Those five samples are then used to produce a monthly Geometric Mean which shall not exceed 130CFU/100mL and shall not exceed 240CFU/100mL in any single sample.
*Pittsburgh Geometric Mean based off of 4 samples in May, June, and September
*Wheeling Geometric Mean based off of 4 samples in June and September
Percent Exceeded April-September 2017 | Pittsburgh* | Wheeling* | Huntington | Cincinnati | Louisville | Evansville
Monthly Geometric Mean | 83% | 50% | 50% | 17% | 50% | 50%
Single Sample | 42% | 29% | 20% | 23% | 23% | 26%

## Slide 14
Chart: 2017 E.coli Monthly Geometric Mean
| Pittsburgh-4.3 | Wheeling-92.8 | Huntington-314.8 | Cincinnati-477.5 | Louisville-619.3 | Evansville-793.7
April | 369 | 228 | 184 | 130 | 138 | 138
May | 401 | 276 | 209 | 224 | 618 | 109
June | 132 | 176 | 146 | 130 | 204 | 70
July | 350 | 130 | 63 | 57 | 51 | 104
August | 209 | 42 | 74 | 17 | 80 | 182
September | 25 | 18 | 14 | 40 | 37 | 378

## Slide 15: Contact Recreation Monitoring
In Cincinnati we also analyze for Enterococcus using Enterolert at three sites and for E.coli/Total Coliform using Colilert at three cross-sections (nine sites).
Special Projects
Dragon SUP Event
Paddlefest
The Great Ohio River Swim

## Slide 16
D.O. and Temperature Monitoring

## Slide 17: Dissolved Oxygen and Temperature Monitoring
Dissolved oxygen (D.O.) and temperature is monitored by the United States Army Corp of Engineers, electric utility/hydropower agencies or ORSANCO for the assessment of aquatic life water quality criteria.
The average D.O. concentration shall be at least 5.0mg/L for each calendar day. Both Markland had one day that fell below 5.0mg/L. (Graphs to follow)
The allowable temperature varies each month and ranges from 71°-89°F. Temperatures did not exceeded the criteria. (Graphs to follow)

## Slide 18
DO mg/L
DO mg/L
DO mg/L
Chart: Montgomery (31.7) Dissolved Oxygen
Chart: 
Chart: Smithland (919) Dissolved Oxygen

## Slide 19
Temperature F°
Temperature F°
Temperature F°
Chart: Montgomery (31.7) Temperature
Chart: Markland (531.5) Temperature
Chart: Smithland (919) Temperature

## Slide 20
Probabilistic Pool Survey Sites
15 random 500m sites per pool + 3 revisits
  Fish Community
  Macroinvertebrate Community
  Continuous DO & Temp logger
  Nutrients & Chlorophyll A
  Instream & Riparian Habitat
New Cumberland
Meldahl
Newburgh
Notes: Emsworth, pike island, meldahl, newburgh

## Slide 21
Other
39 Fish Tissue Samples Riverwide
Notes: 10 events - Pittsburgh, Conesville, Marietta, Ripley, Cincinnati area x3, Louisville, Evansville, Paducah