## Slide 1: Bacteria Trends Report
Technical Committee Meeting
October 3-4, 2017
Agenda Item #9
Informational Item

## Slide 2: Background
Bacteria data collected routinely as part of Contact Recreation Program
Data uses:
  Weekly reporting of conditions for recreation
  Assess attainment of WQS (305b)
Municipalities spending $Billions on Long Term Control Plans and Consent Decrees
Are bacteria levels improving?

## Slide 3: Bacteria Data Availability
1990’s – Commission begins routine fecal coliform sampling
  Weekly sampling in six largest CSO communities
  May through October
2000 – Sampling sites added
  Upstream, downtown, downstream
2001 – E.coli analysis was added
2009 - Sites reduced to two per CSO community
2013 – Sampling period extended to include April

## Slide 4
Contact Recreation Sites

## Slide 5: Study Objectives
Evaluate observed trends in bacteria data set
  Spatial (comparison across and within CSO communities)
  Temporal (Are levels changing over time?)
  Seasonal trends
    Changes over contact recreation season
    Relationship to flow and precipitation

## Slide 6: Assessment
Evaluated based on concentration and frequency samples exceed water quality criteria.
Spatial
  Upstream/Downstream comparison
  2001 to 2015 (All 6 major CSO communities)
Temporal
  Rolling 5 Year aggregates
  1996 to 2015 (Evansville limited to 2001-2015)
Seasonal
  Monthly comparison (May-Oct)
  Precipitation – Grouped by precipitation ranges
  Flow – Grouped by flow quintiles

## Slide 7: Conclusions

## Slide 8: Conclusions
Longitudinal
  Lowest in Cincinnati/ Huntington
  Highest levels in upper river
Rank | City | Median (cfu/100 ml)
1 | Cincinnati | 110
2 | Huntington | 136
3 | Evansville | 211
4 | Louisville | 220
5 | Wheeling | 280
6 | Pittsburgh | 390

## Slide 9: Conclusions (cont)
Upstream / Downstream
  Concentrations significantly greater at downstream site
    Exception in Pittsburgh
City | US Fecal Median | DS Fecal Median | Difference US vs DS
Pittsburgh | 390 | 390 | 0
Wheeling | 67 | 280 | 213
Huntington | 40 | 136 | 96
Cincinnati | 60 | 110 | 50
Louisville | 66 | 220 | 154
Evansville | 69 | 211 | 142
Chart: Upstream vs. Downstream Median Fecal Coliform 2001-2015
| Pittsburgh | Wheeling | Huntington | Cincinnati | Louisville | Evansville
US Median Fecal | 390 | 67 | 40 | 60 | 66 | 69
DS Median Fecal | 390 | 280 | 136 | 110 | 220 | 211

## Slide 10: Conclusions (cont)
Upstream/Downstream
  Decrease in difference between median value over time
    Exception again is Pittsburgh
Chart: Huntington Median US-DS Fecal Coliform 2001-2015
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
US | 84 | 84 | 140 | 71 | 104 | 47.5 | 10 | 20 | 20 | 18 | 32 | 16 | 40 | 40 | 28
DS | 113.5 | 134 | 84 | 120 | 66 | 84 | 84 | 140 | 71 | 104 | 47.5 | 10 | 20 | 20 | 18 | 32 | 16 | 40 | 40 | 28

## Slide 11: Conclusions (cont)
Temporal
  Statistically significant decreasing trend found for Pittsburgh and Huntington
Chart: Huntington Downstream Fecal Coliform Annual Median (cfu/100mL)
| 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Huntington Downstream Fecal | 560 | 209.5 | 124 | 80 | 166 | 80 | 174 | 300 | 206 | 194 | 128 | 114 | 128 | 150 | 145 | 113.5 | 134 | 84 | 120 | 66
Downstream site | Spearman (R) | p-value
Pittsburgh | -0.489 | 0.029
Wheeling | 0.277 | 0.238
Huntington | -0.460 | 0.041
Cincinnati | -0.136 | 0.567
Louisville | -0.322 | 0.166

## Slide 12: Conclusions (cont)
Monthly comparison
  June exceedance rate 27-67%
  October exceedance 11-40%
Fecal Coliform | May | June | July | August | September | October
Pittsburgh | 47 | 59 | 52 | 56 | 49 | 36
Wheeling | 38 | 67 | 43 | 44 | 33 | 27
Huntington | 32 | 28 | 25 | 11 | 13 | 11
Cincinnati | 35 | 27 | 23 | 16 | 24 | 15
Louisville | 44 | 43 | 33 | 38 | 42 | 40
Evansville | 39 | 35 | 30 | 33 | 28 | 27
Average | 39 | 43 | 35 | 33 | 32 | 26
Rank | Month
1 | June
2 | May
3 | July
4 | August
5 | September
6 | October

## Slide 13: Conclusions (cont)
Precipitation
  Median concentrations steadily increase with rainfall
  Variability also increases with rainfall

## Slide 14: Conclusions (cont)
Precipitation
  Significant increasing trend
    Concentration and percentage of exceedances (Fecal and E. coli)
Chart: Fecal Coliform in Louisville 619.3 2001-2015
| 0-0.1 | 0.1-0.3 | 0.3-0.5 | 0.5-0.8 | 0.8-1.2 | 1.2-1.8 | >1.8
 | 0.21656 | 0.36264 | 0.35938 | 0.46875 | 0.65217 | 0.71875 | 0.75
Site Name | R² value | p value
LOUISVILLE | 0.9569 | 0.0001
CINCINNATI | 0.9423 | 0.0003
EVANSVILLE | 0.9230 | 0.0006
HUNTINGTON | 0.9152 | 0.0007
PITTSBURGH | 0.8926 | 0.0013
WHEELING | 0.7960 | 0.0069

## Slide 15: Conclusion (cont)
Precipitation
  No consistent pattern
    Pittsburgh and Huntington did show temporal trend
Chart: Cincinnati 477.5 Median E.coli vs Precipitation
| 1 | 2 | 3
2001-2005 | 32 | 100 | 290
2006-2010 | 38 | 48 | 215
2011-2015 | 24 | 112 | 370

## Slide 16: Conclusions (cont)
Flow
  Median concentrations steadily increase with flow
  Variability also increases with flow

## Slide 17: Conclusions (cont)
Flow
  Significant increasing trend with flow
    Concentration and percentage of exceedances
Site Name | R2 E. coli | p-value
Huntington | 0.867 | 0.000003
Wheeling | 0.814 | 0.000004
Cincinnati | 0.767 | 0.000077
Pittsburgh | 0.746 | 0.000184
Evansville | 0.707 | 0.000200
Louisville | 0.667 | 0.000621
Chart: E. coli in Huntington 314.8
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
 | 0.056452 | 0.065421 | 0.097826 | 0.1 | 0.27419 | 0.25 | 0.30189 | 0.31034 | 0.5641 | 0.68

## Slide 18: Conclusion (cont)
Flow
  A consistent pattern seen over 2001-2015
Chart: Median Fecal Colifrom at all sites vs Flow
| 1 | 2 | 3 | 4 | 5
2001-2005 | 100 | 170 | 191 | 285 | 614
2006-2010 | 57 | 116 | 166 | 200 | 600
2011-2015 | 51 | 74 | 110 | 150 | 251

## Slide 19: Next Steps
Draft Bacteria Trends Report
  Will be distributed to Technical Committee for review by end of October
Final Draft
  Comments will be incorporated and the final draft will be presented to TEC at the February meeting.

## Slide 20: Questions?