## Slide 1
West Virginia 604(b) Project Summary
2016-2017
A Study of Contaminants in Edible Fish from the Kanawha and Monongahela Rivers in West Virginia
215th ORSANCO Technical Committee Meeting
Agenda Item 4C

## Slide 2: WV 604(b) Fish Tissue Project
Beginning in spring 2016,ORSANCO biological staff has operated on the Monongahela and Kanawha rivers on behalf of WVDEP.
Kanawha River:
Below Winfield Locks & Dam to the Byrd Pool of the Ohio River (KAN1)
Winfield Locks & Dam to Nitro, WV, river mile ~44.5 (KAN2)
Nitro, WV (river mile ~44.5) to Marmet Locks & Dam (KAN3)
Marmet Locks & Dam to London Locks & Dam (KAN4)
London Locks & Dam to the Kanawha Falls (KAN5)
Monongahela River:
PA/WV border (river mile 91.5) to Hildebrand Locks & Dam (MON1)
Hildebrand Locks & Dam to river mile ~128 (beginning of Monongahela River) (MON2)

## Slide 6: WV 604(b) Fish Tissue Project
Sauger
Walleye
Hybrid Striper or Striper
White Bass
Freshwater Drum
Common Carp
Channel Catfish < 45 cm
Channel Catfish > 45 cm
Flathead Catfish
Crappie
Largemouth Bass
Smallmouth Bass
Twelve species were targeted from each of the seven locations
Species were selected based on what was likely to be encountered and what is thought to be commonly consumed.
Each sample was to contain 3 to 5 fish if possible. Smaller composites (1 to 2 fish) were submitted in the event that 3 to 5 fish composites could not be attained
Targeted sizes followed legal size restrictions for all species.
Notes: Last of the samples will be shipped...today?

## Slide 7: WV 604(b) Fish Tissue Project
74 of 84 targeted samples (271 individuals) were collected and submitted for analysis.

## Slide 8: WV 604(b) Fish Tissue Project
Fillet homogenates were analyzed for lipids content, polychlorinated biphenyls, (PCBs; aroclors), total mercury (TrHg), and methylmercury (MeHg). All fillet samples from locations 1-4 on the Kanawha River were also analyzed for dioxins (all congeners). Carcass homogenates were analyzed for MeHg only and used to determine whole-fish MeHg.

## Slide 9: WV 604(b) Fish Tissue Project
Over the course of the project, total electrofishing time on the Kanawha was ~31.3 hours and ~9.8 hours on the Monongahela.
Expenditures for the project came to within one percent of the total estimated budget. Although not all target species were encountered, more personnel and travel expenses were accrued expending additional effort to fill as many data gaps as possible within the proposed timeframe.
The data resulting from this initiative provides WVDEP a fairly comprehensive snapshot of contaminant concentrations in fish across two of WV’s major waterways.

## Slide 10: WV 604(b) Fish Tissue Project
Despite the extensive travel and sampling effort, ORSANCO staff and seasonal Biologists suffered no lost-time incidents during the execution of this initiative, nor did any participants / interested party incur any substantial liability due to injury, equipment damage or loss.
ORSANCO would like to thank our State partners at WVDEP for the opportunity to conduct this study on their behalf. We would like to acknowledge WVDNR staff for their logistical assistance and field effort.