## Slide 1: PFOA/PFOS Study
215 TEC Meeting
Oct 3-4, 2017
Columbus, OH

## Slide 2: Background
PFOA = Perfluorooctanoic Acid (C8)
  Used extensively in manufacture of teflon
PFOS = Perfluorooctane Sulfonate
  Used extensively in fire extinguishing foam, scotchguard.
PFCs are highly persistent and bioaccumulate.
Do not occur naturally.
Can be transported in atmosphere long distances. Found in Arctic.

## Slide 3: Background (cont.)
Bioaccumulate. Found in humans and fish tissue.
Carcinogenic.
Use of PfOA/PFOS has largely been phased out.
Replacement compounds (GenX) may be equal or more problematic.
PFOA & PFOS added to drinking water contaminant candidate list.
Drinking water health advisory level of 70 ng/L for PFOA+PFOS (finished water).

## Slide 4: Background (cont.)
Dupont Parkersburg PFOA contamination became apparent earlier in the last decade.
Fairly widespread and high level of contamination.
ORSANCO conducted a study of CECs 2009-2010. Discussion of results to follow.
ORSANCO is proposing a followup study.

## Slide 5: Ohio River PFOA/PFOS Results, 2009
Chart: Ohio River Mile
| 9.7000000000000011 | 86.7 | 220.3 | 306.8 | 394.9 | 462.9 | 600.5 | 791.5 | 889.1 | 934.4
PFOA | 2.5 | 3.01 | 35.2 | 19.1 | 14.1 | 13.1 | 9.21 | 11.5 | 8.93 | 23.9
PFOS | 0 | 2.82 | 2.88 | 2.71 | 3.15 | 2.58 | 5.58 | 7.27 | 6.49 | 35.4

## Slide 6: WWTP Mixing Zone PFOA/PFOS, 2009
Chart: Ohio River Mile
| 3.1 | 91.3 | 478 | 612.20000000000005 | 791.8 | 935.9
PFOA | 3.41 | 5.39 | 14.4 | 9.44 | 18.2 | 31.2
PFOS | 2.63 | 4.42 | 4.97 | 5.8 | 669 | 29.2

## Slide 7: Tributary PFOA/PFOS Results, 2009
Chart: 
| Allegheny R | Monongahela R | Kanawha R | Scioto R | Mill Cr | Wabash R
PFOA | 2.04 | 3.87 | 1.48 | 6.22 | 14.3 | 3.43
PFOS | 2.24 | 2.79 | 0 | 5.14 | 7.36 | 3.9

## Slide 8: Followup Study
Repeat selected sites from 2009.
Proposing ambient sites; no wastewater mixing sites; no tribs.
Instead of grab sampling, proposing to do USGS’s method that allows for calculation of mass loadings in large rivers.
Flow-weighted lateral and depth x-section.
Start Spring-summer of 2018.
High & low-flow event at seven locations.
USEPA to run all analyses – PFOA, PFOS, possibly other PFCs.
ORSANCO covers sample collection personnel, travel and supplies costs. Should be under $5,000.

## Slide 9: Ohio River PFOA/PFOS Results, 2009
Chart: Ohio River Mile
| 9.7000000000000011 | 86.7 | 220.3 | 306.8 | 394.9 | 462.9 | 600.5 | 791.5 | 889.1 | 934.4
PFOA | 2.5 | 3.01 | 35.2 | 19.1 | 14.1 | 13.1 | 9.21 | 11.5 | 8.93 | 23.9
PFOS | 0 | 2.82 | 2.88 | 2.71 | 3.15 | 2.58 | 5.58 | 7.27 | 6.49 | 35.4