## Slide 1: 2018 Biennial Assessment of Ohio River Water Quality Conditions
305b Report
2010-2014

## Slide 2: 305b Workgroup Conference Call
Met last week, all 6 states represented.
Set schedule:
  Draft assessments and data to states by year-end.
  TEC review/approve assessments February, 2018.
  Complete written report; TEC approve report June, 2018.
  Subcommittee will meet Nov. 1-2 to review assessment methodologies.

## Slide 3: 2016 Assessment Summary
 | States | Number Miles Use is Impaired |  |  |  | 
 |  | Aquatic Life | Contact Recreation | Public Water Supply | Fish Consumption for PCBs & Dioxin | Fish Consumption for Mercury
PA | 0.0-40.2 | 0 | 40.2 | 0 | 40.2 | 0
OH-WV | 40.2-317.1 | 0 | 242.2 | 0 | 276.9 | 0
OH-KY | 317.1-491.3 | 0 | 65.0 | 0 | 174.2 | 0
IN-KY | 491.3-848.0 | 0 | 243.6 | 0 | 356.7 | 0
IL-KY | 848.0-981.0 | 0 | 40.6 | 0 | 133.0 | 0
TOTAL | 981.0 | 0 | 631.6 | 0 | 981.0 | 0

## Slide 4: Questions?

## Slide 5: 2016 305(b) Biological Data
2010
2015
= Avg. Pool Macro Condition
= Avg. Pool Fish Condition

## Slide 6: Aquatic Life Water Criteria Violations July 2008 – June 2013
Mile Point | SiteName | WQC Applied | Parameter | Count of Violations | Max Result (ug/L) | # of Events | % Violations
84.2 | Pike Island | WV (1500 ug/L) | Fe (ug/L) | 2 | 3,297 | 30 | 7%
126.4 | Hannibal | WV (1500 ug/L) | Fe (ug/L) | 2 | 3,030 | 30 | 7%
161.8 | Willow Island | WV (1500 ug/L) | Fe (ug/L) | 3 | 4,690 | 30 | 10%
203.9 | Belleville | WV (1500 ug/L) | Fe (ug/L) | 6 | 2,191 | 29 | 21%
279.2 | R.C. Byrd | WV (1500 ug/L) | Fe (ug/L) | 1 | 1,649 | 30 | 3%
341 | Greenup | WV (1500 ug/L) | Fe (ug/L) | 14 | 7,576 | 29 | 48%
436.2 | Meldahl | KY (1000 ug/L) | Fe (ug/L) | 15 | 5,984 | 30 | 50%
477.5 | Anderson Ferry | KY (1000 ug/L) | Fe (ug/L) | 5 | 5,292 | 9 | 56%
531.5 | Markland | KY (1000 ug/L) | Fe (ug/L) | 15 | 6,780 | 30 | 50%
600.6 | Louisville | KY (1000 ug/L) | Fe (ug/L) | 6 | 7,132 | 9 | 67%
606.8 | McAlpine | KY (1000 ug/L) | Fe (ug/L) | 14 | 9,427 | 28 | 50%
720.7 | Cannelton | KY (1000 ug/L) | Fe (ug/L) | 14 | 5,035 | 30 | 47%
776 | Newburgh | KY (1000 ug/L) | Fe (ug/L) | 15 | 8,877 | 30 | 50%
846 | J.T. Myers | KY (1000 ug/L) | Fe (ug/L) | 15 | 14,327 | 30 | 50%
918.5 | Smithland | KY (1000 ug/L) | Fe (ug/L) | 15 | 4,790 | 30 | 50%
938.9 | L&D 52 | KY (1000 ug/L) | Fe (ug/L) | 18 | 6,407 | 30 | 60%

## Slide 7: Contact Recreation Use Assessment
Assessment includes:
    Bacteria data from 15 historical river-wide longitudinal surveys.
    Contact recreation data from the past 5 years collected seasonally in the 6 largest CSO communities.
    Vast majority of river is assessed based on historical longitudinal surveys.
States’ criteria used for assessment.
Criteria violations > 10% indicate Partial Support. > 25% indicate Not Supporting.
Approximately 2/3 of river impaired for contact recreation use: Consistent with past assessments.

## Slide 8: Public Water Supply Use Assessment
Impairment based on finished water MCL violations caused by Ohio River water quality.
Accessed USEPA data base of MCL violations and water utility surveys.
Human health criteria violations in > 10% of samples indicates impairment.
6 utilities had MCL violations for trihalomethanes, one for HAA5’s, two for Fecal coliform.
Attributed to treatment issues, not Ohio River water quality.
Entire river assessed as fully supporting public water supply use.

## Slide 9
 |  |  | Intake Closures | Nonroutine Treatment | MCL Violations
West View | 5 | PA | No | No | 
Robinson | 8.6 | PA | No | No | 
Moon | 11.7 | PA | No | No | 
Beaver Valley (NOVA) | 29 | PA |  |  | 
Midland | 36 | PA |  |  | TTHM (6)
East Liv | 40.2 | OH |  |  | 
Buckeye | 74.1 | OH |  |  | 
Toronto | 59.2 | OH | No | No | 
Arcelor Mittal | 61.7 | WV | No | No | 
Weirton | 62.5 | WV |  |  | TTHM
Steubenville | 65.3 | OH | No | No | 
Follansbee (H.H.) | 70.8 | WV |  |  | 
Wheeling | 86.8 | WV |  |  | 
New Martin | 121.9 | WV | No | No | 
Sistersville | 137.2 | WV |  |  | 
Huntington | 304 | WV |  |  | 
Ashland | 319.7 | KY |  |  | TTHM (5)
Ironton | 327 | OH |  |  | 

## Slide 10
 |  |  | Intake Closures | Nonroutine Treatment | MCL Violations
Russell | 327.6 | KY |  |  | TTHM (4)
Portsmouth | 350.8 | OH | No | No | 
Maysville | 407.8 | KY | No | Yes | Turb
Cincinnati | 462.8 | OH | Yes | Yes | 
N. KY | 462.9 | KY | No | No | 
Louisville | 600 | KY |  |  | 
Evansville | 791.5 | IN |  |  | 
Henderson | 803 | KY | No | No | 
Mt Vernon | 829.3 | IN | No | No | Coliform
Morganfield | 842.5 | KY | No | No | 
Sturgis | 871.4 | KY |  |  | TTHM (7), HAA5, Coliform
Paducah (WTP) | 935.5 | KY | No | No | TTHM
Paducah (USEC) | 945.9 | KY | No | No | 
Cairo | 978 | IL |  |  | 

## Slide 11: Fish Consumption Use Assessment
The entire Ohio River is designated as partially supporting for PCBs and dioxin.
ORSANCO directed by TEC to use US EPA’s approach for determining impairment based on methylmercury fish tissue data.
Collected data necessary to use EPA’s methodology.
Violations of mercury water quality criterion in > 10% of samples indicates impairment.
Using “WOE Approach”, entire river Full Support for fish consumption based on Methylmercury.

## Slide 14: Total Mercury Water Violations
Mile Pt. | SiteName | Count of Hg Violations | Max Result, ng/L | # of Events | % Violations
84.2 | Pike Island | 1 | 12.5 | 30 | 3%
126.4 | Hannibal | 1 | 13.6 | 30 | 3%
161.8 | Willow Island | 1 | 19.1 | 30 | 3%
341 | Greenup | 3 | 16.5 | 30 | 10%
436.2 | Meldahl | 1 | 17.6 | 29 | 3%
477.5 | And. Ferry | 1 | 13.4 | 9 | 11%
531.5 | Markland | 3 | 19.4 | 30 | 10%
600.6 | Louisville | 3 | 20.6 | 9 | 33%
606.8 | McAlpine | 2 | 26.1 | 28 | 7%
776 | Newburgh | 4 | 17.8 | 30 | 13%
846 | J.T. Myers | 6 | 40.6 | 30 | 20%
918.5 | Smithland | 2 | 15.2 | 29 | 7%
938.9 | L&D 52 | 4 | 18.0 | 29 | 14%

## Slide 15: Averaging Data Across Trophic Levels
Cavg = 3.8 * C2 + 8.0 * C3 + 5.7 * C4
(3.8 + 8.0 + 5.7)
Where:
C2 = average mercury concentration for trophic level 2
C3 = average mercury concentration for trophic level 3
C4 = average mercury concentration for trophic level 4
**Calculation is based on apportioning the 17.5 grams/day national default consumption rate for freshwater fish by trophic level
5.7 grams/day of TL 4 fish
8.0 grams/day of TL 3 fish
3.8 grams/day of TL 2 fish
Guidance for Implementing the January 2001 Methylmercury Water Quality Criterion – US EPA
Notes: Came from page 61 and 62 of epa document

## Slide 16: Fish Consumption-Weighted Methylmercury Fish Tissue
Pool | # Samples | Max. MeHg Conc., ppm | N > 0.3 ppm | MeHg Concumption-Weighted Avg. Concentration (ppm)
Emsworth | 7 | 0.27 | 0 | 0.120
Dashields | 8 | 0.23 | 0 | 0.160
Montgomery | 6 | 0.17 | 0 | 0.125
New Cumb. | 4 | 0.27 | 0 | 0.186
Pike Island | 4 | 0.28 | 0 | 0.146
Hannibal | 10 | 0.64 | 3 | 0.246
Willow Island | 18 | 0.4 | 1 | 0.141
Belleville | 11 | 0.29 | 0 | 0.168
Racine | 9 | 0.44 | 3 | 0.211
RC Byrd | 6 | 0.24 | 0 | 0.179
Greenup | 10 | 0.36 | 2 | 0.176
Meldahl | 8 | 0.27 | 0 | 0.177
Markland | 15 | 0.49 | 5 | 0.221
McAlpine | 14 | 0.45 | 1 | 0.191
Cannelton | 6 | 0.37 | 1 | 0.181
Newburgh | 9 | 0.29 | 0 | 0.136
JT Myers | 11 | 0.86 | 4 | 0.246
Smithland | 14 | 0.67 | 6 | 0.281
Olmsted | 11 | 0.4 | 2 | 0.187
Open Water | 5 | 0.49 | 1 | 0.145

## Slide 17: TEC Considerations
Need consideration by TEC for Approval of Assessments.
Bacteria, PCBs & Dioxin data/assessments are old.
Continue collection of Methylmercury in fish tissue.