## Slide 1: 2018 Biennial Assessment of Ohio River Water Quality Conditions
305b Report
2012-2016

## Slide 2: 2018 Assessment Summary
 | States | Number Miles Use is Impaired |  |  |  | 
 |  | Aquatic Life | Contact Recreation | Public Water Supply | Fish Consumption for PCBs & Dioxin | Fish Consumption for Mercury
PA | 0.0-40.2 | 0 | 40.2 | 0 | 40.2 | 0
OH-WV | 40.2-317.1 | 0 | 242.2 | 0 | 276.9 | 0
OH-KY | 317.1-491.3 | 0 | 61.1 | 0 | 174.2 | 0
IN-KY | 491.3-848.0 | 0 | 243.6 | 0 | 356.7 | 0
IL-KY | 848.0-981.0 | 0 | 40.6 | 0 | 133.0 | 0
TOTAL | 981.0 | 0 | 629.7 | 0 | 981.0 | 0

## Slide 3: Weight of Evidence Approach
Recommended by the Technical Committee and approved by the Commission, October 2011.
Weight of evidence utilized in the 2016 assessments.
Weight of evidence had effects on aquatic life use, mercury fish consumption, and public water supply assessments.

## Slide 4: Aquatic Life Use Assessment
“Weight-of-Evidence Approach” relies on biological assessments including fish and macroinvertebrate indices.
First assessment including macroinvertebrate index.
Criteria violations > 10% indicate impairment.
Aquatic life criteria exceeded for:
    Total iron (states’ criteria)
    Dissolved oxygen
    Temperature
305b workgroup recommended against using DO & Temperature data that are collected only during worst-case summer months.
Bioassessments indicate full support river-wide.

## Slide 5: 2012-16 Biological Pool Survey Results

## Slide 6: Iron Aquatic Life Criteria Violations 2012-16

## Slide 7: Contact Recreation Use Assessment
Assessment includes:
    Bacteria data from 15 historical river-wide longitudinal surveys.
    Contact recreation data from the past 5 years collected seasonally in the 6 largest CSO communities.
    Vast majority of river is assessed based on historical longitudinal surveys.
States’ criteria used for assessment – Geo Mean.
Criteria violations > 10% indicate Partial Support. > 25% indicate Not Supporting.
Approximately 2/3 of river impaired for contact recreation use: Consistent with past assessments.

## Slide 8: Public Water Supply Use Assessment
Assessments Consider:
  Bimonthly & clean metals human health criteria violations.
  Impairment based on finished water MCL violations (caused by Ohio River water quality).
Accessed USEPA data base of MCL violations and water utility surveys.
6 utilities had MCL violations for trihalomethanes, one for HAA5’s, two for Fecal coliform.
Attributed to treatment issues, not Ohio River water quality.
Entire river assessed as fully supporting public water supply use.

## Slide 11: Fish Consumption Use Assessment
The entire Ohio River is designated as partially supporting for PCBs and dioxin.
ORSANCO directed by TEC to use US EPA’s approach for determining impairment based on methylmercury fish tissue data.
Collected data necessary to use EPA’s methodology.
Violations of mercury water quality criterion in > 10% of samples indicates impairment.
Using “WOE Approach”, entire river Full Support for fish consumption based on Methylmercury.

## Slide 14: Total Mercury Water Violations
Mile Pt. | SiteName | Count of Hg Violations | Max Result, ng/L | # of Events | % Violations
54.4 | New Cumbrlnd | 0 | 8.2 | 30 | 0%
84.2 | Pike Island | 1 | 12.5 | 30 | 3%
126.4 | Hannibal | 0 | 10.7 | 29 | 0%
161.8 | Willow Island | 1 | 19.1 | 30 | 3%
203.9 | Belleville | 0 | 8.0 | 29 | 0%
279.2 | RC Byrd | 0 | 7.7 | 30 | 0%
341 | Greenup | 1 | 15.2 | 30 | 3%
436.2 | Meldahl | 1 | 13.2 | 30 | 3%
531.5 | Markland | 2 | 15.5 | 30 | 7%
606.8 | McAlpine | 1 | 26.0 | 30 | 3%
720.7 | Cannelton | 1 | 19.0 | 30 | 3%
776 | Newburgh | 4 | 22.0 | 29 | 14%
846 | J.T. Myers | 5 | 31.7 | 30 | 17%
918.5 | Smithland | 4 | 15.2 | 30 | 13%
938.9 | L&D 52 | 3 | 18.0 | 30 | 10%

## Slide 15: Averaging Data Across Trophic Levels
Cavg = 3.8 * C2 + 8.0 * C3 + 5.7 * C4
(3.8 + 8.0 + 5.7)
Where:
C2 = average mercury concentration for trophic level 2
C3 = average mercury concentration for trophic level 3
C4 = average mercury concentration for trophic level 4
**Calculation is based on apportioning the 17.5 grams/day national default consumption rate for freshwater fish by trophic level
5.7 grams/day of TL 4 fish
8.0 grams/day of TL 3 fish
3.8 grams/day of TL 2 fish
Guidance for Implementing the January 2001 Methylmercury Water Quality Criterion – US EPA
Notes: Came from page 61 and 62 of epa document

## Slide 16: Fish Consumption-Weighted Methylmercury Fish Tissue
Pool | # Samples | Max. MeHg Conc., ppm | N > 0.3 ppm | MeHg Concumption-Weighted Avg. Concentration (ppm)
Emsworth | 7 | 0.27 | 0 | 0.106
Dashields | 4 | 0.23 | 0 | 0.179
Montgomery | 7 | 0.17 | 0 | 0.091
New Cumb. | 1 | 0.27 | 0 | 0.082
Pike Island | 2 | 0.28 | 0 | 0.067
Hannibal | 8 | 0.64 | 0 | 0.142
Willow Island | 22 | 0.4 | 1 | 0.132
Belleville | 8 | 0.29 | 0 | 0.149
Racine | 8 | 0.44 | 1 | 0.156
RC Byrd | 6 | 0.24 | 0 | 0.179
Greenup | 17 | 0.36 | 1 | 0.172
Meldahl | 5 | 0.27 | 0 | 0.151
Markland | 19 | 0.49 | 6 | 0.220
McAlpine | 11 | 0.45 | 0 | 0.177
Cannelton | 2 | 0.37 | 0 | 0.230
Newburgh | 7 | 0.29 | 0 | 0.147
JT Myers | 28 | 0.86 | 3 | 0.175
Smithland | 14 | 0.67 | 5 | 0.276
Olmsted | 7 | 0.4 | 1 | 0.176
Open Water | 6 | 0.49 | 1 | 0.143

## Slide 17: TEC Considerations
Need consideration by TEC for Approval of Assessments.
Bacteria, PCBs & Dioxin data/assessments are old.
Continue collection of Methylmercury in fish tissue.