## Slide 1: 2018 Triennial Review
Peter Goodmann
Director
Kentucky Division of Water
To Protect and Enhance Kentucky’s Environment

## Slide 2: 2018 Triennial Review
Clean Water Act (CWA) Section 303(c)(1) Requirements:
  Every 3-years
  Review State Water Quality Standards
  Public Participation:
    Public Comment Period
    Public Meetings

## Slide 3: WQS Amendments
KRS 13A
  File with LRC
  Publish in Legislative Record
  30-Day Comment Period
  Public Hearing

## Slide 4: Tentative Timeline

## Slide 5: Purpose of Listening Session
Provide an Opportunity for Public Comment on:
  Water Quality Standards (WQS) located in 401 KAR Chapter 10
    401 KAR Chapter 10 Revisions
    National Recommended WQS Criteria

## Slide 6: KDOW Considerations
Human Health Criteria for 94 pollutants
Aquatic Life Criteria for Ammonia, Cadmium, Carbaryl, and Selenium (in fish fillets)
Recreational Criteria for E. coli
Adopting CSO wet weather provisions
Allowing use of Copper Biotic Ligand Model
Designating 52 new Outstanding State Resource Waters (OSRW) and 29 new Exceptional Waters

## Slide 7: Human Health
94 Chemicals
  Update to EPA’s 2015 recommended criteria using:
    body weight = 80 kg,
    drinking water ingestion = 2.4 L/day,
    fish consumption rate = 22.8 g/d (Inland South value)

## Slide 8: Aquatic Life
Ammonia
  Update to EPA’s 2013 recommended criteria
    Acute Cold Water
    Acute Warm Water
    Chronic

## Slide 9: Aquatic Life
Cadmium
  Update to EPA’s 2016 recommended criteria but retain as total recovered (not dissolved)
    Acute (μg/L) = e(0.9789 (ln Hardness) – 3.866)
    Chronic (μg/L) = e(0.7977 (ln Hardness) - 3.909)

## Slide 10: Aquatic Life
Carbaryl
  Adopt EPA’s 2012 recommended criteria

## Slide 11: Aquatic Life
Selenium
  Adopt EPA’s 2016 recommended criteria of 11.3 mg/kg dry weight for fish fillet
  Remove Kentucky’s egg/ovary value of 19.3 mg/kg dry weight
    EPA did not approve this egg/ovary value

## Slide 12: Aquatic Life
Copper Biotic Ligand Model
  Retain current criteria but allow site-specific criteria using EPA’s 2007 Copper Biotic Ligand Model

## Slide 13: Recreational Criteria
Primary Contact Recreation
  Adopt EPA’s 2012 recommended criteria
  for E. coli (rounded to nearest 10)

## Slide 14: Recreational Criteria
Wet Weather Standards for residual Combined Sewer Overflows (CSOs) after full implementation of approved Long Term Control Plan (LTCP)
  Allow use of Financial Capability Assessment from LTCP to demonstrate substantial and widespread economic and social impact
  Temporarily suspend recreational criteria during residual CSO events

## Slide 15: Recreational Criteria
Wet Weather Standards for residual Combined Sewer Overflows (CSOs) after full implementation of approved Long Term Control Plan (LTCP)
  Options: consistent with 1994 CSO Policy
    Modify the PCR and SCR language to allow the suspension of the standard(s) during residual CSO events in accordance with an approved LTCP
    Create a CSO designated use and criteria
    Identify CSO receiving waters in a table in 10:026
    Combination of all of the above
    Possible UAA process to complete the suspension of the standard or designated use for CSO receiving waters

## Slide 16: Special-Use Waters
Add 52 Outstanding State Resource Waters
  KY Arrow Darter Basins and Big Sandy Crayfish Segments

## Slide 17: Special-Use Waters
Add 52 Outstanding State Resource Waters
  3 Segments for T&E Mussels

## Slide 18: Special-Use Waters
Add 29 Exceptional Waters
  Based upon finding an excellent fish or macroinvertebrate community

## Slide 19: Written Comments
June 6, 2018 @ 4:00 PM ET
Mail to:
    Carole J. Catalfo, Esq.
    Internal Policy Analyst
    Division of Water
    300 Sower Blvd., 3NW 36WK
    Frankfort, KY 40601
Email to: water@ky.gov
  “2018 Triennial Review” in the subject line

## Slide 20: 2018 Triennial Review Information
http://water.ky.gov/waterquality/Pages/WaterQualityStandards.aspx