## Slide 1: Super Gage sites
Sensors for water temperature, specific conductance, pH, dissolved oxygen, turbidity, nitrate + nitrite, orthophosphate
Compute nutrient and suspended sediment loads
Develop surrogate models for constituents not easily measured in real-time

## Slide 2: Ohio River Sampling and Super Gage Site Network
Super Gages
PROPOSED Super Gages
National Water Quality Network sites
Louisville
Murray
Indianapolis
Louisville
Cincinnati
Ashland
EXISTING
Ohio R @ Olmsted Ill.
Green R @ Spottsville Ky
Ohio R @ Ironton Ohio
NEW FOR 2018
Wabash R @ New Harmony
Kentucky R @ Lock 2
Licking R nr Alexandria, Ky
HAB—Ohio R @ Cannelton IN

## Slide 3: Indiana Super Gage sites

## Slide 4: Eastern Great Lakes Nowcast
https://ny.water.usgs.gov/maps/nowcast/
Environmental variables for E. coli
Rain, turbidity, waves, lake level
Real-time swimming advisories to the public
Data management

## Slide 5: Can we develop models for HABs?
Real-time models include factors that are easily or continuously measured
Comprehensive models include factors from a sample analyzed in a laboratory and may provide advanced warning

## Slide 6: Sampling and data sites: 2016‒18

## Slide 7: Samples and data collected
Microcystins
Cyanobacterial genes (qPCR) and nutrients
Satellite data

## Slide 8
Continuous monitor data
Average measurement for 24-h period up to 10 a.m.
Calculated averages for 1, 3, 5, 7, or 14 days

## Slide 9: Cadiz WTP: 2016‒17
The results presented today are preliminary results only and have not been approved.

## Slide 10: Cadiz real time factors: Continuous monitor in 2017
Spearman’s correlations (rho) to microcystin, p<0.1, p<0.05 | 
 | 2017 (n=37 or 38)
Blue-green algae (BGA): 7d, 5d, 24h, 3d, Inst, 14 d | 0.51 – 0.39
pH: 14d, 7d, 5d | 0.40 – 0.28
Turbidity, 24 h | 0.30
Not significant: dissolved oxygen, water temp, specific conductance, chlorophyll

## Slide 11: Cadiz comprehensive factors: Nutrients and cyanobacterial genes
Spearman’s correlations (rho) to microcystin, p<0.05 | 
2016-17 | Lagged 7-36 days
Planktothrix mcyE toxin genes | 0.76
Planktothrix general genes | 0.64
Microcystis general genes | -0.52
Dolichospermum general genes | -0.51
Nitrate + nitrite | 0.35
Ammonia | -0.39
Not significant: ortho-P, TN, TP

## Slide 12: Carroll WTP: 2016‒17

## Slide 13: Carroll WTP: Real time factors from 3rd party sources
Spearman’s correlations (rho) to microcystin, p<0.05 | 
 | 2016-17 (n=44)
Discharge, Portage River: 14d, 24 h, 3 d prior, 7d or 30 d average or peak | -0.52 to -0.31
NOAA, raw pixel value from satellite imagery | 0.44 (n=22)
Rain: 3-d prior, 14-d sum | -0.26 to -0.25
Lake level: change from spring average | -0.25

## Slide 14: Carroll real time factors: Continuous monitor 2016‒17
Spearman’s correlations (rho) to microcystin, p<0.05 |  | 
N = 40‒43 | Oregon WTP | Ottawa WTP
pH: 24 h, 3d, 7d, 5d, 14d | 0.87 – 0.77 | 0.66 – 0.57
BGA, RFU: 24 h, 3d, 7d, 5d, 14d | 0.76 – 0.74 | 0.49 – 0.45
Specific conductance: | -0.76 – -0.66 | -0.58 – -0.49
Chlorophyll, raw, ug/L or RFU: | 0.26 – 0.21 | 0.48 – 0.38
Not significant: dissolved oxygen, water temp
Oregon WTP

## Slide 15: Virtual Beach Modeling
Free software developed by USEPA
Originally developed for E. coli and beaches
Data exploration and model selection, development, and validation
Training provided
https://www.epa.gov/exposure-assessment-models/virtual-beach-vb

## Slide 16: Cadiz comprehensive model: 2016‒2017
Planktothrix mcyE, lagged
Cosine day of the year
Lake level above spring average
R2 = 0.85

## Slide 17: Carroll real-time model: 2016-17
R2 = 0.87
pH 14 d: Ottawa sonde
BGA 24 h: Oregon sonde
Discharge 7 d ave: Portage River
Wind offshore 24 h: Toledo Airport

## Slide 18: Donna Francy 614-430-7769 dsfrancy@usgs.gov