## Slide 1: Bacteria Trends Report
Technical Committee Meeting
June 5-6, 2018
Agenda Item #3

## Slide 2: Background
Bacteria data collected routinely as part of Contact Recreation Water Quality Monitoring Program
Data uses:
  Weekly reporting of conditions for recreation
  Assess attainment of WQS (305b)
Municipalities spending $Billions on Long Term Control Plans and Consent Decrees
Are bacteria levels improving?

## Slide 3
Contact Recreation Sites

## Slide 4: Study Objectives
Evaluate observed trends in bacteria data set
  Spatial (comparison across and within CSO communities)
  Temporal (Are levels changing over time?)
  Seasonal trends
    Changes over contact recreation season
    Relationship to flow and precipitation

## Slide 5: Assessment
Evaluated based on concentration and frequency samples exceed water quality criteria.
Spatial
  Upstream/Downstream comparison
  2001 to 2015 (All 6 major CSO communities)
Temporal
  Rolling 5 Year aggregates
  2001 to 2015 (Evansville limited to 2001-2009)
Seasonal
  Monthly comparison (May-Oct)
  Precipitation – Grouped by precipitation ranges
  Flow – Grouped by flow quintiles

## Slide 6: Conclusions
Pittsburgh upstream site may not be representative.
Highest fecal coliform / E.coli levels in Pittsburgh and the lowest in Cincinnati.
Highest levels occurred in June (~40% exceedance rate). Lowest levels in October (~25% exceedance rate).
The difference between upstream and downstream was highest in Wheeling and lowest in Pittsburgh.
Concentrations and exceedance rate increases with precipitation.

## Slide 7: Conclusions con’t
Concentrations and exceedance rate increases with flow.
Fecal coliform and E.coli concentrations were approximately four times greater during the highest flow and precipitation grouping.
Fecal coliform and E.coli levels are variable over time, however show a general declining trend.
Fecal coliform / E. coli values normalized for flow show a steady decline overtime.

## Slide 8: Upstream/Downstream Comparison Over Time
Chart: Huntington Median US-DS E.coli 2001-2015
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
US | 46 | 36 | 92 | 51 | 66 | 32 | 4 | 8 | 8 | 4 | 14 | 4 | 20 | 16 | 12
DS | 24 | 84 | 220 | 156 | 97 | 77 | 61.5 | 54 | 77.5 | 75.5 | 55.5 | 82.5 | 32 | 32 | 40

## Slide 9: Fecal Coliform by Flow Quintiles
Chart: Huntington 314.8 Median Fecal Coliform vs Flow Percentile
| 1 | 2 | 3 | 4 | 5
2001-2005 | 81.5 | 189 | 266 | 280 | 645.5
2006-2011 | 66 | 158 | 169 | 186 | 325
2011-2015 | 36 | 87 | 120 | 126 | 230

## Slide 10: Next Steps
Request comments from the Technical Committee by July 31st.
Request comments from other committees (e.g. POTW)
Prepare final report for the October Technical Committee Meeting.