## Slide 1: Overview of a Proposed Eutrophication Standard for Ohio’s Large Rivers
ORSANCO 217th Technical Committee Meeting
June 5-6, 2018
Robert J. Miltner
robert.miltner@epa.ohio.gov

## Slide 2: Eutrophication in Visual Context
165 μg/l
GMR when chlorophyll > 100 ug/l
GMR when chlorophyll < 50 ug/l

## Slide 3: Ohio Chlorophyll Levels in Context
Sestonic Chlorophyll ug/l
Oligotrophic
Eutrophic
Mesotrophic
25th 50th 75th max
4.9 17 35 170
Van Nieuwenhuyse
& Jones 1996 (all data)
25th 50th 75th max
13 34 69 337
Ohio
(all data)
25th 50th 75th max
15 42 85 328
Thames Basin
Maximums*
* 21 sampling stations sampled weekly over three years
700 - 7,000 mi2
~ 5 - 3,841 mi2
~ 1 - 200,000 mi2

## Slide 4: Daily Water Column Chlorophyll in the GMR
CHL ug/l
USGS data from 8/25/1999 to 4/15/2001 near Bolton Well Field
Sep 99
Aug 00
Apr 01

## Slide 5: Daily Oxygen Range and Chlorophyll
USGS Well Field Study

## Slide 6: Dissolved Oxygen and Chlorophyll Ohio EPA Statewide Monitoring Observations

## Slide 7: 5-day Biological Oxygen Demand and Chlorophyll
pre-construction grant levels
elevated levels
Ohio Large River Data

## Slide 8: Effect of Over-Enrichment on Biological Indicators

## Slide 9: Large River Sites Plotted by Ordination of Fish Assemblages
Recovered from carbonaceous
enrichment (i.e., poorly treated sewage)
Legacy issues remain

## Slide 10: Biological Indicators and Over-Enrichment
Rivers with legacy problems
Rivers w/o legacy problems

## Slide 11: Eutrophication Standard - Box Model
 | Acceptable | Enriched or Over Enriched | Over Enriched
Indicator |  | Chronic Condition | Acute Condition
Sestonic Chlorophyll | <30 ug/l as seasonal average | Magnitude 30 < 100 ug/l seasonal average with biological impairment; Frequency > 30 < 100 ug/l as seasonal average in two of three years | Magnitude > 100 ug/l anytime with biological impairment; Frequency > 100 ug/l multiple observations at base flow
BOD5 | <2.5 mg/l as seasonal average | Magnitude > 2.5 < 6 mg/l seasonal average with biological impairment Frequency > 2.5 < 6 mg/l as seasonal average in two of three years | Magnitude > 6 mg/l anytime with biological impairment and seasonal average chlorophyll > 30 ug/l Frequency > 6 mg/l two or more times during the base flow period
24-Hour D.O. Range | <6.5 mg/l | >7 mg/l – 9.0 mg/l (default to chlorophyll, BOD5 and biological indicators) | Magnitude and Frequency ≥9.0 mg/l anytime with biological impairment
TKN | NA | NA | ≥0.75 mg/l May substitute for BOD5
TSS |  | ~20 mg/l; general screening level for inspection of data sets lacking chlorophyll observations. | 

## Slide 12: Nutrient Target Part 1: TSS, Flow and Chlorophyll one outlier excluded

## Slide 13: Flow, TSS and Chlorophyll

## Slide 14: Distributions of Water Quality Parameters Binned by whether TSS is under or over predicted

## Slide 15: Phosphorus Target?

## Slide 16: Nutrient Target - 2nd Line of Evidence Chlorophyll by Nitrogen Level

## Slide 17: Chlorophyll-Phosphorus Relationship by Nitrogen Level
r2 = 0.34
r2 = 0.09

## Slide 18: Summary of Findings and Considerations
Evidence of over-enrichment is compelling
  Ohio rivers have some of the highest documented concentrations of chlorophyll in the world
Eutrophication benchmarks are defensible
  strong associations between enrichment indicators and biological assemblages
  amenable to a box model
WWH biocriteria for large rivers is under-protective
  bar set at clearing the hurdle of industrial pollution and domestic sewage
  eutrophication indicators (BOD, CHL, D.O.) can trigger listing

## Slide 19: Summary of Findings and Considerations
Nutrient co-limitation is evident
  more aptly named co-facilitation
  nitrogen should not be ignored
TP target ~ 130 ug/l
  for over-enriched waters with high TP concentrations
  seasonal average; summer base-flow conditions
  weight-of-evidence needed to list waters
Reach-specific targets possible
  modeling exercise will often suggest nutrients need to be much lower

## Slide 20: Going Forward
Peer-review publication
Share technical document and begin dialogue with EPA
Immediate & Near-Term
Start ESO
Add aspects of implementation to technical document
Medium-Term
Conclude ESO
Produce rule package
Long-Term
✔
✔
You Are Here

## Slide 21: Eutrophication Standard - Box Model
 | Acceptable | Enriched or Over Enriched | Over Enriched
Indicator |  | Chronic Condition | Acute Condition
Sestonic Chlorophyll | <30 ug/l as seasonal average | Magnitude 30 < 100 ug/l seasonal average with biological impairment; Frequency > 30 < 100 ug/l as seasonal average in two of three years | Magnitude > 100 ug/l anytime with biological impairment; Frequency > 100 ug/l multiple observations at base flow
BOD5 | <2.5 mg/l as seasonal average | Magnitude > 2.5 < 6 mg/l seasonal average with biological impairment Frequency > 2.5 < 6 mg/l as seasonal average in two of three years | Magnitude > 6 mg/l anytime with biological impairment and seasonal average chlorophyll > 30 ug/l Frequency > 6 mg/l two or more times during the base flow period
24-Hour D.O. Range | <6.5 mg/l | >7 mg/l – 9.0 mg/l (default to chlorophyll, BOD5 and biological indicators) | Magnitude and Frequency ≥9.0 mg/l anytime with biological impairment
TKN | NA | NA | ≥0.75 mg/l May substitute for BOD5
TSS |  | ~20 mg/l; general screening level for inspection of data sets lacking chlorophyll observations. | 

## Slide 22: Phosphorus Concentrations by Decade Headwater Streams

## Slide 23
1980-1990
Legend
2
10
50
>100
1980-2000
1980-Present
Sediment-Sensitive Species in Ohio

## Slide 24: GMR

## Slide 25: Scioto River

## Slide 26: Chlorophyll Concentrations
GMR
Scioto

## Slide 27: Maumee River