## Slide 1
Estimates of Atmospheric Mercury Deposition
to Ohio River Tributary Watersheds
Work Plan Overview for ORSANCO Technical Committee by Martin Risch June 5, 2018

## Slide 2
Report and Recommendations of the ORSANCO Ad Hoc Committee On Mercury Studies in October 2016
Findings:
Mercury (Hg) is a widespread contaminant and a global pollutant.
The atmosphere is generally the greatest source of Hg to water.
Some inorganic Hg in water is converted to methylmercury, which bioaccumulates in the food chain.
Methylmercury in fish presents the greatest Hg health hazard.
ORSANCO should:
Develop a mass balance source apportionment of Hg in the Ohio River.
Determine the quantity of Hg entering the Ohio River from mainstem point sources, tributaries, and tributary point sources.
Estimate atmospheric Hg deposition within each tributary watershed.
Determine the total amount of Hg flowing in the Ohio River.
Identify the portion of Hg in the Ohio River from each source category.

## Slide 3
Work Plan
  Study Area:
15 major Ohio River tributary watersheds (Allegheny, Monongahela, Beaver, Muskingum, Kanawha, Big Sandy, Scioto, Little Miami, Licking, Great Miami, Kentucky, Green, Wabash, Cumberland, Tennessee) and main stem Ohio River
  Study Period:
November 1, 2015 through October 31, 2016, the time of monthly Hg load estimates for 15 tributaries near Ohio River confluence
  Estimates for each watershed:
Annual wet atmospheric Hg deposition from precipitation
Annual dry atmospheric Hg deposition to forest landscapes
Annual dry atmospheric Hg deposition to non-forest landscapes
Annual wet and dry atmospheric Hg load to watershed (mass)
Annual atmospheric Hg yield from watershed (mass per unit area)

## Slide 4
Work Plan, contd.
  Wet Hg Deposition:
  Compute annual precipitation-weighted Hg concentrations for selected National Atmospheric Deposition Program Mercury Deposition Network sites in the study area.
  Develop a GIS spatial data grid of interpolated annual Hg concentrations for the study area for the study period.
  Develop a GIS spatial data grid of annual precipitation depth based on PRISM climate spatial data (Oregon State).
  Develop a GIS spatial data grid of the product of annual Hg concentrations and annual precipitation = annual wet Hg deposition to the study area.
  Overlay the Ohio River tributary watershed boundaries and sum the annual wet deposition for each watershed.

## Slide 5
Example of annual atmospheric Hg wet deposition map from GIS grid (Risch and Kenski, 2018, Atmosphere doi:10.3390/atmos9010029)

## Slide 6
Work Plan, contd.
  Dry Hg Deposition to Forest Landscapes:
  Compute annual litterfall Hg deposition for selected National Atmospheric Deposition Program Litterfall Mercury Monitoring Initiative sites in the study area. (Method in Risch et al. 2017 doi:10.1016/j.envpol.2017.05.004)
  Develop a GIS spatial data grid of interpolated annual litterfall Hg dry deposition to forest land cover in the study area for the study period. (Forest land cover from the USGS National Land Cover Dataset.) Assign dry Hg deposition to forest class and type according to U.S. Forest Service forest inventory.
  Overlay the Ohio River tributary watershed boundaries and sum the annual dry deposition to forests for each watershed.

## Slide 7
Work Plan, contd.
  Dry Hg Deposition to Non-Forest Landscapes:
  Compute annual Hg dry deposition for selected National Atmospheric Deposition Program Atmospheric Mercury Network (AMNet) sites in non-forest landscapes in the study area for the study period.
  Compute and sum the fluxes of 3 Hg species using measured air concentrations and vertical deposition velocities. (Method in Zhang et al. 2016 doi:10.1021/acs.est.6b04276)
  Develop a GIS spatial data grid of interpolated annual dry Hg deposition to non-forest land cover in the study area for the study period.
  Overlay the Ohio River tributary watershed boundaries and sum the annual dry deposition to non-forests for each watershed.

## Slide 8
Atmospheric Mercury Network (AMNet)
Litterfall Mercury Monitoring Initiative Network through 2016

## Slide 9
From Risch et al. 2017

## Slide 10
Work Plan Result
Sum wet Hg load and dry Hg load grids using the GIS to obtain estimated atmospheric Hg loads (mass) and yields (mass per area) for each of the 15 watersheds in the study area, along with totals for the study area.
Estimates of annual atmospheric Hg loads and yields from the can be compared with annual surface water Hg loads and yields from the ORSANCO monitoring.
Work to be performed by ORSANCO with assistance of consultant and completed in 2018.