## Slide 1: 2018 Monitoring Activities: Summer Water Quality Conditions
Technical Committee Meeting
October 2-3, 2018
Agenda Item #7

## Slide 2: 2018 Field Activities

## Slide 3: Summer 2018 Monthly Precipitation Relative to Normal
May
June
July
August
September

## Slide 4
Average Monthly Streamflow May – September 2018
Chart: Pittsburgh (ORM 13)
| May | June | July | Aug | Sept
Observed | 50.8714 | 30.7875 | 17.8517 | 17.3296 | 69.1824
Long-Term | 37.9 | 25.6 | 17.8 | 14.5 | 13.8
Chart: Cincinnati (ORM 471)
| May | June | July | Aug | Sept
Observed | 143.9429 | 99.9167 | 52.2172 | 56.4296 | 173.4706
Long-Term | 120.2 | 72.1 | 48.1 | 40.2 | 34.8
Chart: Evansville (ORM 791)
| May | June | July | Aug | Sept
Observed | 175.7964 | 132.9583 | 78.4034 | 71.5148 | 176.4529
Long-Term | 180.4 | 118.8 | 74.4 | 61 | 54.1

## Slide 5
Clean Metals and Bimonthly Sampling

## Slide 6: Metals and Bimonthly Program Parameters
Metals
Mercury
Aluminum
Chromium
Manganese
Nickel
Copper
Zinc
Arsenic
Selenium
Silver
Cadmium
Antimony
Thallium
Lead
Magnesium
Calcium
Iron
Barium
Nutrients, Major Ions
Ammonia Nitrogen
Bromide
Chloride
Hardness
Nitrate-Nitrite Nitrogen
Phenols
Sulfate
Total Dissolved Solids
Total Kjeldahl Nitrogen
Total Organic Carbon
Total Phosphorus
Total Suspended Solids
Cyanide

## Slide 8
Organics Detection System Sites
ODS Monitoring Stations
Notes: In November 2017, the Kanawha Valley Water Treatment Plant on the Elk River, in Charleston WV was added as an ODS site. American H20/KVTP is a self-supporting ODS station. (Slide corrected to include Maysville H20 from last year).

## Slide 9: Organics Detection System
Summary of ODS repairs and Training (September 1st 2017 to August 31st 2018)
    ORSANCO staff lost Field Service R&M person at the end of July 2018. (actively recruiting for position)
  Pittsburgh – Extended down time due to frozen water line & CMS service
  St. Albans - Site down since June 2018 – Building renovation
  Huntington - Assisted WV American install CMS5000 (July)
  Paducah – Experienced temporary outage due to system leak
  Exposed source water lines froze at all CMS5000 sites; sites down for several weeks during winter months
  GC calibration, training, and service –
    Hays Mine, West View Water, Weirton Water, Huntington have had training due to new operators at host site.
  Maintenance Agreements on GCMS instrumentation expires December 31, 2018.
Notes: Similar to last year, the ods lost operators at host sites, additional training & support required.
New site on-line in November 2017. WV American Kanawha Valley Plant on the Elk River in Charleston had CMS unit installed. Staff provided training and support.
WV
Pittsburgh CMS unit was repaired, returned, installed and same issue occurred again. It was sent back for additional repairs. Avg repair for CMS units ~ 4 weeks TAT.

## Slide 10: Contact Recreation Sampling

## Slide 11: Contact Recreation Monitoring
Bacteria samples are collected April 1 through October 31.
Samples are collected at an upstream and downstream location in Pittsburgh, Wheeling,
Huntington, Cincinnati, Louisville and Evansville.
Five rounds of sampling are completed monthly for each urban community sampling location and analyzed for E. coli using Colilert Method. Those five samples are then used to produce a monthly Geometric Mean which shall not exceed 130CFU/100mL and shall not exceed 240CFU/100mL in any single sample.
*Less than 5 samples were collected due to weather/equipment issues-no
Geometric Mean was calculated for those months.
Percent Exceeded April-September 2018 | Pittsburgh* | Wheeling* | Huntington | Cincinnati | Louisville | Evansville
Monthly Geometric Mean | NA | NA | 83% | 50% | 50% | 50%
Single Sample | 40 % | 42% | 50% | 47% | 47% | 47%

## Slide 12: Contact Recreation Monitoring
In Cincinnati we also analyze for E.coli/Total Coliform using Colilert at three cross-sections (nine sites) weekly.
Special Projects
Paddlefest
The Great Ohio River Swim (Postponed
until Oct. 14 due to weather)

## Slide 13
D.O. and Temperature Monitoring

## Slide 14: Dissolved Oxygen and Temperature Monitoring
Dissolved oxygen (D.O.) and temperature is monitored by the United States Army Corp of Engineers, electric utility/hydropower agencies or ORSANCO for the assessment of aquatic life water quality criteria.
The average D.O. concentration shall be at least 5.0mg/L for each calendar day. Both Markland and Smithland had multiple days that fell below 5.0mg/L. (Graphs to follow)
The allowable temperature varies each month and ranges from 71°-89°F. Temperatures did not exceeded the criteria. (Graphs to follow)

## Slide 15
Chart: Montgomery (RMI 31.7) Dissolved Oxygen
Chart: Markland (RMI 531.5) Dissolved Oxygen
Chart: Smithland (RMI 919) Dissolved Oxygen

## Slide 16
Chart: Montgomery (RMI 31.7) Temperature
Chart: Markland (RMI 531.5) Temperature
Chart: Smithland (RMI 919) Temperature