## Slide 1: Mass Balance/Source Apportionment
1) Calculate Instream Hg mass loads:
- Ohio River at 4 sites.
- 15 major tributaries.
- Based on 1-yr survey, monthly sampling.
2) Calculate Hg mass loads from sources
    - Atmospheric sources.
    Point sources.
Mass balance apportionment.
  - All calcs for annual period Nov. 1 2015 to Oct 31, 2016.

## Slide 2: Project Status
Instream loads have been completed.
  Used monthly Hg results and best daily flow data sets for one year in “Loadest”. Loadest is USGS load calculator.
  Looked at USGS measured flows, NWS modeled flows, and USACE “Cascade” modeled flows.
  Considered Ln-Linear model and Loadest model.
  Loadest looks at multiple relationships and always generated excellent r-squared values.
  We are writing up the report now.
  Will show some results after Marty’s presentation.
Atmospheric loads have been completed.
- Marty will show results and report has been drafted.
Point Source Loads have been completed.
- Need to verify work, collate and summarize on watershed basis in GIS.

## Slide 4
Chart: Tributary Mercury Loads
| Allegheny | Monongahela | Beaver | Muskingum | Kanawha | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | Green | Wabash | Cumberland | Tennesse
Instream Mercury Load (lbs) | 83.7916 | 75.0771 | 33.277 | 73.903 | 186.8983 | 74.1539 | 93.0416 | 14.0359 | 100.2093 | 17.8906 | 77.2474 | 285.1243 | 406.2061 | 236.4585 | 323.748
Atmpsheric Mercury Load (lbs) | 1356.5949 | 900.9994 | 321.6985 | 813.8654 | 1529.9592 | 557.0671 | 687.1295 | 190.0632 | 423.3557 | 559.6606 | 894.3914 | 1197.3988 | 4087.8493 | 2299.0311 | 5482.2279

## Slide 5
Chart: Ohio River Mercury Loads
| ORM 126 | ORM 282 | ORM 782 | ORM 912
Instream Mercury Load (lbs) | 252.9067 | 593.1511 | 2152.7092 | 2940.3921
Atmpsheric Mercury Load (lbs) | 2973.0804 | 6128.7598 | 11386.0006 | 17243.8524

## Slide 6
Chart: Tributary Mercury Yields
| Allegheny | Monongahela | Beaver | Muskingum | Kanawha | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | Green | Wabash | Cumberland | Tennesse
Instream Mercury Yield (µg/m^2) | 1.2514 | 1.7825 | 1.8458 | 1.6078 | 2.6723 | 3.0251 | 2.5021 | 1.3984 | 4.7359 | 0.5838 | 1.9422 | 5.4075 | 2.1587 | 2.312 | 1.386
Atmospheric Mercury Yield (µg/m^2) | 20.2609 | 21.3923 | 17.8439 | 17.7061 | 21.8756 | 22.7255 | 18.4788 | 18.9355 | 20.0077 | 18.2628 | 22.4871 | 22.7091 | 21.724 | 22.4794 | 23.4705

## Slide 7
Chart: Ohio River Mercury Yields
| ORM 126 | ORM 282 | ORM 782 | ORM 912
Instream Mercury Yield (µg/m^2) | 1.7196 | 1.9677 | 3.8591 | 3.574
Atmospheric Mercury Yield (µg/m^2) | 20.2147 | 20.3309 | 20.4116 | 20.9596