## Slide 1: Probabilistic Survey of PFOS/ PFOA along the Ohio River ORSANCO October 3rd, 2018 Lansing, WV
Katie McKone
Peter Goodmann
Melanie Arnold
Kentucky Division of Water

## Slide 2: What are PFOS and PFOA?
perfluorooctane sulfonate (PFOS)
perfluorooctanoic acid (PFOA)
Part of a larger group of chemicals called per- and polyfluoroalkyl substances (PFAS)
  Released into the environment through industrial manufacturing and disposal/ use of products containing PFAS
  Persistent in the environment
  Resistant to environmental degradation
  Widely distributed across all trophic levels
  Found in soil, air, and groundwater
  “The toxicity, mobility and bioaccumulation potential of PFOS and PFOA result in potential adverse effects on the environment and human health.”
        EPA Technical Fact Sheet – November 2017

## Slide 3: Federal and State Guidelines
Drinking water health advisories: 70 ppt (0.07 µg/L) for PFOS and PFOA combined
  “Above these levels, EPA recommends that drinking water systems take steps to assess contamination, inform consumers and limit exposure.”
EPA Technical Fact Sheet – November 2017
Ranges from 0.02 to 2.0 µg/L

## Slide 4: Evidence along the OH River
PFOS and PFOA have been reported at drinking water intakes and finished water
PFOS and PFOA have not been characterized along the Ohio River with a scientifically designed study
Based on the sources of PFOS and PFOA, urban settings may have higher levels than non-urban settings of the river
  Urban = Red
  Non-Urban = Blue
    Based on census data (Tony Olsen, EPA)
Anecdotal evidence: 4 ppt – 20 ppt

## Slide 5: A probabilistic survey to achieve ORSANCO’s goals
Characterize the concentration of PFOS and PFOA along the Ohio River
Probabilistic survey
  Sites randomly selected within the constraints of the study design
  Unbiased
  Known confidence
  Study design depends upon the question you are trying to answer
    Design 1: What is the mean concentration of PFOS and PFOA in the urban and non-urban settings of the Ohio River, and what proportion of the sampling population is above a threshold?
    Design 2: What is the mean concentration of PFOS and PFOA in the urban and non-urban settings of the Ohio River?
    Design 3: What is the mean concentration of PFOS and PFOA along the Ohio River?
    Credit: Tony Olsen, EPA

## Slide 6: Design 1: 30 sites in the non-urban (pink dots) and urban (green dots) – 60 total
What does this answer?
  Mean concentration of urban setting with known confidence
  Mean concentration of non-urban setting with known confidence
  What proportion of the urban setting is above a defined threshold
  What proportion of the non-urban setting is above a defined threshold
    What threshold would we use?

## Slide 7: Design 2: 20 sites in the non-urban (red dots) and urban (purple dots) – 40 total
What does this answer?
  Mean concentration of urban setting with known confidence
  Mean concentration of non-urban setting with known confidence
  What is the confidence?
    Depends on the variance
      Low variance = higher confidence
      High variance = lower confidence
    Need a little bit of data to determine how much data is appropriate
      6 sites per population is minimum
      30 can be thought of as maximum
      With 20 per population, reasonable expectation that preferred confidence would be met

## Slide 8: Design 3: 30 sites (black dots) along the Ohio River, no sub-categories
What does this answer?
  What is the mean concentration of PFOS and PFOA along the Ohio River?
  18% of OH River characterized as urban
  Only 1 site of the 30 falls in the urban setting
  If this one site has much higher PFOS/ PFOA
    Increases overall variability
    Characterize the urban setting with one site

## Slide 9: The details are important
How many samples?
  Increasing number of samples decreases variance, which increases confidence
  Monthly for an entire year
    Target both high and low flow events (with safety concerns recognized)
Where do you collect?
  Exactly at the Lat/Long
  Right Bank
  Left Bank
  Composite of longitudinal survey
How deep?
  Surface?
  1 m below surface?
Need a QAPP
  Define roles and responsibilities
  Define where and how
  Define QA/QC
    Field Blanks
    Duplicates or Replicates
  Define Data Quality Objectives (DQO)
  Define Deliverables

## Slide 10: Recommendation (up for debate)
  Design 2
    20 urban
    20 non-urban
    40 total sites
  Monthly samples
  Composite of 3 samples
    Collect 3 samples per site
      At Lat/Long
      RB adjacent to Lat/Long
      LB adjacent to Lat/Long
    Analyze 1 sample per site
  Per month
    120 water samples collected
    40 samples analyzed
  1 year project
    1,440 water samples collected
    480 samples analyzed
  Still need to consider
    Cost
    Staff availability
    How accessible are these sites?
    What is the longest boat ride?
    What’s doable in the summer might not be doable in the winter
      We can have an overdraft for sites that aren’t accessible or where access is overly burdensome
  Standard Method can be found at
    https://cfpub.epa.gov/si/si_public_file_download.cfm?p_download_id=525468

## Slide 11: Thank You. Questions?
Contact Information:
katie.mckone@ky.gov
Works Citied:
US EPA. November 2017. Technical Fact Sheet – Perfluorooctane Sulfonate (PFOS) and Perfluorooctanoic Acid (PFOA). Office of Land and Emergeny Management (5106P). EPA 505-F-17-001. https://www.epa.gov/sites/production/files/2017-12/documents/ffrrofactsheet_contaminants_pfos_pfoa_11-20-17_508_0.pdf
Photo Credit: https://www.cruisecritic.com/articles.cfm?ID=2111