## Slide 1: Bacteria Trends Report
Technical Committee Meeting
October 2-3, 2018
Agenda Item #3
Action Item

## Slide 2: Background
Bacteria data collected routinely as part of Contact Recreation Water Quality Monitoring Program
Data uses:
  Weekly reporting of conditions for recreation
  Assess attainment of WQS (305b)
Municipalities spending $Billions on Long Term Control Plans and Consent Decrees
Are bacteria levels improving?

## Slide 3
Contact Recreation Sites

## Slide 4: Study Objectives
Evaluate observed trends in bacteria data set
  Spatial (comparison across and within CSO communities)
  Temporal (Are levels changing over time?)
  Seasonal trends
    Changes over contact recreation season
    Relationship to flow and precipitation

## Slide 5: Assessment
Evaluated based on concentration and frequency samples exceed water quality criteria.
Spatial
  Upstream/Downstream comparison
  2001 to 2015 (All 6 major CSO communities)
Temporal
  Rolling 5 Year aggregates
  2001 to 2015
Seasonal
  Monthly comparison (May-Oct)
  Precipitation – Grouped by precipitation ranges
  Flow – Grouped by flow quintiles

## Slide 6: Conclusions
Pittsburgh upstream site may not be representative.
Highest fecal coliform / E.coli levels in Pittsburgh and the lowest in Cincinnati.
Highest levels occurred in June (~40% exceedance rate). Lowest levels in October (~25% exceedance rate).
The difference between upstream and downstream was highest in Wheeling and lowest in Pittsburgh.
Concentrations and exceedance rates increase with both precipitation and flow.

## Slide 7: Conclusions con’t
Fecal coliform and E.coli concentrations were approximately four times greater during the highest flow and precipitation grouping.
Fecal coliform and E.coli levels are variable over time, however show a general declining trend.
Fecal coliform / E. coli values normalized for flow show a steady decline overtime.

## Slide 8: Upstream/Downstream Comparison
Chart: Huntington Median US-DS E.coli 2001-2015
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
US | 46 | 36 | 92 | 51 | 66 | 32 | 4 | 8 | 8 | 4 | 14 | 4 | 20 | 16 | 12
DS | 24 | 84 | 220 | 156 | 97 | 77 | 61.5 | 54 | 77.5 | 75.5 | 55.5 | 82.5 | 32 | 32 | 40

## Slide 9: Fecal Coliform by Flow Quintiles
Chart: Median Fecal Coliform at Long-Term Sites vs Flow Precentile
| 1 | 2 | 3 | 4 | 5
2001-2005 | 150.5 | 275 | 270 | 415 | 732
2006-2010 | 110 | 196 | 226 | 310 | 600
2011-2015 | 104 | 120 | 178 | 174 | 280

## Slide 10: Questions or Comments?