## Slide 1
Atmospheric Mercury Loads to Watersheds in the Ohio River Basin
by Martin Risch, Bridget Taylor, and Jason Heath

## Slide 2
Report and Recommendations of the ORSANCO Ad Hoc Committee On Mercury Studies in October 2016
Findings:
Mercury (Hg) is a widespread contaminant and a global pollutant.
The atmosphere is generally the greatest source of Hg to water.
Some inorganic Hg in water is converted to methylmercury, which accumulates and magnifies in the food chain.
Methylmercury in fish presents the greatest Hg health hazard.
ORSANCO should:
Develop a mass balance source apportionment of Hg in the Ohio River.
Determine the quantity of Hg entering the Ohio River from main stem point sources, tributaries, and tributary point sources.
Estimate atmospheric-Hg loads within each tributary watershed.
Determine the total amount of Hg flowing in the Ohio River.
Identify the portion of Hg in the Ohio River from each source category.

## Slide 3
Purpose and Scope
Calculate the annual atmospheric mercury (Hg) “load” to 15 tributary and 5 main stem watersheds in the Ohio River Basin from November 2015 through October 2016
“Load” is Hg mass transferred in wet and dry forms from atmosphere to land and water
Does not address Hg transport, retention, release, or transformation

## Slide 4
Ohio River Basin study area
527,884 km2
52 % deciduous forest
34 % cropland
9.4 % urban
Land cover type in km2

## Slide 5
Approach
Hg data from three National Atmospheric Deposition Program (NADP) monitoring networks
Spatial data sets of watershed boundaries, annual precipitation, land cover, forest type
Data processing using Geographic Information System (GIS)
Calculations of three types of annual Hg loads: Wet-Hg load from precipitation Dry-Hg load to forest land cover Dry-Hg load to non-forest land cover
Annual sum of wet and dry atmospheric-Hg loads (mass)
Normalized annual atmospheric Hg load (mass per unit area)

## Slide 6
Annual wet-Hg loads
Annual precipitation-weighted Hg concentrations from 20 NADP sites for study period
Ranged 6.5 to 10.4 nanograms per liter
Inverse-distance-weighting algorithm applied to 5 x 5-km grid overlay--isopleth

## Slide 7
Annual precipitation depth for study period from PRISM climate spatial data set
Ranged 780 to 2,124 mm/year
Multiply Hg concentration X precipitation depth in 5 x 5-km grid overlay = wet-Hg load
Overlay HUC-8 watershed boundaries and summarize wet-Hg load by watershed
Ranged 27 kg (Main Stem 5) to 1,277 kg (Tennessee River)

## Slide 8
Normalized annual wet-Hg loads by watershed
Ohio River Basin was 10.6 microgram per square meter per year
Ranged from 7.9 in Sciotto River and Muskingum River watersheds to 13.3 in Main Stem 4 watershed
5,574 kg of wet-Hg load to study area

## Slide 9
Wet-Hg load method spatial and statistical assessments
Criteria of inverse-distance-weighting algorithm (number of known data points and power of nearest points) did not have a strong influence on the interpolation grid (+/- 5%)
Watershed area was not primary driver of wet-Hg load—Hg concentration and precipitation depth also were important
Statistical assessment of Hg concentrations and precipitation depths for 2014-2015-2016 indicated 2014 had significantly higher concentrations and 2015 had significantly higher precipitation, but study period was not biased
Wet-Hg load for study area was comparable to other published data

## Slide 10
Annual dry-Hg loads to forest land cover
GIS delineation of forest land cover and delineation of 5 forest types (U.S. Forest Service)
Oak-hickory (84.5 %), maple-beech-birch (10.4 %), oak-pine (2.3 %), elm-ash-cottonwood (1.4 %), oak-gum-cypress (0.4 %)

## Slide 11
Annual dry-Hg load in litterfall from 13 NADP monitoring sites in 2016
Hg concentration in litterfall X mass of litterfall = dry-Hg load in microgram per square meter per year
Inverse-distance-weighting algorithm for oak-hickory forest type
Index rate for annual dry-Hg load for other 4 forest types

## Slide 12
Normalized annual dry-Hg load
2.5 x 2.5-km grid overlay of forest land cover
Sum of dry-Hg for 5 forest types in grid cover, by watershed
12.5 micrograms per square meter per year for study area
Ranged 1.0 in Great Miami River to 11.8 in Big Sandy River watershed
3,225 kg dry-Hg load to forests in study area -- 85 % from oak-hickory type, 11.4 % from maple-beech-birch type, 2.4 % from oak-pine type

## Slide 13
Forest dry-Hg load method assessments
Criteria of inverse-distance-weighting algorithm (number of known data points and power of nearest points) did not have a strong influence on the interpolation grid (+/- 3%)
Forested area was not single driver of dry-Hg load, although there was a general relation
Dry-Hg load for study area was comparable to other published data

## Slide 14
Annual dry-Hg loads to non-forest land cover
GIS delineation of non-forest land cover and delineation of 4 land cover types (National Land Cover Dataset)—cropland, urban, grassland, open water
NADP Atmospheric Hg Network sites continuously sample and analyze air for 3 Hg species
NADP uses published model for vertical deposition velocity by land use for 3 species
Daily dry-Hg loads aggregated into annual dry-Hg loads by Hg species
Dry-Hg load index rate for 4 land cover types from selected NADP data

## Slide 15
Normalized annual dry-Hg load
Grid overlay of non-forest land cover
Sum of dry-Hg for 4 land cover types in grid cover, by watershed
10.3 micrograms per square meter per year for study area
Ranged 1.6 in Big Sandy River to 8.9 in Great Miami River watershed
2,600 kg dry-Hg load to non-forest land in study area-- 81 % from cropland, 14 % from urban, 4.6 % grassland, 0.4 % open water

## Slide 16
Annual atmospheric-Hg load
Sum of wet-Hg plus dry-Hg
11,400 kg Hg to study area
21.6 micrograms per square meter per year
Ranged 17.7 in Muskingum River to 23.9 in Main Stem 4
49 % wet and 51 % dry loads

## Slide 17
Summary and Conclusions
Documented methods were used to combine national Hg-monitoring data with widely accepted spatial data.
Calculated annual atmospheric Hg loads to 20 watersheds in the Ohio River Basin for 12 month study period.
Combined transfer of wet Hg in precipitation and dry Hg to forest and non-forest land cover in the study area was 11,400 kg (21.6 micrograms per square meter).
Methods and data were evaluated with several techniques and found to be reasonable and representative measures of atmospheric Hg loads during the prescribed study period.
Findings are limited in accuracy by the density of Hg monitoring network sites.
Results contribute to larger goal for ORSANCO to compute Hg mass balance and source apportionment for Ohio River.

## Slide 18
ATMOSPHERIC-HG LOAD
NONPOINT- SOURCE LOAD TO STREAMS
POINT-SOURCE LOAD TO STREAMS
HG RETAINED ON LAND
STREAM-HG LOAD
HG RELEASED