## Slide 1: Preliminary Results of Mercury Ohio River Basin Mass Balance Project
Report to TEC Committee
February 12-13, 2019

## Slide 2: Ad Hoc Mercury Committee Background
  Ad Hoc Established June, 2015.
  Held 5 conference calls & meeting Aug. ‘16.
  Charge:
    Identify what is known and unknown about mercury.
    Determine the value and costs of addressing the unknowns.
    Make recommendations for studies to the Commission.
  Work completed by Mercury Ad Hoc:
    Identified available outside data.
    Completed literature review & background report.
    Identified and prioritized information needs.
    Identified a project and schedule to fill in information gaps.
  Held 5 conference calls.
  1 in-person meeting at ORSANCO Aug. 3.

## Slide 3: Committee Membership
Stuart Bruny OH Commissioner
Doug Conroe NY Commissioner
Jessica Dexter Environmental Law & Policy Center
George Elmaraghy Federal Commissioner
Erich Emery US Army Corps of Engineers
Tom FitzGerald Federal Commissioner
Madeline Fleisher Environmental Law & Policy Center
Toby Frevert IL Commissioner
Eileen Hack IDEM
Tim Henry USEPA
John Kupke (Chair) IN Commissioner
Ron Lovan Commission Chairman (Kentucky)
Paul Novak IDEM/TEC NPDES Chair
Eric Nygaard OEPA
Ron Potesta WV Commissioner
Rob Reash Power Industry Advisory Committee
Martin Risch USGS
Mike Wilson NY Commissioner

## Slide 4: Ad Hoc Committee Identified Information Needs
Priority #1:
  Mass Balance to quantify and apportion sources of mercury in Ohio River.
  Are point sources having an impact and what is the magnitude of the impact?
  These questions could lead towards development of management scenarios.

## Slide 5: Ad Hoc Committee Recommended Study to Complete a Mercury Mass Balance for the Ohio River.
Considered various approaches.
Decided on a point source focus.
Relies heavily on existing studies and information.
Very low cost project. Completed with existing staff. No special studies/surveys/projects needed to complete the effort.
Project recommended Oct. 2016

## Slide 6: Background on Hg
Hg is a natural, trace element found everywhere
Global Pollutant – Atmospheric emissions.
Has toxicological risks to humans & wildlife
  Main exposure to humans is fish-consumption
Hg is responsible for Fish Consumption Advisories in all 50 states

## Slide 7: Fate and Transport within Aquatic Systems
Methylation
temperature
DO
organic matter
sulfates
sulfides
etc
Thresholds
USEPA – 0.3ppm
FDA – 1.0ppm
1 ml/wk FCA – 0.02ppm
*from Risch et al. 2010
Notes: Methylation rates of Ohio River main stem are believed to be low. Algae concentrate MeHg from water up to 10,000x. Can bioaccumulate up to 1,000,000x by top piscivore. Variable in each system based on many factors from presence of Se to types of zooplankton present. Commonly accepted that 90-100% of Hg in fish is MeHg. Higher concentrations in larger/older individuals of a species.

## Slide 8: Mass Balance Diagram
Ohio River
Trib Watershed
Atmospheric
+
Point Source
Trib Instream Sampling
Mainstem Instream Sampling
Trib Watershed
Atmospheric
+
Point Source
Trib Watershed
Atmospheric
+
Point Source
Trib Watershed
Atmospheric
+
Point Source
Trib Watershed
Atmospheric
+
Point Source
Trib Instream Sampling
Trib Watershed
Atmospheric
+
Point Source
Trib Instream Sampling
Atmospheric + PS = Instream

## Slide 9: Mass Balance/Source Apportionment
1) Calculate mass loads in Ohio River.
    Based on existing studies.
    Adjust data to trib timeframe Nov. ‘15-Oct. ‘16.
2) Calculate mass loads from 15 largest tribs.
    Accounts for approx. 85% of watershed.
    Based on sampling effort – Nov ‘15 to Oct. ‘16.

## Slide 10: Mass Balance/Source Apportionment (cont.)
3) Calc. Point Source Loads.
    Use USEPA ECHO data base.
    Align with trib sampling Nov ‘15-Oct ‘16
4) Putting It All Together.
    Instream = PS + Atmospheric
    Percent source contributions to instream.
    Nov ’15-Oct ‘16.

## Slide 11: Study Limitations Identified & Accepted from Project Inception
Atmospheric deposition study does not account for the amount of atmospheric mercury deposition retained in the landscape.
Point source loads rely on ECHO data base does not include data for all mercury discharges. Uses discharge monitoring report data.
Instream loads
  Used existing stream data from different periods of record (mainstem data adjusted to a common timeframe. LOADEST to calc. loads.
  Does not account for instream transport and fate.

## Slide 12: Project Components
Instream Loads – 4 mainstem; 15 tribs.
Point Source Loads.
Atmospheric Loads.
Mass Balance Accounting.
These are the 4 main components of the project.
Either one large report with a Chapter for each component, or 4 individual reports.

## Slide 13: Geographic Scope of Project

## Slide 14: Tributary Mass Balance
Watershed | Instream Hg Annual Load (lbs) | % Atmospheric Hg Contribution (loads in pounds) | % Point Source Hg Contribution (loads in pounds) | Number of Outfalls with Hg data
Allegheny | 81.1 | 17x (1,357) | 3.7% (3) | 7
Monongahela | 71.0 | 13x (901) | 2.2% (1.5) | 74
Beaver | 31.1 | 10x (322) | ~0% ~0) | 33
Muskingum | 80.7 | 10x (814) | ~0% (~0) | 80
Kanawha | 168.4 | 9x (1,530) | 20.5% (35) | 44
Big Sandy | 71.3 | 8x (557) | 0.7% (0.5) | 48
Scioto | 83.5 | 8x (687) | ~0% (~0) | 62
Little Miami | 10.8 | 18x (190) | ~0% (~0) | 22
Licking | 102.4 | 4x (423) | 0.1% (0.08) | 11
Great Miami | 17.1 | 33x (560) | 0.8% (0.1) | 53
Kentucky | 71.5 | 13x (894) | 13.9% (10) | 10
Green | 285.1 | 4x (1,197) | 1.6% (4) | 31
Wabash | 389.2 | 11x (4,088) | 9.3% (36) | 98
Cumberland | 211.1 | 11x (2,299) | 9.2% (19) | 47
Tennessee | 278.4 | 20x (5,482) | 4.9% (14) | 52

## Slide 15
Mainstem Mass Balance |  |  |  | 
Ohio River Stations | Instream Hg Annual Load (lbs) | % Atmospheric Hg Contribution (loads in pounds) | % Point Source Hg Contribution data provided (loads in pounds) | # of Outfalls w/ Hg Data Upstream of Station (including tributaries and direct watersheds)
ORM 126 | 223 | 13x (2,973) | 3.8% (8) | 186
ORM 282 | 593 | 10x (6,129) | 11.2% (66) | 389
ORM 782 | 2,153 | 5x (11,387) | 4.5% (96) | 704
ORM 912 | 2,961 | 6x (17,244) | 4.7% (139) | 856

## Slide 16
Chart: Tributary Mercury Instream Yield
| Allegheny | Monongahela | Beaver | Muskingum | Kanawha | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | Green | Wabash | Cumberland | Tennessee
Annual Instream Hg Yield (µg/m²/yr) | 1.2112 | 1.6865 | 1.726 | 1.7559 | 2.4074 | 2.9082 | 2.2453 | 1.0786 | 4.8376 | 0.55709 | 1.7963 | 5.4075 | 2.0682 | 2.0641 | 1.192

## Slide 17
Chart: Tributary Instream Mercury Contribution
| Allegheny | Monongahela | Beaver | Muskingum | Kanawha | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | Green | Wabash
% Tributary Instream Hg Contribution | 0.027386 | 0.023987 | 0.010509 | 0.027256 | 0.05686 | 0.024074 | 0.028195 | 0.003656 | 0.034568 | 0.0057653 | 0.024127 | 0.096287 | 0.13143

## Slide 18: Completion Schedule
At Feb TEC Meeting – Ask TEC for additions to Ad Hoc Mercury Committee membership.
March – Convene Ad Hoc Committee. Review project results/report. Concurrent TEC review.
June TEC Meeting -- Bring drafts back to TEC.
  Requested comments by end of May and have received 4 sets of comments to date.
Need any corrects to states’ point source DMR data.
Final draft to TEC/Ad Hoc no later than end of August.
Oct. TEC/Commission Meeting -- Finalize project/approve reports.