## Slide 1
Chris Nietch1, Leslie Gains-Germain2, Jim Lazorchak1, Scott Keely1, 1USEPA, Office of Research and Development, and 2Neptune and Company
The ideas and opinions expressed herein are those of the authors and do not reflect official position or policy of their affiliated agencies
CyanoHAB Risk Characterization Model
for the Ohio River
Photo: Flikr (J Stephen Conn)

## Slide 2
Background
Objective: Develop a risk characterization model for a CyanoHAB on the Ohio River based on the conditions that produced the record-setting bloom in 2015
-------------------------------------------------------------
Approach:
  determine data availability
  prepare data and conduct exploratory analysis
  derive conceptual model of cause and effect
  determine different modeling approaches
  develop and test different predictor variables
  model development and testing
  model refinement
  consider supporting information
  develop visualization application
  establish a strategy for serving stakeholders
Notes: Is that last bullet intended to be a circle rather than a checkmark?

## Slide 3
Hydrologic Data
Used historical data for flow on the Ohio River to characterize the unique hydrologic conditions that coincided with the record-setting HAB in the late summer of 2015
Important: We are NOT predicting the probability of a HAB, rather characterizing river flows in terms of their similarity to the conditions that coincided with the past HAB and presenting it as a probability!
Stage/Discharge Curves
flow
Use lock and dam tailwater flows and some free channel flows

## Slide 4
Conceptual cause and effects Model
Extensive Rainfall/Runoff Produces High Flows
Check time of year
Extended Period of low flows
Excessive Nutrient Loading
High Residence Time
Harmful Cyanobacteria bloom
Biological Source Strength?
Not light limited

## Slide 5
Ohio River Sites

## Slide 6
Prepare Data
Red = bloom period
High Flows in Late June to Mid July, followed extended period of low flow
Rank Flows at each site and use Exceedances to normalize across sites
Notes: I put up a new version of this that has the newer data, if you want to use it (although this one might be better because it has a blank area for the text): https://users.neptuneinc.org/lgermain/TO0002/eda/focused_eda.html

## Slide 7
Terms
21-55-day lagged exceedance - characterizes the flow conditions ca. 1month prior to the 2015 bloom: We suppose that flows have to be “High” for this period. This is the first criteria (lower exceedances = higher flows)
19-day lagged exceedance - characterizes the flow conditions proximal to bloom start. We suppose that flows have to be “Low” for an extended period for the bloom to develop. (higher exceedances = lower flows)
  “best fit” lag terms determined by brute force modeling of every possible combination and using AIC.
21-55-day lagged exceedance
19-day lagged exceedance
https://users.neptuneinc.org/lgermain/TO0002/eda/exceedances_and_lags.html

## Slide 8
Predictor Variables
For the model
“Maximum Ratio” - The maximum 0-19 to 21-55 lagged average exceedance ratio that occurred prior to the bloom start date
“Number of Increasing Ratio Days”
  The number of days in the 15 days prior to the day the maximum ratio occurred in which the ratio increased
      Found to be a better predictor than average slope of the ratio over the 15-day period
On other years (other than 2015), the maximum ratio is defined as the maximum ratio that occurred at any time during May to October when a HAB is possible
  Use time of year to set boundary conditions
predictors are summarized yearly, but probabilities will be estimated on a daily basis by using daily ratio and number of increasing ratio days
Only a probability based on similarities of flow conditions can be calculated for a given day!
Notes: On the third bullet, you could say that we included May through October as the domain of when a HAB is possible

## Slide 9
The Model
Used Mixed Effects Binary Logistic Regression in preliminary development and for optimizing lag terms.
Final version is a Bayesian Model including months May through October.
Notes: I think writing the name of the months would be more interpretable than saying the numbers

## Slide 10
Results
Probability plots are produced for each site with uncertainty. The model characterizes the uniqueness of the 2015 flow conditions at 20 of the 24 sites.
Interpretation: If river monitors observe a current day ratio of 28 that has been increasing for the previous 15 days, the probability of 2015 bloom conditions is 99% with a 95% confidence interval from 60% to 99.9%.
Notes: Interpretation: If river monitors observe a current day ratio of 28 that has been increasing for the previous 15 days, the probability of 2015 bloom conditions is 99% with a 95% confidence interval from 60% to 99.9%.

## Slide 11
Supporting Evidence - Nutrients
ORSANCO’s nutrient monitoring data for the mainstem and tributaries were analyzed to determine if there was evidence for elevated nutrient loads in and to the river in the period before the bloom (i.e., July). There were.
Plots of the data for TP, TN, and TIN are available in the risk characterization tool
Total Phosphorus Mainstem Loads
Total Phosphorus Tributary Loads
July 2015

## Slide 12
Supporting Evidence – Residence Time
The USACE provided pool volumes for the river. The L&Ds are operated largely to maintain a consistent pool volume for navigation. The volumes were used to determine if there was evidence supporting the idea that water residence time leading up to and during the bloom is a controlling factor.
Perhaps residence times in the upper river were not long enough for blooms to develop in sites above Pike Island.
Residence times in the upper river sites were shorter.
We’re looking into modeling residence times rather than flows.
Notes: Perhaps worth a mention that we’re looking into modeling residence times rather than flows?

## Slide 13
Risk Characterization Tool - Demo
R Shiny software was used to develop a web application that would allow river stakeholders to visualize data and model results. https://opencpu.neptuneinc.org/shiny-ohio-river/
Where real-time flow data is available the tool calculates the independent variables in the Bayesian model, then characterizes the existing conditions relative to those of 2015.
The result is then reported as a similarity to 2015 conditions in terms of a probability.
Notes: This is now updated with a probability and a confidence interval (and the model results plot now works)

## Slide 14
Conclusions
We used historical flow data for 27 Ohio River sites and our understanding of ecology of CyanoHABs to characterize the unique hydrologic conditions that coincided with the record-setting HAB in 2015.
We developed predictor variables to characterize what are assumed prerequisite flow conditions for a CyanoHAB and used them to parameterize a Bayesian model.
The model qualifies the flow conditions relative to bloom presence and absence and can report results in terms of a probability with uncertainty.
The probability for current conditions at a site can then be estimated and used to characterize the degree of similarity to conditions that produced the 2015 bloom.
We developed a risk characterization tool web application. It conveys risk in terms of the similarity of flow conditions in the present to those that produced a CyanoHAB in the past.
This tool could be accessed through the ORSANCO web site. Risk could be characterized for up to 20 sites along 900 miles of the river provided that real time flow information is available.

## Slide 15
Acknowledgements
Frank Borsuk, Region 3; Meghan Hemken, Region 5; Abram DeSilva and Brian Astifan, ORHFC-NWS; Robert Moyer and Erich Emery, USACE; Greg Youngstrom, Jason Heath, and Richard Harrison, ORSANCO; Anna Springsteen, Neptune and Company; Jeff Vogt, GCWW