## Slide 1: Short Strand DNA Tracer Projects
  Dr. Helen Buse, buse.helen@epa.gov
  Dr. Jim Goodrich, Goodrich.james@epa.gov
  John Hall, hall.john@epa.gov

## Slide 2: DNA Tracing Technology is Cool
Short strand DNA is considered Generally Recognized As Safe (GRAS) by the US Food and Drug Administration
Strands are less than 200 pairs
DNA strands are being added to ocean going vessels fuel tanks to facilitate spill forensics. Similar to how radioisotopes are added to petroleum pipeline products to identify ownership. Kind of a modern day Cattle Brand.
Also being used to identify conflict free diamonds from certified mines
Burberry clothing and handbags are also using DNA tracers

## Slide 3: Why is EPA Interested
We would like to calibrate the Riverine Spill Model Simulator.
http://rsms2017.cloudapp.net
Thankfully, there have not been enough large spills in the Ohio River since we updated and upgraded the HEC-RAS based RSMS.
Incorporate specific contamination route simulations. Develop in house expertise to perform studies under various river conditions.
From
http://www.hec.usace.army.mil/software/hec-ras/

## Slide 4: Brief History of DNA Tracers in Watersheds
Short strand DNA tracer research originated in Europe (groundwater, glacial melt, small streams). N. Paunescu is primary EU researcher. A. Sharma (Cornell) and H. Dahlke (UC Davis) are primary researchers in USA.
Environmental Science and Technology, 2012, 46 (16) pp 8928-8936, “Hydrological Tracers Using Nanobiology : Proof of Concept”, Asha N. Sharma, et. al.
Hydrological Processes, 2015 Vol. 29, Issue 25, pp 5257 -5274, “Using Concurrent DNA Tracer Injections to infer Glacial Flow Pathways” Helen Dahlke, et. al.
DNA Tracers used on small stream near Ithaca NY and Yuba and American Rivers in Northern California.

## Slide 5: More Background
The short strands need some type of coating or encapsulation to protect the DNA in the tracer.
Two major types of encapsulation are emerging. Polylactic Acid (PLA) or Silicon dioxide E551.
PLA is a food grade material and E551 is a synthetic amorphous silica used as an anti caking agent in foods.
University groups tend to make their own encapsulated DNA beads.
We didn’t think we would be good at making DNA beads without grad students so we have talked to 2 European companies to buy beads.
Forecast Technologies, Ltd. (UK) & Haelixa, Inc. (Switzerland)

## Slide 6: Starting Research with Haelixa

## Slide 7: Tracer Detection and Enumeration
After sample collection, tracer particles are dissolved to release the DNA, which is then mixed with qPCR reagents. The DNA sequence is then identified and quantified using a standard qPCR device, and data is processed to deliver easy-to-interpret results.
Analysis can be done either in high-throughput in our laboratories, or with a portable device on-site.

## Slide 8: A little Goes a Long way
1 mg = enough to trace 1 million liters (1ppt)
No magnetic parts – dispersion stable for expended periods of time

## Slide 9: Final Thoughts
This summer 2019, We would like to release some DNA beads into the Big Sandy River near the Marathon Refinery and go downstream and collect some samples for enumeration by Haelixa.
We are interested in getting your thoughts and input on the project.
We want to identify and obtain all the necessary permits for the DNA tracer study.
We are considering a co release of a food grade fluorescent dye with the DNA beads. The dye is not expected to persist but it may help locate the beads. (Rhodamine WT?)
We are upsizing the current research by an enormous magnitude. The steam in Ithaca was only 0.023 cu m/ sec. The Ohio River is over 100,000 cu ft/ sec.
What Permits and Approvals are necessary?

## Slide 10: Questions and Comments
John Hall (513) 487- 2814 or hall.john@epa.gov