## Slide 1
Preparing for Spills into Spills into Sources of Drinking Water
ORSANCO Technical Committee Meeting
June 5, 2019
Steven C. Allgeier
U.S. EPA
Office of Ground Water and Drinking Water
Water Security Division

## Slide 2
Presentation Overview
Risk of Acute Source Water Contamination
America’s Water Infrastructure Act: Section 2018, Source Water
America’s Water Infrastructure Act: Section 2013, Risk Assessments and Response Planning
Update on Ohio River Source Water Alliance Threat Inventory

## Slide 3: Risk of Acute Source Water Contamination

## Slide 4
How Common are Spills into Source Waters?
Analyze National Response Center spill reports
Analysis period: 2010 through 2018
Data standardization:
  Standardize names of material spilled
  Standardize names of bodies of water
  Standardize units for amount of material spilled
Removed spills with amount spilled < 100 gallons
Geospatial analysis to identify spills that could have impacted sources of drinking water
  Identify spills that occurred within 0.25 miles of an NHD flowline
Caveat: NRC spill reports are preliminary and often don’t capture the precise details of a spill

## Slide 5
Occurrence of Spills Potentially Impacting
Surface Water Sources (2010-2018)
Total Spills = 11,184

## Slide 6
Materials Spilled (2010-2018)
Material Category | Number of Spills | Cumulative Amount Spilled (gallons) | Cumulative Amount in Water (gallons)
Petroleum Products | 19,891 | 5,107,372 | 2,286,649
Other | 1,763 | 4,557,132 | 2,247,715
Unknown | 1,590 | 88,670 | 63,491
Gasoline | 1,427 | 5,621,991 | 382,663
Wastewater | 1,306 | 375,532,498 | 157,515,774
PCBs | 742 | 33,844 | 4,266
Antifreeze | 391 | 27,763 | 16,454
Paint | 262 | 7,205 | 1,236
Drilling Fluid | 200 | 8,486,235 | 6,139,365
Acids | 196 | 136,894 | 35,609
Total Spills = 29,024

## Slide 7
Types of Spills
Fixed Facilities: 8,267
Vessels/Watercraft: 4,853
Transportation: 3,915
Storage Tanks: 1,502
Pipelines: 1,005

## Slide 8
Incident Causes and Responsible Party
Incident Cause:
  Equipment failure
  Dumping
  Natural phenomenon, hurricane, flooding
  Transportation accident
Responsible Party:
  Private enterprise
  Private citizen
  Public utility
  Local government
  Military

## Slide 9: America’s Water Infrastructure Act Section 2018: Source Water

## Slide 10
Overview of America’s Water Infrastructure Act
Sec 2005: Drinking water resilience and sustainability grant program
Sec 2007: Innovative water technology grant program
Sec 2008: Improved consumer confidence reports
Sec 2012: Asset management
Sec 2013: Community water system risk and resilience
Sec 2014: Authorization for grants for State programs
Sec 2015: State revolving loan funds
Sec 2018: Source water
Sec 2020: Assistance for areas affected by natural disasters

## Slide 11
AWIA Section 2018: Source Water
Motivated by several recent source water contamination incidents, such as the MCHM spill into the Elk River in Charleston, WV in 2014
Amends the Emergency Planning and Community Right to Know Act (EPCRA)

## Slide 12
Overview of EPCRA
EPCRA was created to help communities plan for chemical emergencies
EPCRA regulates facilities that store or handle hazardous chemicals above threshold planning quantities
EPCRA administration and oversight:
  U.S. EPA Office of Emergency Management
  State Emergency Response Commissions (SERCs)
  Local Emergency Planning Committees (LEPCs)

## Slide 13
Key Provisions of EPCRA
Sec 301-303: Emergency Planning
Sec 304: Emergency Notification
Sec 311- 312: Chemical Inventories
Sec 313: Toxic Release Inventory
Sec 322: Trade Secrets

## Slide 14: Emergency Notification
Amends EPCRA Section 304 to add (e)(1) Applicable State Agency Notification

## Slide 15
SERCs & TERCs
State Drinking Water Primacy Agency
Community Water System
Promptly notify of reported release(s)
If no State Drinking Water Primacy Agency, directly notify Community Water System
EPCRA 304(b)(2)
304(c)
304(b)(2)
304(c)
EPCRA 304(b)(2)
304(c)
Promptly notify of reported release(s)
EPCRA 304(b)(2)
304(c)
Release Occurs and Facility Provides all Information Required Under EPCRA 304(b)(2) and 304(c)

## Slide 16
Information Included in the Notification
The chemical name
Extremely Hazardous Substance Y/N
An estimate of the quantity released
The time and duration of the release
The medium into which the release occurred
Acute or chronic health risks
Medical treatment for exposed individuals
Contact information for the responsible party

## Slide 17: Chemical Inventory Data Availability
Amends EPCRA Section 312(e) to add
Community Water Systems

## Slide 18
Chemical Inventory Data Availability
AWIA Sec 2018(b) amends EPCRA Sec 312
  Requires SERCs (or TERCs) and LEPCs (or TEPCs) to provide affected* community water systems with chemical inventory data submitted under Tier 2 of EPCRA for their source water area, upon request from the system.
  * One or more community water systems (as defined in SDWA Section 1401(15)) that receives supplies of drinking water from a source water protection area delineated under SDWA Section 1453, in which a facility that is required to prepare and submit an inventory form under EPCRA Section 312 is located.

## Slide 19: America’s Water Infrastructure Act Section 2013: Risk Assessment / Response Plan

## Slide 20
Consider risks from malevolent act and natural hazards
And must include:
  Pipes/conveyances, source water, water collection/intake, pretreatment, treatment, storage and distribution, electronic, computer, or other automated systems (including security);
  Monitoring practices;
  Financial infrastructure;
  Use, storage or handling of chemicals; and
  Operation and maintenance
Risk and Resilience Assessments

## Slide 21
Prepare or revise an Emergency Response Plan that incorporates findings from the risk assessment:
  Strategies and resources to improve resilience, including physical security and cybersecurity;
  Plans, procedures, and equipment for responding to a malevolent act or natural hazard;
  Actions, procedures, and equipment to lessen the impact of a malevolent act or natural hazard, including alternative source water, relocation of intakes, and flood protection barriers; and
  Strategies to detect malevolent acts or natural hazards.
Emergency Response Plans

## Slide 22
  Population
  served
  ≥100,000
March 31, 2020
  Population
  served
  50,000-99,999
December 31, 2020
  Population
  served
  3,301-49,999
June 30, 2021
Risk Assessment
Emergency Response Plan
Certify ERP not later than 6 months after completion of the risk assessment
Schedule

## Slide 23: Ohio River Source Water Alliance Contamination Threat Inventory

## Slide 24: Project Overview
Objective: develop a regional contamination threat inventory for 33 utilities along the Ohio River
Approach: inventory, manage, and analyze information about contamination threats to improved preparedness
Outcome: a robust threat inventory for the Ohio River and a model for other source water collaboratives

## Slide 25: Current Project Participants
ORSANCO
Greater Cincinnati Water Works
Northern Kentucky Water District
Maysville
Portsmouth
Louisville

## Slide 26
Overview of the Inventory Process
Establish boundary
Identify threat types
Collect & QC Information
Fill data gaps
Prioritize threats

## Slide 27
Chemical storage facilities
Power plants
Flyash lagoons
Pipelines
Discharges
Railways, hazmat routes, bridges
Landfills
Oil and gas wells
Conc. animal feeding operations
Identify the Types of Threats to Inventory

## Slide 28
Federal Resources
  Federal Registry Service
  Toxic Release Inventory System
State Resources
  State-level Tier II chemical inventories
  Above ground storage tank registries
  NPDES permits
Local Resources
  County-level Tier II data
  Commodity flow studies
Private / Non-profit Resources
  Watershed stewardship programs
Resources for Identifying Threats

## Slide 29: WaterSuite Platform
Secure, cloud-based system for managing information
Establishes relationships among data from disparate sources
Presents information in a geo-spatial context
Quality control and periodic updates to improve accuracy

## Slide 30
Zone of Critical Concern: 26 river-miles along main stem

## Slide 31
Extended Zone of Concern: 61 river-miles

## Slide 32
X-ZCC + Maysville-Portsmough: 138 river-miles

## Slide 33: Hazardous Chemical Storage Data Requests
We have data for: Clermont, OH 2016 Hamilton, OH 2016 Mason, KY 2017 Lawrence, OH 2013 | Outstanding counties intersecting the zones of concern: Brown, OH Adams, OH Scioto, OH Lewis, KY Greenup, KY

## Slide 34: Project Schedule
Complete inventory through Portsmouth Zone of Concern by July 2019
Schedule WaterSuite training for new users, summer 2019
Extend the inventory upstream to Huntington, WV and downstream to Louisville by July 2020
Refine the risk assessment / threat prioritization, ongoing
Apply inventory to source water protection activities, ongoing
Conduct project close-out workshop
Transition project ownership to the Ohio River Source Water Alliance / ORSANCO

## Slide 35: Contact Information
Steve Allgeier
allgeier.steve@epa.gov
513-569-7131
Contact Sam or Steve if your utility is interested in joining the Ohio River Contamination Threat Inventory project.
Sam Dinkins
sdinkins@orsanco.org
513-231-7719 x-108