## Slide 1: IN 604b HABs Monitoring Project
Agenda Item 4a

## Slide 2: 2018 Proposal
Install and maintain 2 datasondes on the Indiana section of the Ohio River for HAB detection.
Monitor for pH, temperature, conductivity, dissolved oxygen, turbidity, chlorophyll a, and phycocyanin.
Samples collected twice per month.
Nitrate/Nitrite, Total Kjeldahl Nitrogen, total phosphorus, soluble reactive phosphorus, chlorophyll, algal toxins (microcystins and cylindrospermopsin), and algal community.
Data made available on our web site.

## Slide 3: Locations
Grant awarded March 2019
Ohio River locations selected in coordination with IDEM
Markland L&D and Newburgh L&D
Installation planned for June 2019 (flow dependent)
Operate through June 2020
FLOW
DATASONDE
LOCATION

## Slide 4: 2019 IN604b
Applied for 2019 604b grant May 15.
Continuation of current project for 1 year.
Analysis of the data collected to determine causes of algal blooms.
Determination of award should be early 2020

## Slide 5: HAB Monitors
84.2 - Pike Island (ORSANCO)
279.2 - R.C. Byrd (Marshall University)
341.0 - Greenup (Marshall University)
436.2 - Meldahl (ORSANCO)
531.5 - Markland (IN 604b)
776.1 - Newburgh (IN 604b)

## Slide 6: Algal Toxin Recreation Standards
US EPA has released national recommendations for the Human Health Recreational Ambient Water Quality Criteria or Swimming Advisories for Microcystins and Cylindrospermopsin.
Microcystin – 8 ug/L
Cylindrospermopsin – 15 ug/L
Can be used in two ways
  As a recreational water quality criteria for frequency and duration EPA recommends states use 10 day assessment periods, not a rolling 10 day period, over the course of the recreation season. When an excursion occurs more than 3 times in a season and for more than one year, then the designated use would be impaired.
  For issuing a swimming advisory, EPA recommends the magnitude not be exceeded on any single day.

## Slide 7: Questions?