## Slide 2: PCB TMDLs in Virginia - Development and Implementation
2019 ORSANCO Technical Meeting (Richmond, VA)
Mark Richards
TMDL Team Lead / Sr. Environmental Scientist
October 9, 2019

## Slide 3: Outline
Background
Example PCB TMDL
  Source Contribution
TMDL Implementation
  Point Sources
    Example (Success Story)
  NonPoint Sources

## Slide 4
Impairments due to PCB Fish Consumption Advisories

## Slide 5
Polychlorinated Biphenyls (PCBs)
2 Carbon rings (6 carbon atoms to a ring, 12 total)
1 – 10 Chlorine atoms
0 – 9 Hydrogen atoms
209 different formations (known as congeners)
Mixtures of congeners are known by the trade name “Aroclor”
PCB 11
PCB 118
Notes: There are 209 different formations of PCBS that exist known as congeners.
How do we know about these though? Well somehow someone discovered a PCB-like chemical as a byproduct of coal tar in 1865. Then, 20 years later, it was decided, lets make this in a lab! And of course if we can make it, we can sell it. The commercial production of PCBS took off in the US in the 1930s with different mixtures of congeners, primarily under the trade name “Aroclor”, tailored for different uses.
Individual pure PCB congeners are colorless, often crystalline compounds, but commercial PCBs have a clear, light yellow or dark color. They do not crystallize at low temperatures, but turn into solid resins. Because of the chlorine atoms in the molecule, their density is rather high. PCBs are, in practice, fire resistant with rather high flash-points (170-380°C). They form vapors heavier than air, but do not form any explosive mixtures with air. They possess very low electrical conductivity and an extremely high resistance to thermal breakdown (US EPA, 1980; WHO/EURO, 1987; DFG, 1988).
The PCBs manufactured commercially are known by a variety of trade names including: Aroclor, Pyranol, Pyroclor (USA), Phenoclor, Pyralene (France), Clophen, Elaol (Germany), Kanechlor, Santotherm (Japan), Fenchlor, Apirolio (Italy), and Sovol (USSR). Table 3 contains the most common trade names for commercial products, some of which are not in use any more (Brinkman & De Kok, 1980; WHO/EURO, 1987)

## Slide 6: Congener vs Homolog vs Aroclor
Homolog | Congeners
mono | 1-3
di | 4-15
tri | 15-39
tetra | 40-81
penta | 82-127
hexa | 128-169
hepta | 170-193
octa | 194-205
nona | 206-208
deca | 209
PCB 11
Aroclor 1260
Notes: Congeners: 209 possible formations of a PCB with regards to # of chlorine atoms and position of the chlorine atoms
Homologs: groups of congeners grouped by the number of chlorine atoms
Aroclors: tradename of congener mixtures produced by Monsanto (other companies produced Aroclor-like mixtures too). The naming nomenclature follows a basic formula. For example Aroclor 1260 is so named because it has 12 carbons and is 60% Chlorine by weight. Though I am not sure why there is a 1016…. which is a distillation product of Aroclor 1242 containing only 1% of components with 5 or more chlorine atoms (Burse et al., 1974)
Pyranol, Pyroclor (USA), Phenoclor, Pyralene (France), Clophen, Elaol (Germany), Kanechlor, Santotherm (Japan), Fenchlor, Apirolio (Italy), and Sovol (USSR)

## Slide 7: PCB Analytical Methods
EPA Method 608
Detection Limit: 0.065 ug/L
7 Aroclors Underestimates tPCBs
EPA Method 1668
Detection Limit: 0.000003 ug/L
209 Congeners
Accounts for weathering
Notes: The difference between the 2 images is akin to the differences in the EPA Method 608 that is still used to determine compliance for point sources and the new method, EPA 1668. 1668 has a detection limit that is 13000 times smaller than 608 and can detect all 209 congeners, while 608 can only detect 7 Aroclor mixtures of congeners. This means 1668 can detect VERY LOW levels of ALL 209 versions of PCBs. This is a big deal.
Since the 1980s, we have not detected any PCBs coming from a lot of point sources and therefore assumed they were not contributing anything to the daily load of PCBs into the environment. But 1668 has shown how we were wrong. For example, in the New River PCB TMDL study from Radford to where it reaches West Virginia receives over half of its PCBs from point sources. DEQ has established and encouraged permitted facilities that are potential sources for PCBS to take effluent samples and analyze them via 1668. This gives DEQ a better sense of what is actually entering from the water from their facility and more than likely will lead to a smaller reduction (for WLA).
A note…
Contract with laboratories (not DCLS)
Water & SED: SGS AXYS, 1668
FT & some SED: VIMS, VELAP certified process (subset and not as sensitive as 1668)

## Slide 8: Toxics Substances Control Act (TSCA)
1976 Law regulates PCBs
  Bans the manufacture, processing, use and distribution in commerce
  Non-PCB Transformer defined as containing < 50 ppm PCB
  Inadvertent manufacture of PCBs – products up to 50 ppm allowed to leave site as long as annual average is < 25 ppm
    Unintentional by-products of manufacturing processes
50 ppm compared to DEQ’s WQC - 6.4 X 10-7 ppm (0.00000064)
Notes: Banned in 1979
PCB Regulations: Part 761 in Title 40 of the Code of Federal Regulations
https://www.epa.gov/pcbs/learn-about-polychlorinated-biphenyls-pcbs
Has list of federal notices
6 Sept 2012: changes made so that PCB regs matched RCRA regs (40 CFR 262, 263, 264)
TSCA Cleanup level of 1 ppm
9VAC20-81-630: wastes containing PCBs (effective 2011)

## Slide 9
Examples of Other products tested
  Pennzoil SAE5W-30
  Valvoline Full Synthetic
  Road paint
March 2015

## Slide 10: VA Water Quality Criterion-Total PCBs
Water Quality - Acute/Chronic criterion
Tissue and PWS - WQC represents concentration in the water column where the bioaccumulation of tPCBs in fish and drinking water is minimized for safe human consumption (derived from fish tissue)
Consumption Advisories Fish Tissue (ppb) | Water Quality Criterion (ppb)
VDH (100) DEQ (20) | 0.00064
PCB WQC
FDA Threshold for prohibition of interstate commerce in fish tissue = 2.0 ppm (or 2,000 ppb)
Challenge - No expression for duration/frequency of excursions
Notes: At some point it was 50 pg/g BUT VDH has changed what they consider to be the average human weight & rate of consumption
Site specific= equation derived value that takes into account x,x,x,x and is the value that would get fish tissue <20 pg/g (screening advisory)
…talk about median vs 30-day rolling average?

## Slide 11: Site Specific Endpoint BAF (New River PCB TMDL)
VA WQC
Combined observations
2010
2011
2013
2014
Modeled PCB Concentrations
Notes: Box & Whisker plots (whisker = range) quartiles; first data set on left = modeled data using HMFY 2006; second is combined observations, third and one are by year.

## Slide 12
Non-point source
PCB Contaminated
Sediment
Wet Deposition
Dry Deposition
Air Emissions
Non-point source
Runoff
2
Contaminated Sites
1
6
5
MS4 SW Runoff
4
Point Source Effluent
Runoff
3
Sources
Considered
within PCB TMDL
PCB
PCB
PCB
PCB
PCB

## Slide 13: TMDL Source Category – Point Sources
Permitted facilities effluent screened using DEQ’s PCB Monitoring Guidance (TMDL GM 09-2001)
  Municipal WWTP
  Standard Industrial Classification (SIC)
    Individual Industrial Facilities
    Industrial Storm Water General Permitted Facilities
PCB effluent data collected from most applicable facilities for a TMDL study
  Default tPCB values used when low level PCB data unavailable
    Specific to Standard Industrial Classification (SIC)
    Median tPCB concentrations derived from statewide database.

## Slide 14: TMDL Category – Non-Point Sources (Contaminated Sites)
Contaminated Sites:
  RCRA Corrective Action Program, CERCLA/Federal Facilities Program, VRP, & Regional Office anecdotal evidence
  Review Available Databases
    CERCLIS
    PCB Activity Database System (PADs)
    EPA’s Superfund website
  Electric Utility Transformer Pads (spills)
  Railyards/spurs
  Pollution Response Spills

## Slide 15: New River PCB TMDL (2018)

## Slide 16: PCB TMDL - Lower New River
TMDL = 164.5g/yr 92.2% reduction (Based on WVA WQC and 0% exceedance)
Chart: Relative Contribution (%) of different PCB sources to the Lower New River
| Permitted Facilities | MS4 Permits | Atmospheric Deposition | Boundary inputs | Streambed sediment | Spills | Uncharacterized sources | Railyards | Contaminated Sites
 | 54 | 17 | 1 | 17 | 0.5 | 0.2 | 11 | 0.2 | 0.25
Existing Load = 2115.5 g/yr
Parameter | C3 | A4
PCB (ng/l) | 0.045 | 0.044
West Va 47CSR2
Appendix E, Table 1
3 Protect human health …through fish consumption; Conc. not to be exceeded.
4 Protect human health …through drinking water; Conc. not to be exceeded
TMDL Endpoint
WLA
LA
Notes: 40 CFR131.10(b) Must take into consideration WQS of downstream waters and provide for the attainment and maintenance of WQS in downstream waters.

## Slide 17
Implementation Process
Point sources
WLA---- PMP
Nonpoint sources
Source “Fingerprinting”
Deliberate Monitoring
Investigation
of Hotspots
Detect “uncharacterized sources”
Funding

## Slide 18: VPDES Point Sources
If existing (baseline) condition > WLA
Pollutant Minimization Plan
Submitted and Approved
Backtrack/Source ID
Re-evaluate baseline load
Remediation
/BMPs
Adaptive Implementation

## Slide 19: Point Source/Nonpoint Source - “fingerprinting”
Objective: To identify a specific pattern or “fingerprint” of congeners that could be indicative of a pollution source
1. # of fingerprints in the system
2. Chemical composition in each fingerprint
3. contribution of each fingerprint in each sample

## Slide 20: Fingerprinting Methods
Approaches
  Visual (homologs)
  Principal Component Analysis (PCA)
  Positive Matrix Factorization (PMF)
  Cosine Similarity
Chart: 
| 3-MTN024.05Se | 3-XIH000.06-S | 3-BLS000.08-S | 3-HID000.22-S | 3-MTN022.01-S | 3-XEH000.10-S | 3-XEH000.10-S | 3-MTN014.88-S | 3-MTN000.59-S
mono ratio to tPCB | 0.0026683 | 0.0016565 | 0.0025083 | 0.0010347 | 0.00042421 | 0.004385 | 0.0055339 | 0.0003754 | 0.00011523
di ratio to tPCB | 0.010965 | 0.07301 | 0.035814 | 0.022312 | 0.0097017 | 0.11136 | 0.11098 | 0.0024437 | 0.0011725
tri ratio to tPCB | 0.046066 | 0.35646 | 0.036718 | 0.017519 | 0.042177 | 0.046476 | 0.049552 | 0.0067222 | 0.0037352
tetra ratio to tPCB | 0.1141 | 0.42969 | 0.091476 | 0.06855 | 0.14528 | 0.088323 | 0.088798 | 0.045834 | 0.024519
penta ratio to tPCB | 0.24164 | 0.10598 | 0.20396 | 0.34558 | 0.26141 | 0.24443 | 0.23068 | 0.32368 | 0.25415
hexa ratio to tPCB | 0.31024 | 0.019756 | 0.3015 | 0.36925 | 0.25395 | 0.27956 | 0.28687 | 0.46346 | 0.52397
hepta ratio to tPCB | 0.13931 | 0.008382 | 0.17191 | 0.1113 | 0.10236 | 0.13062 | 0.13338 | 0.10941 | 0.13359
octa ratio to tPCB | 0.063828 | 0.0033972 | 0.080174 | 0.047432 | 0.09086 | 0.058153 | 0.057934 | 0.033421 | 0.0359
nona ratio to tPCB | 0.037332 | 0.0011141 | 0.046654 | 0.01369 | 0.073661 | 0.025222 | 0.0254 | 0.011071 | 0.016883
deca ratio to tPCB | 0.033856 | 0.0005527 | 0.029292 | 0.0033399 | 0.020163 | 0.011481 | 0.010871 | 0.0035809 | 0.0059653
Sediment PCB results – Homolog ratios to tPCB

## Slide 21: Staunton R. Sediment - Textile Mill PCB Signature -
Congeners 155 & 184
Chart: Total PCBs in Sediment Collected from the Staunton River
| 131.55000000000001 | 129.55000000000001 | 127.79 | 97.76 | 90.5 | 67.910000000000025 | 59.120000000000012
Sediment | 2922 | 1294 | 762 | 8447 | 65267 | 109553 | 71337
Chart: Total PCBs Compared with Two PCB "ITG Tracer" Congeners in Sediment Collected from the Staunton River
| 131.55000000000001 | 129.55000000000001 | 127.79 | 97.76 | 90.5 | 67.910000000000025 | 59.120000000000012
tPCB Sediment | 2922 | 1294 | 762 | 8447 | 65267 | 109553 | 71337
Congener 155 | 5.9 | 0 | 10.1 | 4.7 | 8.5 | 50.8 | 32.1
Congener 184 | 10.4 | 0 | 13.1 | 10 | 13.2 | 96.4 | 58.4

## Slide 22: Staunton River – Textile Mill Treatment Ponds
tPCB = 13,100 pg/L water
tPCB = 1,210 ng/g (ppb) sludge
PCB 155 ~ 33%, PCB 184 ~ 48% of total
tPCB = 17,200 pg/L water (n = 2)
tPCB = 1,290 ng/g (ppb) sludge
PCB 155 ~ 33%, PCB 184 ~47% of total
> 10 Million Gallons contaminated Wastewater
Polishing Pond
Aeration Basin
Contributed ~ 10 % of PCB load

## Slide 23: Staunton River – Textile Mill
Ensured at least 185 g of PCB not released to river
TMDL Source ID Study detected previously unknown contamination
  Success story found on DEQ’s webpage
Aeration Basin
Polishing Pond

## Slide 24: Point Source PMP Guidance
Guidance under development
  PCB Track Down/Sampling Plan
  Industrial, Municipal, MS4(?)
  Source Identification (Site specific)
    Includes a table offering a variety of PCB Analytical Methods (method pros/cons, relative cost, etc.)
    Analytical Method selection optional based on study objective
        Method 1668 not required for track down
  Influent/Effluent, evaluate flows from pump stations
  Fingerprinting techniques are an option (benefit of using more sensitive method)

## Slide 25: Non-Point Source Approach
Nonpoint sources
Source “Fingerprinting”
Deliberate Monitoring
Investigation
of Hotspots
Detect “uncharacterized sources”
Only during wet weather
Sediment sample= 100,715 pg/g
Use fingerprints to identify potential sources
Focus monitoring efforts on areas with railyards to validate model PCB loads

## Slide 26: Funding Options
Virginia Environmental Emergency Responses Fund
Emergency response to pollution incidents
For the development and implementation of corrective actions
EPA Section 319 funds
For BMPs used to reduce soil erosion
Supports education and monitoring to assess the success of nonpoint source implementation projects
Virginia State Revolving Fund
Provides financing option for cities, towns and wastewater authorities for the upgrade, expansion or repair to public wastewater collection and treatment facilities

## Slide 27: TMDL - Contaminated Sites
RCRA Corrective Action, TSCA, CERCLA
Clean-up standards for land based contaminated sites have no relationship to PCB water quality criterion
  The PCB clean-up level of 1 mg/kg is not adequate to protect the fish consumption use
How about PCB contaminated drainage that leaves the site?
  Contamination occurs when stormwater comes into contact with PCB contaminated soils (< 1 mg/kg) and migrates off-site (e.g., MS4, direct drainage to waterbody, etc.)

## Slide 28: U.S. Navy PCB Monitoring (2011-2012)
Chart: Mean tPCB (pg/L) by Facility
| Craney Island Defense Fuel Support Point - Navy | Naval Station Norfolk | Norfolk Naval Shipyard | Southgate Annex - Navy | St. Juliens Creek - Navy
Individual Permits | 31.3215 | 8102.9181 | 10123.8356 | 0 | 0
SW Industrial Permits | 0 | 0 | 0 | 14492.535 | 3828.2483
Data source: U.S. Navy

## Slide 29: Norfolk Naval Station

## Slide 30: Possible BMPs
Use individually or in a “treatment train”
  Flow Reduction/Eliminate contact
  Sedimentation ponds
  Natural Media Filtration
  Buffer Strips
  Phytoremediation
    Switchgrass (with bioaugmentation)
PCB Pollution Minimization Plan Guidance:
*PMP Guidance document under development*
Supporting documentation
Pollution Minimization Plan Technical Resource Guide
Table 1 - Media and Technologies
Table 2 - Technology Summaries
DEQ’s Webpage – Resources for PCB TMDLs

## Slide 31: Thank You!
Mark.richards@deq.virginia.gov