## Slide 1: 2019 HAB Event
Agenda Item 4c
Anderson Ferry (ORM 477.5)

## Slide 2
September 11
Russell, KY
Report from KY-DOW of
algae bloom at Russell intake

## Slide 3
September 12
Huntington WV – Greenup L&D
Approximately 35 miles
Identified as
Microcystis wessenbergii
8.2 ug/L
microcystin

## Slide 4
September 17
Ripley, OH
Citizen report
Repeat of sampling in Greenup Pool
Reduced bloom conditions observed

## Slide 5
September 19-20
Cincinnati, OH
Mile 462-477
9.8 ug/L
microcystin
KY DOW issues cautionary statement – 9/23

## Slide 6
September 24-26
Cincinnati, OH
Mile 462-477
1020 ug/L
microcystin
Louisville/Beargrass Creek
Neville, OH
10.3 ug/L
Aberdeen, OH
>25 ug/L
Recreational advisory issued – 9/26

## Slide 7
October 1-2
Cincinnati, OH
Mile 462-477
835 ug/L
microcystin
Louisville/Beargrass Creek
Neville, OH
0.699 ug/L
Aberdeen, OH
6.34 ug/L
16 ug/L
microcystin

## Slide 8: Recreation Advisories
Advisories in Meldahl, Markland, and McAlpine Pools

## Slide 9: Week of October 7
KY-DOW sampling in Louisville area
  Ironman swim scheduled for October 13
US EPA – Cincinnati area (counts, toxin, nutrients)
ORSANCO observe/sample
  Cincinnati area (462-477.5)
  Ironton, OH – Meldahl L&D (327-436)
  Markland L&D (531.5)
  Carrolton, KY-Hanover, IN (545-562)
  Newburgh L&D (776.1)
  JT Myers L&D (846.0)

## Slide 10: General Observations
Bloom is intermittent. Not continuous as it was in 2015
Advisories/cautionary statements from KY, OH, IN
Sampling/observations from Corps of Engineers, USEPA, PA, WV, KY, OH, IN, IL, ORSANCO
Observations covered all of the Ohio River and major tributaries
Weekly conference calls to coordinate sampling/laboratories
Conference calls/sampling to continue until all advisories lifted