## Slide 1: Status of Ohio River Basin Mercury Loading Analysis Project
Report to TEC Committee
October 7-8, 2019

## Slide 2: Ad Hoc Mercury Committee Background
  Ad Hoc Established June, 2015.
  Held 5 conference calls & meeting Aug. ‘16.
  Charge:
    Identify what is known and unknown about mercury.
    Determine the value and costs of addressing the unknowns.
    Make recommendations for studies to the Commission.
  Work completed by Mercury Ad Hoc:
    Identified available outside data.
    Completed literature review & background report.
    Identified and prioritized information needs.
    Identified a project and schedule to fill in information gaps.
  Held 5 conference calls.
  1 in-person meeting at ORSANCO Aug. 3.

## Slide 3: Committee Membership
Stuart Bruny OH Commissioner
Doug Conroe NY Commissioner
Jessica Dexter Environmental Law & Policy Center
George Elmaraghy Federal Commissioner
Erich Emery US Army Corps of Engineers
Tom FitzGerald Federal Commissioner
Madeline Fleisher Environmental Law & Policy Center
Toby Frevert IL Commissioner
Eileen Hack IDEM
Tim Henry USEPA
John Kupke (Chair) IN Commissioner
Ron Lovan Commission Chairman (Kentucky)
Paul Novak IDEM/TEC NPDES Chair
Eric Nygaard OEPA
Ron Potesta WV Commissioner
Rob Reash Power Industry Advisory Committee
Martin Risch USGS
Mike Wilson NY Commissioner

## Slide 4: Ad Hoc Committee Identified Information Needs
Priority #1:
  Mass Balance to quantify and apportion sources of mercury in Ohio River.
  Are point sources having an impact and what is the magnitude of the impact?
  These questions could lead towards development of management scenarios.

## Slide 5: Ad Hoc Committee Recommended Study to Complete a Mercury Mass Balance for the Ohio River.
Considered various approaches.
Decided on a point source focus.
Relies heavily on existing studies and information.
Very low cost project. Completed with existing staff. No special studies/surveys/projects needed to complete the effort.
Project recommended Oct. 2016

## Slide 6: Background on Hg
Hg is a natural, trace element found everywhere
Global Pollutant – Atmospheric emissions.
Has toxicological risks to humans & wildlife
  Main exposure to humans is fish-consumption
Hg is responsible for Fish Consumption Advisories in all 50 states

## Slide 7: Mass Balance Diagram
Ohio River
Trib Watershed
Atmospheric
+
Point Source
Trib Instream Sampling
Mainstem Instream Sampling
Trib Watershed
Atmospheric
+
Point Source
Trib Watershed
Atmospheric
+
Point Source
Trib Watershed
Atmospheric
+
Point Source
Trib Watershed
Atmospheric
+
Point Source
Trib Instream Sampling
Trib Watershed
Atmospheric
+
Point Source
Trib Instream Sampling
Atmospheric + PS = Instream

## Slide 8: Mass Balance/Source Apportionment
1) Calculate mass loads in Ohio River.
    Based on existing studies.
    Adjust data to trib timeframe Nov. ‘15-Oct. ‘16.
2) Calculate mass loads from 15 largest tribs.
    Accounts for approx. 85% of watershed.
    Based on sampling effort – Nov ‘15 to Oct. ‘16.

## Slide 9: Mass Balance/Source Apportionment (cont.)
3) Calc. Point Source Loads.
    Use USEPA ECHO data base.
    Align with trib sampling Nov ‘15-Oct ‘16
4) Putting It All Together.
    Instream = PS + Atmospheric
    Percent source contributions to instream.
    Nov ’15-Oct ‘16.

## Slide 10: Geographic Scope of Project

## Slide 11: Tributary Mass Balance
Watershed | Instream Hg Annual Load (lbs) | % Atmospheric Hg Contribution (loads in pounds) | Old % Point Source Hg Contribution (loads in pounds) | New % Point Source Hg Contribution (loads in pounds) | New Number of Outfalls with Hg data
Allegheny | 81.1 | 17x (1,357) | 3.7% (3) | 3.2% (2.6) | 7
Monongahela | 71.0 | 13x (901) | 2.2% (1.5) | 1.8% (1.3) | 50
Beaver | 31.1 | 10x (322) | ~0% (~0) | 3.2% (1) | 33
OR Direct 1 |  | (394) | (3.9) | (127) | 67
Muskingum | 80.7 | 10x (814) | ~0% (~0) | 3.2% (2.6) | 101
Kanawha | 168.4 | 9x (1,530) | 20.5% (35) | 21.6% (34) | 42
OR Direct 2 |  | (812) | (23.3) | (24) | 68
Big Sandy | 71.3 | 8x (557) | 0.7% (0.5) | 0.7% (0.5) | 32
Scioto | 83.5 | 8x (687) | ~0% (~0) | 3.9% (3.2) | 82
Little Miami | 10.8 | 18x (190) | ~0% (~0) | 5.9% (0.6) | 28
Licking | 102.4 | 4x (423) | 0.1%(0.08) | 0.1% (0.1) | 9
Great Miami | 17.1 | 33x (560) | 0.8% (0.1) | 16.8% (2.9) | 69
Kentucky | 71.5 | 13x (894) | 13.9% (10) | 1.1% (0.8) | 8
OR Direct 3 |  | (87) | (19.3) | (87) | 116
Green | 285.1 | 4x (1,197) | 1.6% (4) | 1.9% (5.3) | 27
Wabash | 389.2 | 11x (4,088) | 9.3% (36) | 6.8% (27) | 86
OR Direct 4 |  | (573) | (2.4) | (19) | 19

## Slide 12
Ohio River Mainstem Mass Balance |  |  |  |  | 
Ohio River Stations | Instream Hg Annual Load (lbs) | % Atmospheric Hg Contribution (loads in pounds) | Old % Point Source Hg Contribution data provided (loads in pounds) | New % Point Source Hg Contribution data provided (loads in pounds) | New # of Outfalls w/ Hg Data Upstream of Station (including tributaries and direct watersheds)
ORM 126 | 223 | 13x (2,973) | 3.8% (8) | 58.9% (131) | 157
ORM 282 | 593 | 10x (6,129) | 11.2% (66) | 32.8% (195) | 368
ORM 782 | 2,153 | 5x (11,387) | 4.5% (96) | 13.5% (290) | 712
ORM 912 | 2,961 | 6x (17,244) | 4.7% (139) | 10.9% (323) | 844
Ohio River Basin Total (lbs) |  |  | 178.5 | 355 | 

## Slide 13
Chart: Tributary Mercury Instream Yield
| Allegheny | Monongahela | Beaver | Muskingum | Kanawha | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | Green | Wabash | Cumberland | Tennessee
Annual Instream Hg Yield (µg/m²/yr) | 1.2112 | 1.6865 | 1.726 | 1.7559 | 2.4074 | 2.9082 | 2.2453 | 1.0786 | 4.8376 | 0.55709 | 1.7963 | 5.4075 | 2.0682 | 2.0641 | 1.192

## Slide 14
Chart: Ohio River Tributaries Annual Mercury Loads
| Allegheny | Monongahela | Beaver | Muskingum | Kanawha | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | Green | Wabash | Cumberland | Tennessee
Instream | 81.095 | 71.0308 | 31.1178 | 80.7106 | 168.3721 | 71.2874 | 83.4912 | 10.8261 | 102.3623 | 17.0721 | 71.4456 | 285.1243 | 389.1786 | 211.0972 | 278.4358
Atmospheric | 1356.5949 | 900.9994 | 321.6985 | 813.8654 | 1529.9592 | 557.0671 | 687.1295 | 190.0632 | 423.3557 | 559.6606 | 894.3914 | 1197.3988 | 4087.8493 | 2299.0311 | 5482.2279
Point Source | 2.5858 | 1.2845 | 0.98452 | 2.6026 | 36.4518 | 0.49359 | 3.2191 | 0.64273 | 0.066758 | 2.8636 | 0.7653 | 5.3318 | 26.6451 | 18.9875 | 13.5497
1,530
4,088
2,299
5,482

## Slide 15
13x
Chart: Ohio River Accumulation Percent of Atmospheric & Point Source Mercury loads per Instream Load at ORM 912
| ORM 126 | ORM 282 | ORM 782 | ORM 912
Atmospheric | 13.3269 | 10.3329 | 5.2894 | 5.8235
Point Source | 0.58925 | 0.32817 | 0.13479 | 0.10906
59%
33%
14%
11%

## Slide 16
Chart: Tributary Instream Mercury Contribution per Total Instream Mercury (ORM912)
| Allegheny | Monongahela | Beaver | ORM 126 | Muskingum | Kanawha | ORM 282 | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | ORM 782 | Green | Wabash
% Tributary Instream Hg Contribution | 0.027386 | 0.023987 | 0.010509 | 0.07534 | 0.027256 | 0.05686 | 0.20031 | 0.024074 | 0.028195 | 0.003656 | 0.034568 | 0.0057653 | 0.024127 | 0.72698 | 0.096287 | 0.13143
72.7%

## Slide 17
Chart: % Point Source Mercury Contribution per Total Instream Mercury (ORM 912)
| Allegheny | Monongahela | Beaver | OR Direct 1 | Muskingum | Kanawha | OR Direct 2 | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | OR Direct 3 | Green | Wabash | OR Direct 4 | Cumberland | Tennessee | OR Direct 5
 | 0.00087323 | 0.00043378 | 0.00033248 | 0.042755 | 0.00087892 | 0.01231 | 0.0081524 | 0.00016669 | 0.0010871 | 0.00021705 | 2.2544e-05 | 0.00096704 | 0.00025844 | 0.029535 | 0.0018006 | 0.0089981 | 0.00027714 | 0.0064121 | 0.0045758 | 0.0025624
4.28%
3%

## Slide 18: Results of August, 2019 Ad Hoc Committee Call
Committee recommended all states submit updated point source mercury data.
No consensus to include/exclude intermittent stormwater discharges.
Committee recommended to exclude non-contact cooling water discharges.
Committee recommended including the Cumberland & Tennessee River Basins in the report even though they enter the Ohio River downstream of the most downstream mainstem mercury station.
Committee recommends revising report title from “Mass Balance” to “Loading Ananlysis”.
Report needs additional discussion on its relevancy, as well as limitations of the study.

## Slide 19: Project Status
Ad Hoc Mercury Committee & TEC have been given multiple opportunities to comment on the written report. Many comments have been received and incorporated into the report. Staff has maintained a log of comments with their disposition.
Updated point source data has been received and is still needed from one state. The report has been updated with all revised point source data received.
Identification of non-contact cooling water outfalls is needed in order to exclude those from the point source loadings.
Based on updated point source data, all point sources in the basin account for approximately 11% of the instream mercury at ORM 912. This figure doubled from previous estimates with uncorrected point source data.
Future report revisions would include updated point source data from one state, and incorporation of Marty Risch’s comments to the extent practical.
Report title needs to be changed. Additional discussion of project relevancy and limitations is needed for the report.
A final draft is anticipated to go out with agendas for the February 2020 meetings.