## Slide 1: Ohio River PFAS Study
Survey Design

## Slide 2: Study Objective
Characterize present ambient concentrations of PFASs in Ohio River at multiple locations.
  Baseline of 20 sites
  Outside of any regulatory mixing zones
2 separate events – attempt to get 1 higher flow & 1 lower flow condition.
Results may inform states, EPA, utilities & other interested parties on Ohio River ambient water quality conditions.

## Slide 3: Project Scope
USEPA research lab will analyze water samples for PFASs.
They have indicated 20 samples would be doable. Thus survey design is based on 20 sampling sites.
ORSANCO will collect samples.
Begin survey Spring, 2020?

## Slide 4: General Workplan
1) Establish Work Group to develop work plan specifics.
  Ask TEC members to appoint representative.
  Workgroup will propose:
    Monitoring locations.
    Sample collect methodology and all that goes with it.
    Suite of PFAS compounds to be analyzed for (GenX).
2) Selection of Sampling Sites
  Good spatial coverage.
  Look at probabilistic approach.
  Reflect ambient conditions.
  Represent range of flows.

## Slide 5: General Workplan (cont.)
3) Establish Sample collection protocol
  Grab sample versus USGS “IDE” method.
  Minimization of sample contamination potential.
  Determination of field QA samples.
4) Analyte selction ie. GenX? Other PFASs.

## Slide 6: PFAS Workgroup Met Jan 15 and May 23
Bruno Pigott – Commissioner/TEC Chairman
Ron Potesta – Commissioner/Commission Chairman
Eileen Hack, Ally Miles – IDEM
Erich Emery – USACE
Bruce Whitteberry – WUAC
Katie McKone – KYDOW
Kevin Halloran – PADEP
Mike Profitt, Jeff Lewis, Erin Sherer, Audrey Rush – OEPA
Amy Kramer – NKY Water
Chris Tavenor – OH Environmental Coalition
John Wirts - WVDEP

## Slide 7: Site Selection Proposal
Survey of Ambient Conditions
20 Sampling Stations
Probabilistic/Systematic Sampling Approach
  Recommended by EPA Expert
Sites outside of regulatory mixing zones.
Good geographic coverage

## Slide 8: Sample Collection Methodology
Preferred Method is EDI-Equal Discharge Increment.
Collects a flow-weighted cross-sectional composite of the river.
Needs to be evaluated for suitability for PFAS compounds.

## Slide 9: USGS EDI Sampling Equipment

## Slide 10: What to Sample
EPA has a couple of analytical methods – both include 24 PFAS compounds.
Workgroup asked to see detection levels on both methods.
Rely heavily on EPA expertise for method selection.
Workgroup recommends including Gen-X compounds – EPA can do this.
Flow measurements at every site with ADCP (Acoustic Doppler Current Profiler) instrumentation considers full X-sectional flows.

## Slide 11: Systematic-Probabilistic Approach

## Slide 12: 20 PFAS Sampling sites overview

## Slide 13
Alternate Sites
Original Probabilistic Sites

## Slide 15: 1) Mile point 11.70
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
1 | 11.70 | 40.534042 | -80.186169 | 40.532756 | -80.187306 | 40.531569 | -80.188344
Alt.1 | 11.76 | 40.533628 | -80.185131 | 40.532275 | -80.186281 | 40.530983 | -80.187356

## Slide 16: 2) Mile Point 60.75
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
2 | 60.75 | 40.441808 | -80.604633 | 40.442611 | -80.607167 | 40.443372 | -80.60965

## Slide 17: 3) Mile Point 109.80
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
3 | 109.80 | 39.854978 | -80.802628 | 39.856433 | -80.803547 | 39.857931 | -80.80445
Alt.3 | 111.32 | 39.844158 | -80.822678 | 39.844819 | -80.824314 | 39.845539 | -80.826133
Revised Alt. 3 | 109.60 | 39.856656 | -80.799325 | 39.858006 | -80.800511 | 39.859372 | -80.801739
Original #3 proposed sampling site

## Slide 18: 3) Mile Point Alternatives
Alternative 3) Mile Point 111.32
Revised Alternative 3) Mile Point 109.60

## Slide 19: 4) Mile Point 158.85
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
4 | 158.85 | 39.378058 | -81.2717 | 39.380636 | -81.274233 | 39.383108 | -81.276708
Alt.4 | 159.22 | 39.3757 | -81.27855 | 39.377575 | -81.280039 | 39.379392 | -81.281467

## Slide 20: 5) Mile Point 207.90
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
5 | 207.90 | 39.075631 | -81.780783 | 39.077333 | -81.780783 | 39.078981 | -81.780803

## Slide 21: 6) Mile point 256.95
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
6 | 256.95 | 38.951144 | -82.100194 | 38.952019 | -82.102031 | 38.952822 | -82.103728
Alt.6 | 257.60 | 38.943867 | -82.103581 | 38.944531 | -82.106594 | 38.945133 | -82.109614

## Slide 22: 7) Mile Point 306.00
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
7 | 306.00 | 38.435886 | -82.404478 | 38.4382 | -82.404522 | 38.440711 | -82.404594

## Slide 23: 8) Mile point 355.05
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
8 | 355.05 | 38.724172 | -82.988264 | 38.725794 | -82.987878 | 38.727403 | -82.987489

## Slide 24: 9) Mile Point 404.10
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
9 | 404.10 | 38.628406 | -83.686358 | 38.629953 | -83.685606 | 38.631544 | -83.684844
Alt.9 | 404.71 | 38.631997 | -83.697056 | 38.633753 | -83.695864 | 38.635556 | -83.69465

## Slide 25: 10) Mile point 453.15
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
10 | 453.15 | 38.993714 | -84.305828 | 38.994547 | -84.3027 | 38.995397 | -84.299519

## Slide 26: 11) Mile point 502.20
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
11 | 502.20 | 38.993969 | -84.835522 | 38.992347 | -84.838211 | 38.990719 | -84.840897
Alt.11 | 502.25 | 38.993358 | -84.835086 | 38.991792 | -84.837647 | 38.99015 | -84.840303

## Slide 27: 12) Mile point 551.25
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
12 | 551.25 | 38.733742 | -85.262956 | 38.736139 | -85.261681 | 38.738528 | -85.260425

## Slide 28: 13) Mile point 600.30
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
13 | 600.30 | 38.283217 | -85.697536 | 38.285414 | -85.6993 | 38.287631 | -85.701094
Alt.13 | 600.48 | 38.281828 | -85.700256 | 38.284083 | -85.702078 | 38.286422 | -85.703972

## Slide 29: 14) Mile point 649.35
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
14 | 649.35 | 38.026233 | -86.223811 | 38.028136 | -86.221511 | 38.030067 | -86.219183

## Slide 30: 15) Mile point 698.40
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
15 | 698.40 | 37.945508 | -86.505769 | 37.944417 | -86.508119 | 37.943331 | -86.510464

## Slide 31: 16) Mile point 747.45
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
16 | 747.45 | 37.881214 | -87.037739 | 37.880942 | -87.040939 | 37.880661 | -87.044167

## Slide 32: 17) Mile point 796.50
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
17 | 796.50 | 37.9304 | -87.614083 | 37.932656 | -87.618878 | 37.934892 | -87.623686

## Slide 33: 18) Mile point 845.55
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
18 | 845.55 | 37.786097 | -87.987147 | 37.789386 | -87.98625 | 37.792667 | -87.985344
Alt.18 | 845.31 | 37.785511 | -87.983486 | 37.788361 | -87.982083 | 37.791364 | -87.980628

## Slide 34: 19) Mile point 894.60
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
19 | 894.60 | 37.4087 | -88.382033 | 37.409914 | -88.380736 | 37.411328 | -88.379225

## Slide 35: 20) Mile point 943.65
I.D. | Ohio River Mile Point | Left Descending Bank Y | Left Descending Bank X | Mid-Point Y | Mid-Point X | Right Descending Bank Y | Right Descending Bank X
20 | 943.65 | 37.138442 | -88.737292 | 37.141464 | -88.735167 | 37.144553 | -88.732992
Alt.20 | 944.23 | 37.142006 | -88.746867 | 37.145586 | -88.74435 | 37.149206 | -88.741772
Revised Alt. 20 | 943.9 | 37.139739 | -88.741142 | 37.142917 | -88.739022 | 37.14625 | -88.736806

## Slide 36: Status
We have been communicating with USGS on EDI method.
QAPP has been developed to the extent possible. Sample collection and handling methods based on Michigan.
Meeting scheduled with EPA Cincinnati regarding analytical services.
20 sites have been selected and sent to states to check alignment with regulatory mixing zones.

## Slide 37: Site Selection to Bracket Parkersburg Area
Two additional sites are to be selected to bracket the Parkersburg area.
Consider all existing data.
Initially confer with OEPA & WVDEP, then bring to PFAS workgroup, and TEC in February.

## Slide 41: Remaining Tasks
Secure analytical services.
Confirm use of USGS EDI sampling method for PFAS and obtain any needed alternative equipment.
Select 2 sites to bracket Parkersburg area of Ohio River.
Finalize QAPP, Sampling Plan, and Communication Plan.
Confirmation that sites are not within a regulatory mixing zone.