## Slide 1: 2019 Monitoring Activities: Summer Water Quality Conditions
Technical Committee Meeting
October 8-9, 2019
Agenda Item #7

## Slide 2: 2019 Sampling Sites

## Slide 3
May
June
July
August
September
2019 Precipitation

## Slide 4
Average Monthly Streamflow May – September 2019
Chart: Pittsburgh (ORM 13)
| May | June | July | Aug | Sept
Observed | 51.592 | 55.0625 | 33.5462 | 11.4346 | 11.0208
Long-Term | 37.9 | 25.6 | 17.8 | 14.5 | 13.8
Chart: Cincinnati (ORM 471)
| May | June | July | Aug | Sept
Observed | 148.22 | 174.8333 | 96.2615 | 37.7346 | 25.6833
Long-Term | 120.2 | 72.1 | 48.1 | 40.2 | 34.8
Chart: Evansville (ORM 791)
| May | June | July | Aug | Sept
Observed | 195.684 | 254.4 | 125.9038 | 40.7692 | 28.0125
Long-Term | 180.4 | 118.8 | 74.4 | 61 | 54.1

## Slide 5: Bacteria Sampling

## Slide 6: Bacteria Monitoring
April thru October
5 rounds monthly
Analyzed for E. coli.
Criteria:
  GeoMean: 130 CFU/100mL
  Single Sample: 240 CFU/100mL
Percent Exceeded April-September 2019 | Pittsburgh* | Wheeling | Huntington | Cincinnati | Louisville | Evansville
Monthly Geometric Mean | NA * | 67% | 67% | 50% | 67% | 50%
Single Sample | 35% | 37% | 33% | 30% | 33% | 27%
*Less than 5 samples were collected due to weather/equipment issues-no
Geometric Mean was calculated for those months.

## Slide 7: Bacteria Monitoring
In Cincinnati we also analyze for E.coli/Total Coliform using Colilert at three cross-sections (nine sites) weekly.
Special Events
1. Paddlefest
2. The Great Ohio River Swim
* Cancelled due to HAB

## Slide 8
D.O. and Temperature Monitoring

## Slide 9: Dissolved Oxygen and Temperature Monitoring
Dissolved Oxygen
Monitored by the Army Corp of Engineers, electric utility/hydropower agencies and ORSANCO for the assessment of aquatic life use.
Markland had multiple days that fell below 5.0 mg/L.
Smithland had one day that fell below 5.0mg/L.
Temperature
The allowable temperature varies each month and ranges from 71°-89°F.
Temperatures did not exceeded the criteria at Montgomery and Markland.
Smithland had four days in the end of June that exceeded the criteria.

## Slide 10
Chart: Montgomery (RMI 31.7) Dissolved Oxygen
Chart: Markland (RMI 531.5) Dissolved Oxygen
Chart: Smithland (RMI 919) Dissolved Oxygen

## Slide 11
Chart: Montgomery (RMI 31.7) Temperature
Chart: Markland (RMI 531.5) Temperature
Chart: Smithland (RMI 919) Temperature

## Slide 12
Clean Metals and Bimonthly Sampling

## Slide 13: Metals and Bimonthly Parameters
Metals
Mercury
Aluminum
Chromium
Manganese
Nickel
Copper
Zinc
Arsenic
Selenium
Silver
Cadmium
Antimony
Thallium
Lead
Magnesium
Calcium
Iron
Barium
Nutrients, Major Ions
Ammonia Nitrogen
Bromide
Chloride
Hardness
Nitrate-Nitrite Nitrogen
Phenols
Sulfate
Total Dissolved Solids
Total Kjeldahl Nitrogen
Total Organic Carbon
Total Phosphorus
Total Suspended Solids
Cyanide

## Slide 14
Hg criteria: >12ng/L
WV Fe criteria: >1,500 µg/L
KY Fe criteria: >3,500 µg/L

## Slide 15
15 random 500m sites per pool
  Fish Community
  Macroinvertebrate Community
  Submerged Aquatic Vegetation
  Paired Water Quality
  Continuous DO & Temp logger
  Nutrients & Chlorophyll a
  Instream & Riparian Habitat
R.C. Byrd
Smithland
Notes: Emsworth, pike island, meldahl, newburgh