## Slide 1: Characterization of Dissolved Solids in the Ohio River
TECHNICAL COMMITTEE MEETING
FEBRUARY 12-13, 2013

## Slide 2: Study Objectives
Characterize ambient background levels of TDS
Develop site-specific translators to convert conductivity to TDS
Quantify TDS constituent makeup to evaluate seasonal and spatial variability
Provide data to support possible development of an Ohio River bromide stream criterion

## Slide 3: Sampling Design
Weekly samples collected at 16 sites
Collection sites located at water intakes
  Participants identified through the WUAC and PIAC
Sampling conducted for 1-year
  December, 2011 thru December 2012
Analysis – In-house and contract lab

## Slide 5: Analysis
Dissolved Solids Analytes
Sodium
Potassium
Magnesium
Calcium
Lithium
Bicarbonate
Total Dissolved Solids
Supplemental Parameters
pH
Conductivity
Temperature
Stream flow
Coordinate THM sampling when possible
Chloride
Sulfate
Bromide
Fluoride

## Slide 6: TDS Results Summary
ORSANCO Total Dissolved Solids Results Summary December 2011 - December 2012 |  |  |  |  | 
 |  |  | TDS Result, mg/L |  | 
River | Mile | Ohio River | Min | Median | Max
Allegheny | 8.2 | 0 | 62 | 161.5 | 236
Monongahela | 4.5 | 0 | 113 | 218.0 | 362
Ohio | 11.7 | 11.7 | 124 | 205.0 | 280
Beaver | 6 | 25 | 163 | 276.0 | 386
Ohio | 65.3 | 65.3 | 104 | 206.0 | 307
Ohio | 86.8 | 86.8 | 106 | 217.0 | 328
Ohio | 137.2 | 137.2 | 110 | 222.0 | 359
Muskingum | 29 | 172 | 148 | 362.0 | 584
Ohio | 190.5 | 190.5 | 106 | 227.0 | 364
Ohio | 260 | 260 | 160 | 222.0 | 368
Ohio | 306 | 306 | 126 | 188.5 | 301
Big Sandy | 23.6 | 317.1 | 155 | 362.0 | 579
Ohio | 462.8 | 462.8 | 150 | 195.0 | 335
Ohio | 600 | 600 | 166 | 215.0 | 332
Ohio | 791.5 | 791.5 | 160 | 223.0 | 341
Ohio | 978 | 978 | 142 | 203.0 | 339
Ohio River
Ranged from 104 to 368 mg/L
Median conc ~190 to 230 mg/L
Tributaries
Ranged from 62 to 584 mg/L
Median conc ~160 to 360 mg/L

## Slide 7: TDS by Location All Sites
TDS Standard
=
500 mg/L

## Slide 8: Flow vs TDS (ORM 12)

## Slide 9: Flow vs TDS (MU029)

## Slide 10
TDS by Date
TDS Standard
=
500 mg/L

## Slide 11: Bromide Results Summary
ORSANCO Bromide Results Summary |  |  |  |  |  |  | 
 |  |  | Bromide Result, mg/L |  |  |  | 
River | Mile | Ohio River | Min | Median | Max | % Detects Week 1-12 RL 100 ppb | % Detects Week 13-48 RL 35 ppb
Allegheny | 8.2 | 0 | < 0.035 | 0.1053 | 0.8998 | 7.69 | 94.12
Monongahela | 4.5 | 0 | < 0.035 | 0.0812 | 0.8752 | 0.00 | 77.14
Ohio | 11.7 | 11.7 | < 0.035 | 0.0999 | 1.1721 | 15.38 | 88.57
Beaver | 6 | 25 | < 0.035 | 0.0364 | 0.2233 | 14.29 | 90.63
Ohio | 65.3 | 65.3 | < 0.035 | 0.1040 | 0.5053 | 7.14 | 88.57
Ohio | 86.8 | 86.8 | < 0.035 | 0.1036 | 0.415 | 7.69 | 88.24
Ohio | 137.2 | 137.2 | < 0.035 | 0.1252 | 0.2899 | 10.00 | 82.35
Muskingum | 29 | 172 | < 0.035 | 0.0875 | 0.8151 | 0.00 | 91.43
Ohio | 190.5 | 190.5 | < 0.035 | 0.1051 | 0.7426 | 0.00 | 80.00
Ohio | 260 | 260 | < 0.035 | 0.0975 | 0.5862 | 0.00 | 91.18
Ohio | 306 | 306 | < 0.035 | 0.0821 | 0.7916 | 0.00 | 82.14
Big Sandy | 23.6 | 317.1 | < 0.035 | 0.0718 | 1.1245 | 7.69 | 74.29
Ohio | 462.8 | 462.8 | < 0.035 | 0.0999 | 0.292 | 15.38 | 81.08
Ohio | 600 | 600 | < 0.035 | 0.0784 | 0.7631 | 0.00 | 69.70
Ohio | 791.5 | 791.5 | < 0.035 | 0.0867 | 0.2171 | 0.00 | 65.71
Ohio | 978 | 978 | < 0.035 | 0.0756 | 0.3824 | 15.38 | 54.84
Ohio River
Ranged from <0.035 to 1.17 mg/L
Median conc 0.076 to 0.125 mg/L
Tributaries
Ranged from <0.035 to 1.12 mg/L
Median conc 0.036 to 0.105 mg/L

## Slide 12: Bromide by Location

## Slide 13: Bromide by Location

## Slide 14: Bromide by Date

## Slide 15
Notes: Other = Fl-, NO2, Br-, NO3, PO4, Li, NH3, K+, Mg
<number>

## Slide 16: Data Assessment
Data assessment ongoing
Compare TDS results to 500 mg/L standard
  Levels did not approach standard on the Ohio River
  6 samples from Muskingum and Big Sandy >500 mg/L
Evaluate spatial and seasonal trends
  Concentrations are inversely correlated with stream flow
  Tributaries exhibited higher and more variable levels of TDS; lower and less variable bromide levels
Develop site specific relationship between TDS and conductivity
  Not yet assessed
Evaluate relationship between bromide in source water and THMs in finished water
  Not yet assessed; Compiling THM data from water utilities
Report to be completed mid 2013.

## Slide 17: Questions ?