## Slide 1
Technical Committee Meeting
February 12-14, 2013
Agenda Item # 15

## Slide 2: Policy on Dissolved Oxygen Monitoring Requirements For Ohio River Hydroelectric Power Generating Facilities
Background
  Adopted by the Commission at its 131st meeting on May 26, 1988 at Louisville, Kentucky.
  The Commission’s primary concern with hydropower development was the potential impact on dissolved oxygen (DO) concentrations.
  In 1987, the Federal Energy Regulatory Commission (FERC) issued an environmental impact study of hydropower development on the lower Allegheny and upper Ohio Rivers. Among the study findings was that some dams were “good aerators” and some were not. For the “good aerator” dams, it was proposed that FERC licenses require maintenance of a 6.5 mg/L DO level while a 5.0 mg/L level (the water quality standard for the main stem states) was recommended for the “poor aerators”.
  A hydro facility does not lower the DO level directly; rather it prevents the river from receiving an input of oxygen. It is that oxygen input that needs to be preserved at critical periods (i.e., low flow, high temperature periods when DO is typically lowest). The Technical Committee therefore recommended, and the Commission adopted, a policy based on the protection of the aeration capability of each dam.

## Slide 3: Policy on Dissolved Oxygen Monitoring Requirements For Ohio River Hydroelectric Power Generating Facilities, Cont’
Policy
  Operating licenses for Ohio River hydropower facilities should contain provisions to assure that:
    Adequate studies are conducted prior to facility operation to define aeration characteristics of the dam.
    Continuous monitoring of dissolved oxygen is provided at representative locations above and below the facility as appropriate, with data available to ORSANCO through remote interrogations.
    Provisions are made in the facility design and operation to allow maintenance of the full aeration potential of the dam during critical conditions.
Specific application of this policy shall be on a case-by-case basis.

## Slide 5: Hydropower Highlights
Application Filed with FERC
  Newburgh
  Uniontown
Under Construction
  Willow Island
  Meldahl
  Smithland
Surrendered its License
  New Cumberland
  Pike Island

## Slide 6: Hydropower Highlights, Cont
Active Hydros
  New Martinsville
  Belleville
  Racine
  Greenup
  Markland
  Ohio Falls
  Cannelton

## Slide 7: Hydropower D.O. Data
Current Data Collection:
  Hannibal and Greenup via dial-up modem
  Racine and Markland real time
  Ohio Falls weekly from Louisville Gas & Electric
  John T. Myers (Uniontown) and Smithland via ORSANCO
  Belleville annual report
  ORSANCO does not receive data from Willow Island, Meldahl, Cannelton, or Newburgh at this time.
The U.S. Army Corps of Engineers has asked the districts to revise existing MOAs (memorandum of understanding) such that hydro operators will be required to collect temperature and D.O. data in real time and make the data available via the web between May 1 and Oct 31.