## Slide 1
Status of the Organics Detection System Upgrade
ODS Network and Website
CMS 5000 Process GC/ Purge and Trap

## Slide 2
The ODS website displays the current status of each of the sites
Green dots indicate that data is successfully being uploaded to the secure website
By selecting the sites you can view recent VOC data for that site

## Slide 3
Daily organics detection system data is available remotely using a password protected website
Volatile organic carbon data from ODS sites is displayed automatically and updated as new data is available

## Slide 4: ODS Network Progress to Date
All ODS Sites have been networked
ORSANCO staff can access all of the ODS sites remotely to troubleshoot, review chromatography data and provide training
The Sites with CMS have been setup to log data to the ODS Website
Moving Forward
The reports generated by the Thermo GC/MS will be set up to export to the ODS website
Compound Names will be standardized
Reports on the website will include unknown compound detections

## Slide 5
The CMS 5000 Process GC/ Purge and Trap
CMS 5000s are currently in use at Midland, Ashland and Cincinnati Water Works
An additional CMS is scheduled to be installed at Wheeling Water
The CMS 5000 monitors VOCs at user defined intervals allowing for around the clock operation
Unlike previous process VOC instrumentation, the CMS 5000 uses large diameter fittings and is perfectly suited for the demands of real time monitoring of Ohio River water

## Slide 6
Total Number of Ohio River Water samples analyzed for 2013: 4589
For Upgraded ODS sites
Total Number of Ohio River Water samples
analyzed by ODS sites that have been upgraded: 1821
Number of volatile organic compound detections
over 2ppb: 32
For the upgraded ODS sites detections over 2 parts per billion occurred in less than 2% of Ohio River water samples.
Of the volatile organics detected the trihalomethanes were by far the most common.

## Slide 7
ODS Detections 2012