## Slide 1: FGD MONITORING PROJECT
ORSANCO Technical Committee Meeting June 4, 2013
Item 8a

## Slide 2: FGD Monitoring Sampling Plan
Four sample events (quarterly) at four coal-fired power generation facilities
Analytical parameters:
Filtered total Hg Unfiltered total Hg Filtered methyl Hg Unfiltered methyl Hg Selenium | Bromide Dissolved Organic Carbon Dissolved Sulfate Chlorophyll pH/Specific Conductance

## Slide 3: FGD Monitoring Results by Sample Site
Raw Water Intake
Chloride Purge Stream Internal Outfalls
Final Effluent

## Slide 6: “THERE IS NO TYPICAL FLUE GAS DESULFURIZATION SYSTEM” - NORTH AMERICAN ELECTRIC RELIABILITY COUNCIL , 1991
“…mercury behavior is difficult to estimate … it is recommended to measure mercury in all cases and not rely simply on engineering estimates.”
-Siemens Environmental Systems 2009

## Slide 7: Ohio River Scrubbed Generating Capacity

## Slide 8: Ohio River Scrubbed Generating Capacity

## Slide 9: Plant 1
Original online year 1967, 1977
Total Generating capacity 1800 MW (3 Units)
Scrubbers online 2007, 2008, 2010 (Limestone Jet Bubbling no byproduct recovery)
FGD Chloride Purge Stream discharge 0.32 MGD, mixed with 1,144 MGD cooling water prior to discharge
All coal used is North Appalachian (higher S, Hg)
Notes: <number>

## Slide 10: Plant 2
Original online year 1971
Total Generating capacity 1560 MW (2 Units)
Scrubbers online 2007 (Limestone Tray Type with gypsum recovery)
FGD Chloride Purge Stream to clear pond discharged with 5.79 MGD non-cooling water.
Coal used is a mix of Northern Appalachian (Higher S, Hg) and Central Appalachian (Lower S, Hg)
Notes: <number>

## Slide 11: Plant 3
Original online year 1980
Total Generating capacity 1300 MW (1 Unit)
Scrubber online 2007 (Limestone Spray Type no byproduct recovery)
FGD Chloride Purge Stream 0.48 MGD, Treated in bioreactors and mixed with 4.31 MGD other non-cooling water from reclaim pond prior to discharge
All coal used is Appalachian (not specified N or S but reported lower sulfur content than others)
Notes: <number>

## Slide 12: Plant 4
Original online year 1955
Total Generating capacity 1200 MW (6 Units)
Scrubbers online May 2013 (Limestone Jet Bubbling with gypsum recovery)
FGD Chloride Purge Stream will go to Bottom Ash pond with 20.5 MGD non-cooling waters
Coal used is 25% Western PRB (lower S, Hg), 75% Eastern/Cumberland (lower S, Hg). Will switch to 100% Illinois Basin (higher S, lower Hg) when current stock is gone
Notes: <number>

## Slide 13: FGD Wastewater Treatments

## Slide 14: Final Effluent

## Slide 15: Methyl Mercury in Final Discharge

## Slide 16: Seasonal Differences

## Slide 17: Conclusions
No potential violations of 12ng/L total mercury in final effluent were observed
Methyl mercury concentrations consistent across raw intake, CPS, and Final Effluent
Bioreactor treatment is effective for mercury, selenium, and bromide
Study average mass discharge:
  CPS contain ~0.30g/day total mercury
  Final Effluents contain ~0.05g/day total mercury
    Results indicate internal discharge to ash ponds/clear water ponds captures 85% of mercury