## Slide 1: Fish Otolith Ablation: A New Technique for Evaluating Lifetime Exposure to Mercury
Rob Reash
American Electric Power, Columbus, Ohio

## Slide 2: Issues re: Hg in Ohio River fish
Is fish consumption use impaired?
Are levels increasing for any species?
What are the primary point-source and non-point sources?
What is the extent of in situ methylation?

## Slide 3: What tools are being implemented?
Long-term monitoring of THg (and, recently, MeHg) in several fish species.
Monitoring of THg and MeHg in ambient water.
Implementation of adopted MeHg human health criterion re: use attainment.

## Slide 4: Fish fillet analyses - limitations
It is a snapshot ; year-to-year variation in Hg exposure is unknown.
Analysis of composite samples masks exposure patterns of individual fish.
Selecting largest, oldest fish for fish consumption use attainment may bias potential risk.

## Slide 5: Otolith laser ablation: the concept
Trace elements deposit onto otoliths (ear bones) based on timing and magnitude of exposure.
Levels of trace elements are quantified directly from fish “birth” to time of collection using ICP-MS.
Technique first used at Canadian mining sites where regulators were concerned of salmonid exposure to Se-enriched wastewater.

## Slide 6: Preliminary evaluation – Ohio River freshwater drum
AEP/EPRI study (2010) documented levels of THg, MeHg, and Se in five fish species collected near coal power plants.
All fish aged using scale, spine, or otoliths.
Otoliths from six freshwater drum analyzed for THg and Se (cannot speciate metals).

## Slide 7: Range of measured THg, MeHg, and Se in fillet samples
THg: 0.117 – 0.419 mg/kg wet wt. MeHg: 0.072 – 0.368 mg/kg wet wt. Se: 1.67 – 4.84 mg/kg dry wt.

## Slide 8
Distance (micrometers)
Low fillet MeHg: Age = 4+

## Slide 9
Distance (micrometers)
Medium fillet MeHg; Age = 17+

## Slide 10
Distance (micrometers)
High fillet MeHg;
Age = 21+

## Slide 11
Distance (micrometers)
High fillet MeHg;
Age = 21+

## Slide 12: Preliminary observations based on small sample size
Exposure patterns differ for each fish….such information cannot be inferred by tissue analysis.
The relationship between tissue MeHg and recent (last 12 month) otolith Hg concentration is difficult to discern….need larger sample sizes.
Need to understand the importance of moving average vs. peak vs. upper percentile concentration re: best predictor of otolith [Hg].

## Slide 13: My contact
Rob Reash Principal Environmental Scientist Certified Fisheries Scientist American Electric Power 1 Riverside Plaza Columbus, OH 43215 P: 614-716-1237 rjreash@aep.com