## Slide 1: Characterization of Dissolved Solids in the Ohio River
TECHNICAL COMMITTEE MEETING
JUNE 4-5, 2013

## Slide 2: Background
Commission adopted 500 mg/L standard for TDS in June 2011
Rivers Users Program developed study to investigate TDS and major ions
Water Users simultaneously proposed similar study for bromide
Integrated the two study plans for cost efficiencies and more robust data set

## Slide 3: Study Objectives
Characterize ambient background levels of TDS
Quantify TDS constituent makeup to evaluate seasonal and spatial variability
Develop site-specific translators to convert conductivity to TDS
Provide data to support possible development of an Ohio River bromide stream criterion

## Slide 4: Sampling Design
Weekly samples collected at 16 sites
Collection sites located at water intakes
  Participants identified through the WUAC and PIAC
Sampling conducted for 1-year
  December, 2011 thru December 2012
Analysis – In-house and contract lab

## Slide 6: Analysis
Dissolved Solids Analytes
Sodium
Potassium
Magnesium
Calcium
Lithium
Bicarbonate
Total Dissolved Solids
Supplemental Parameters
pH
Conductivity
Temperature
Stream flow
Chloride
Sulfate
Bromide
Fluoride

## Slide 7: What do the results tell us about ambient levels of TDS?
Peak concentration in Ohio River was 368 mg/L
Median level ~200 mg/L
Highest levels on Muskingum and Big Sandy Rivers
  584 mg/L and 579 mg/L respectively
Lowest levels on Allegheny R.

## Slide 8: Are there seasonal variations?
Highest concentrations observed in late Aug./early Sept.
Stream flow is major driver of seasonal variation
Concentrations of TDS and most ions are inversely correlated with Q
All Ohio River samples well below 500 mg/L std., even during low flow conditions

## Slide 9: What are the major ions?
5 ions makeup 93% of TDS in Ohio River
  Sulfate, bicarbonate, calcium, chloride, sodium
Bromide is typically <0.05%
Sulfate and chloride combined account for 43% of TDS

## Slide 10: How does ionic composition vary spatially?
SO4 decreases from upstream to down
  36% at mile 12 to 21% at mile 978
  Beaver R. 19%; Big Sandy 42%
HCO3 doubles from 19% in Pittsburgh to 38% in Cairo
Calcium remains fairly consistent (13-16%)
Cl- shows general decline from 14.5% at mile 137 to 8.8% at mile 792
  Big Sandy 4%; Beaver R. 19%
Sodium decreases moving downstream
  11% in Pittsburgh to 7% in Cairo
Bromide generally highest in upper river

## Slide 11
Notes: Other = Fl-, NO2, Br-, NO3, PO4, Li, NH3, K+, Mg
<number>

## Slide 13: What is the relationship of TDS and conductivity in the Ohio River?
Conductivity sometimes used as surrogate for TDS
0.67 is commonly used to convert conductivity to TDS
Reported conversion factors range from 0.5 to nearly 1
  Conv. factor depends on ionic composition
Compared TDS to specific conductance
Ohio River conversion factors ranged from 0.55 to 0.58
Could overestimate TDS by 20% using 0.67 conv. factor.

## Slide 14: Still to Come
Address Study Objective #4: Evaluate relationship between bromide in source water to THM formation in finished drinking water
Solicit comments on draft report from Technical Committee, River Users, Water Users, others(?).
Final draft to be distributed with agenda for approval at October meeting

## Slide 15: Questions ?