## Slide 1: Biennial Assessment of Ohio River Water Quality Conditions
305(B) REPORT TO CONGRESS
2014

## Slide 2: Determining Impairment for Mercury in Fish Tissue
During the 2012 305(b) Assessment, TEC directed staff to:
  Utilize USEPA’s assessment methodology
  Designate the Ohio River “unassessed” for mercury in fish tissue due to a lack of TL2 and TL3 fish tissue data.
  Collect additional fish tissue data to fill in missing data.
  Consider utilization of outside data.

## Slide 3: USEPA’s Methodology
Basic concept is to generate an “average” concentration across the representative species and trophic levels consumed for comparison against the criterion for MeHg = 0.3 mg/Kg.
National default consumption rate for freshwater & estuarine fish is 17.5 grams/day:
    3.8 g/d TL2 + 8.0 g/d TL3 + 5.7 g/d TL4 = 17.5 g/d
  The criterion was developed incorporating these consumption values.

## Slide 4: Methodology for Averaging
Cavg = 3.8*CTL2 + 8.0*CTL3 + 5.7*CTL4
17.5 g/d
Take geometric mean of each species in a trophic level, then take a weighted arithmetic average of the geometric means; weighted by the number of samples in each species.
Bottom line effect is that species having more samples get a greater “weighting” or influencing in the averaging methodology.
This is basic concern with accepting outside data.

## Slide 5: Effect due to Sample Size
Species | Trophic Level | No. Samples | Geometric Mean, mg/Kg
White Crappie | 3 | 5 | 0.35
Bluegill | 3 | 20 | 0.25
Blue Catfish | 3 | 5 | 0.30
Smallmouth Buffalo | 2 | 5 | 0.30
Striped Bass | 4 | 5 | 0.30
CTL3 = 5*0.35 + 20*0.25 + 5*0.30 = 0.275 mg/Kg
30
Cavg = 3.8*CTL2 + 8*CTL3 + 5.7*CTL4
17.5 g/d
Cavg = 3.8*0.3 + 8*0.25 + 5.7*0.3 = 0.28
17.5

## Slide 6: Problems with Methodology
ORSANCO not in agreement with EPA-defined trophic levels.
Not many commonly consumed Trophic level 2 for Ohio River.
Weighting the averages by number of samples creates situation where numbers of samples collected for a particular species could affect the outcome of the assessment.
Herein the concern with accepting outside data.

## Slide 7: Possible Solutions
Define the species in each of the trophic levels that are commonly consumed for the Ohio River.
Give equal weighting to each species in a trophic level regardless of number of samples for each species.
Develop better information on commonly consumed species and size classes.
Develop guidance on use of size classes.

## Slide 8: Proceed with Recommendations?