## Slide 1
IOWA NUTRIENT REDUCTION STRATEGY
A science and technology-based framework to assess and reduce nutrients to Iowa waters and the Gulf of Mexico
James Gillespie
June 5, 2013
<number>
Notes: <number>

## Slide 2: Need for Iowa Strategy
Required by 2013 under Gulf hypoxia action plan and by EPA
Encourage progress and provide proactive “roadmap” to achieve technically possible and economically feasible change
Understand how to maximize nutrient reduction per dollar spent
Establish science and economic feasibility limitations to guide realistic expectations
Notes: WQ standards will call for large nutrient reductions to meet goals
Will need strategy that encompasses actions needed with tools that work
<number>

## Slide 3: Goal – Iowa Leader
“As Iowa is a national and global leader in the production of food and renewable fuels, a goal of this strategy is to make Iowa an equal national and global leader in addressing the environmental and conservation needs associated with food and renewable fuels production.”
<number>

## Slide 4: What’s New?
Nonpoint and point sources integrated plan & working together towards goal
Nonpoint source science assessment
Harness the collective initiative of Iowa ag organizations, ag business & farmers
Major cities and industries treat to remove nutrients
Coordination through Water Resources Coordinating Council (WRCC)
<number>

## Slide 5: Science Assessment Summary
Process has identified practices that have greatest potential for nutrient load reduction
Process has estimated potential field-level costs associated with practice implementation and is also considering larger-scale economic impacts of practice implementation
To achieve goals will require a combination of practices
N versus P requires different practices
Multiple benefits of practices will need to be considered
Knowing the starting point is still a challenge and knowing what is being done on the land could (would) improve estimates of progress that can be made
<number>
Notes: <number>

## Slide 6: Nitrogen Reduction Practices
 | Practice | % Nitrate-N Reduction [Average (Std. Dev.)]
Nitrogen Management | Timing (Fall to spring) | 6 (25)
 | Source (Liquid swine compared to commercial) | 4 (11)
 | Nitrogen Application Rate | Depends on starting point
 | Nitrification Inhibitor | 9 (19)
 | Cover Crops (Rye) | 31 (29)
Land Use | Perennial – Land retirement | 85 (9)
 | Living Mulches | 41 (16)
 | Extended Rotations | 42 (12)
Edge-of-Field | Drainage Water Mgmt. | 33 (32)*
 | Shallow Drainage | 32 (15)*
 | Wetlands | 52
 | Bioreactors | 43 (21)
 | Buffers | 91 (20)**
Notes: In-field practices are annual management practices. Rate, source and time of application have small average reduction and wide variability of effectiveness. N inhibitor is compared to applying N when soils are 50 degrees and cooling. Rye cover crop was used because of availability of research data.
Edge-of-field technologies have large upfront costs and relatively low annual costs. Higher and more predictable effectiveness. Large buffer number applies to the water that intersects the root zone of the buffer.
*Load reduction not concentration reduction
**Concentration reduction of that water interacts with active zone below the buffer
Land-use changes reduce N loss because N is not added and is taken up by plants. Capturing income on these areas is difficult.
In general:
  Practice reductions not necessarily additive. For example, cover crop reduces N 31% before water gets to wetland which reduces the remaining N another 52%.
  Other than cover crops, the average N reduction is relatively small and variability is wide. Biological systems are complex with lots of variables.
  Taking land out of crops does not prevent N loss. Iowa soils are highly organic and release N with water movement.
<number>

## Slide 7: Phosphorus Reduction Practices
 | Practice | % Phosphorus-P Reduction [Average (Std. Dev.)]
Phosphorus Management | Producer does not apply phosphorus until STP drops to optimal level | 17 (40)
 | Source (Liquid swine compared to commercial) | 46 (45)
 | Incorporation | 36 (27)
 | No-till (70% residue) vs. conventional tillage (30% residue) | 90 (17)
 | Cover Crops (Rye) | 29 (37)
Land Use | Perennial – Land retirement | 75 (-)
 | Pasture | 59 (42)
Edge-of-Field | Buffers | 58 (32)
Phosphorus assessment does not include stream bed and bank contribution
Notes: In-field: No P applied to soil with high or very high soil test P (STP) levels. Switching from conventional to conservation tillage or to no-till. Cover crops reduce erosion.
Edge-of-field: buffers along streams.
Land-use changes reduce P loss through reduced erosion. Capturing income on these areas is difficult.
In general:
  Easier to achieve P goal than N goal.
  Higher average reductions, but still wide standard deviation.
<number>

## Slide 8: Nonpoint Source Actions
Watershed prioritization & goals
Setting priorities
Research & technology
Strengthen outreach, education, collaboration
Increased public awareness & recognition
Funding
Accountability & verification measures
Public reporting
<number>

## Slide 9: Why is Strategy Important?
Based on sound science in Iowa, for Iowa
Meaningful and measureable progress
Builds on current programs and targeted watersheds
Utilizes the policy framework which will provide greatest progress and success
Improves water quality in Iowa and Gulf of Mexico
<number>

## Slide 10: Strategy Future Actions
The strategy sets forth concepts, from which operational plans will be developed in the future
The strategy is a dynamic document that will change over time as new information, data and science is discovered and adopted
<number>
Notes: <number>

## Slide 11: For More Information
www.nutrientstrategy.iastate.edu
<number>