## Slide 1
Notes: <number>

## Slide 2: Iowa Nutrient Reduction Strategy: Point Source Reductions
Excerpts from a presentation prepared by
Adam Schnieders,
NPDES Program Supervisor,
Iowa Department of Natural Resources
April 2013

## Slide 3: PS and NPS Common Threads
  Acknowledgement of the problem
  Recognition that traditional approaches are not workable (e.g. cost, technically)
  Willingness to want to do something now to make progress
  Needs to be practical in its implementation

## Slide 4: Iowa Strategy General Approach
Achieve nutrient load reductions through technology-based actions, while
2) Continuing to assess and evaluate nutrient water quality standards

## Slide 5: Point Source Strategy
In Iowa point sources contribute 8% of the TN and 20% of the TP
Point sources can have greater impacts at low flows and certain watersheds
Similar to Kansas approach
Working closely with CWA regulated community
Use existing rules (Chapter 567 IAC Chapter 62)
Use technology-based limits in lieu of nutrient criteria
  Limits based on the effect of the pollutant in the water and feasibility and reasonableness of treating such pollutant

## Slide 6: Point Source Strategy
  Focus on:
  102 major municipal wastewater treatment plants
  28 major industries (10 of which have nutrients)
  18 minor industries with biological treatment for process waste
  Total of 148 (130 expected to have sig. nutrient loads)
  Treat more than 1 million gallons of wastewater a day
  Handle 80 percent of all municipal wastewater
  Provide wastewater treatment for 55-60 percent of Iowa’s population

## Slide 7: Strategy vs. Numeric Criteria Permit Limits
Nutrients | Typical Effluent Concentration without nutrient removal (mg/L) | Numeric Nutrient Criteria (WQ-based) (mg/l) | Limit of Technology (WQ-based) (mg/l) | Strategy Tech-Based Limits (mg/L)
Total Phosphorus (TP) | 4.0 | 0.1 | 0.1 to 0.3 | 1.0
Total Nitrogen (TN) | 25.0 | 0.5 to 3.0 | 3.0 | 10.0

## Slide 8: Results
At the 130 wastewater treatment plants included in the strategy:
Assume 25 mg/L total nitrogen (TN) and 4 mg/L total phosphorus (TP) discharge concentrations
Use annual average flows
Use Biological Nutrient Removal technology limits (10 mg/L TN and 1 mg/L TP)
Currently Point Source Facility Loading
18,300 tons/yr TN
2,900 tons/yr TP
After implementation
7,300 tons/yr TN
730 tons/yr TP
2/3 to 3/4 reduction possible

## Slide 9: Results
At the watershed level
Using GIS (Geographic Information System) with ambient data (132 samples from 58 sites over 11-year period) – aka - the 2012 Nutrient Budget
Point Source State-wide Loading Currently
~ 8 percent TN
~ 20 percent TP
State-wide Load Reduction after Implementation
~ 4 percent overall TN load reduction
~ 16 percent overall TP load reduction

## Slide 10: Implementation Details
Submit feasibility and planning study within two years
DNR reviews study
Negotiate Construction schedule
Amend permit to incorporate the schedule
Limits incorporated in permit following one year performance evaluation
Benefits
  Regulatory certainty – 10 year assurance
  Economic Considerations
  Ability to fine tune
  Annual average permit limits
  Numeric Nutrient Criteria to be assessed long term

## Slide 11: Cost and Affordability
Total Present Worth Cost
= 1.53 ($B)
Total Capital Cost
= 1.00 ($B)
Estimated Costs for BNR Improvements for all Industries with Biological Treatment (Target Effluent TN = 10 mg/L, Target Effluent TP = 1 mg/L) |  |  |  |  |  |  | 
Treatment Type | # of Facilities | Combined Design Flow (MGD) | Total Capital Cost ($M) | Total Annual O&M Cost ($M) | Total Present Worth Cost ($M)1 | Total Annual Cost ($M) | $/1,000 gallons Treated2
Activated Sludge | 20 | 44.2 | 29.3 | 2.0 | 56.1 | 4.2 | 0.26
Fixed Film | 1 | 0.6 | 2.7 | 0.04 | 3.3 | 0.2 | 1.06
Aerated Lagoon | 7 | 5.8 | 86.5 | 2.20 | 116.0 | 8.6 | 4.05
Totals | 28 | 50.7 | 118.5 | 4.2 | 175.5 | 13.1 | 0.71
Notes: Points: 1. The $1.53 B represents the cost of BNR at all 130 facilities. The amount shows that there is a serious financial commitment. This cost is spread over ~20 years. Accuracy is within ~ 50%.
Not an instantaneous cost, rather, the cost is spread over time.
3. This approach is practical for activated sludge facilities, with an added cost of ~$8/month; not feasible, for example, for aerated lagoon systems. Feasibility is determined by not more than 2% of median household income.
4. Will consider the need to implement on a case-by-case basis: there is no requirement for implementation.
<number>

## Slide 12: Status:
4 public meetings held
Public comment period closed January 18, 2013
1,700+ comments received
Reviewed comments and made improvements
Document final as of May 29
Documents and public comments can be accessed at:
www.nutrientstrategy.iastate.edu
Notes: <number>

## Slide 13: Questions?
Adam Schnieders
515.281.7409
adam.schnieders@dnr.iowa.gov
John Olson
John.olson@dnr.iowa.gov
515-281-8905