## Slide 1
ODS System
Louisville Water Company
June 2017

## Slide 2: Presentation Outline
Introduction
Louisville’s source water monitoring programs
Current ODS analytical capabilities
Proposed CDS monitoring capabilities

## Slide 3
Best Water Must Meet 3 Standards
Meet/exceed stringent and complex regulations: health risk issues or safe to drink
  Pathogens
  Organics (spills & pesticide contamination)
  Inorganics (lead and copper)
  Distribution water quality and residual management
90+ contaminants required for simultaneous compliance
Maintain/improve customer satisfaction: aesthetics issues or best tasting
  Taste & Odor (algae, di-chloramine)
  Discolored water (red water, black water)
Customers often use aesthetic parameters as water safety indicators
Maintain public understanding and trust: perceived risks
  Detection of unregulated chemicals: Dose makes the poison!
  NGO, media, societal and political pressures: Upgrade treatment goals
Customer response to the EWG report on Cr-6 exceeded the response to the annual rate increase

## Slide 4
ORSANCO’s Role
Spill notification
Technical support – ODS analytical
Algae program (T&O and HAB)
Public confidence

## Slide 5: LWC’s Event Response Experience
2005 Kentucky River Oil Spill
2012 Ohio River T&O Event
  Largest T&O in history (Max Raw MIB 178 ppt)
  Timely detection, treatment and communications
  No Customer Complaints
2014 WV MCHM Spill
  Correctly identified as a T&O concern for LWC customers
  Plan development, monitoring, and treatment with 100% execution
2015 HAB
  Largest Microcystin bloom observed
  Timely detection, treatment and communications
  No toxins detected in finished water

## Slide 6: Recent Events That Impacted LWC
Elk River 4-MCHM & PPH January 2014
  More than 10,000 gallons of MCHM (88.5% MCHM 7.3% PPH) was released to the Elk River on January 9, 2014
    Plume arrived at LWC January 17th as predicted with collaboration with ORSANCO
    Qualitative and quantitative analysis ready with collaboration with GCWW
Duke Energy August 2014
  5,000-8,000 gal No 2 fuel released at mile marker 450
  Low impact to LWC

## Slide 7: LWC’s Existing Source Water Quality Monitoring Programs
Spill Monitoring
  Collaborate with Ohio River Valley Sanitation Commission
  Detect 30 volatile organic compounds (VOCs)
Pesticide/Herbicide Monitoring
  Daily immuno-assay and/or GC-MS from April to August
  Weekly immuno-assay and monthly GC-MS from Sept. to March
Algae Monitoring (T&O and Algae Toxins)
(April to November)
  T&O panel
  Lab SPME/GC/MS : MIB/Geosmin
  Algae identification and quantification
  ELISA

## Slide 8
LWC’s Source Water Monitoring

## Slide 9: ODS at LWC – The Last 10 years
No unknown event detections by the current ODS GC-MS
  Sampling (frequency, location, technique)?
  Sampling/analysis frequency not giving an accurate picture of river conditions
  Lack of pollution/Limits of detection?
  Instrumental limitations?
      Column
      Temperature programs
      Purge & trap

## Slide 10: Proposed CDS Monitoring Capabilities
  ODS to CDS: Contaminant Detection System?
  Comprehensive source water monitoring with tiered approach
    Everyone:
      More frequent sampling (on-line/photo-based analyzer)
      Daily WQ database (pH, turbidity, flow, DO, ammonia, ORP, UV…)
      Additional screening tools (bench)
    A selected few
      Sensitive confirmation analysis
      Treatment guidance and technical support
      In-house investment including drone technology
    Lead and/or coordination by ORSANCO

## Slide 11: Proposed CDS Monitoring Capabilities
  ID water quality events: spills, T&O, HAB, pesticides, etc.
  Historical data: what, how much, when?
  Analyze these data to get information
  Review/analyze current ODS sites
  Convert all the current ODS sites to CDS sites with screen capabilities
  ID 3 to 5 sites/utilities that can conduct in-house confirmation: GC-MS and other analytical capabilities
  ORSANCO leads and coordinates all the communications/activities. GCWW & LWC provide technical support

## Slide 12: Monitoring Technologies
  Everyone - Screen:
    On-line: FEEM, etc.
    Bench: Elisa, etc.
  A Selected few - In-depth analysis:
    GC-MS
    Additional analytical tools
    Treatment case studies