## Slide 1: Ohio Statewide Nutrient Balance
Division of Surface Water
Modeling, Assessment and TMDL Section
Notes: Statewide project: large endpoint (LE, OR)
Nutrients: N and P
Balance = total load at a defined point on river equal to sum of parts (sources of load) upstream within the watershed.

## Slide 2
Objectives
Guide Ohio EPA policy & management
  Relative loads (by watershed)
  Load sources (CSO vs. NPS vs. wastewater)
Support national programs – Annex 4 and Gulf Hypoxia Task Force
From HB 64, statutory obligation 6111.03 (U) requires Agency…
  total load, load sources
  report every 2 years

## Slide 3: Division of Surface Water Modeling, Assessment and TMDL Section December 30, 2016
Report available at:
http://www.epa.state.oh.us/dsw/wqs/NutrientReduction.aspx#146065085-nutrient-mass-balance

## Slide 4: Statewide Nutrient Reduction Efforts Strategies, Funding, and Legislation
Nutrient Reduction Strategy (2013): 3 agencies
GLRI Projects:
  9 grants, $12 million
Legislation
  SB 1 (2015): POTW 1 mg/L, fertilizer/manure application
  SB 150 (2014): certified fertilizer application
WLEB Collaborative Plan:
  40% reduction tot P & DRP “Western Basin”
Notes: Recognize govt institutions recognize the problem and likely sources…here are examples of activity during/since wy13 and wy14
GLRI: Cover crops, controlled drainage, farm cons plans, wetland restoration
Other efforts not listed:
  Ohio Clean Lakes Initiative
  Healthy Lake Erie Fund (2014): reduce open lake dredge deposit
  Ag Nutrients and WQ Workgroup (2012)
  LE PTF 2 (2012)
  PS and Urban Runoff Workgroup (2012): reduce P from WWTP, industrial, and urban SW

## Slide 5
Study Area Covered
7 major watersheds
26,000 sq. mi. (in Ohio)
63% of Ohio’s land area
Lake Erie Basin
Ohio River Basin
Western LE Basin
Central LE Basin
Great Miami
Maumee
Scioto
Muskingum
Sandusky
Cuyahoga
Cuya
Portage
Notes: Map:
  Name 7 watersheds (4 LE – 2 enter Western Basin, 2 enter Central Basin, 3 OR)
  Major rivers are shown in blue
  Red points are called pour–points (defined at daily WQ monitoring stations – Heidelberg) – where the nutrient balance is calculated
We intend to expand our work into the remaining portions of Ohio; however, we can postulate that these 7 watersheds (63%) may produce a higher % of total load entering LE or OR.

## Slide 6: Data Time Period
Loads calculated for ‘water years’ (Oct 1 to Sept 30 basis)
  Most recent complete data available for 2013 and 2014 (when study started)
  Designated “wy13” and “wy14”
  Matches related efforts in reporting e.g., GLWQA - Annex 4, NCWQR, USGS

## Slide 7: Calculation Methodology
Mass balance loading calculation:
  NPDES = sum of all NPDES loads
  HSTS = estimate of total HSTS load
  NPSupst = calculated ‘Pour Point’ load minus (NPDES + HSTS)
  NPSdst = est. from NPSupst relative to downstream area

## Slide 8: Watershed Schematic for Calculation
Pour Point
NPDES-1
NPDES-2
NPDES-3
HSTS est.
NPS-upstr
NPS-dstr
Upstream Drainage Area
Downstream Drainage Area
Outlet (River or Lake)
HSTS est.
•
•
Notes: Total Upstream Load is measured directly at the Pour Point.
Upstream NPS Load is estimated by subtracting the sum of measured or estimated Upstream PS and HSTS loads from the Total Upstream Load (Pour Point Load).
Downstream NPS load estimated based upon upstream NPS yield (loading per unit area) times the Downstream Area.
Total Load at Outlet is sum of Total Upstream Load plus sum of measured or estimated Upstream PS and HSTS loads plus estimated Downstream NPS Load.

## Slide 9: Calculation: NPDES
NPDES sources
  Municipal NPDES
    Total annual discharge (reported data)
    Median of nutrient concentration, if reported
    Nutrient concentration estimates from similar facilities, if not reported
  CSOs (all wet weather) includes bypass flows
    Actual reporting data or system characterization flows (LTCP) if under-represented
    Most SSOs do not report volume (only occurrence)
    CSO nutrient concentrations fixed (based on literature values)
  Industrial facilities
    Total annual discharge (reported data)
    Nutrient concentration only if there was reported data
    If no nutrient monitoring, assume de minimis contribution

## Slide 10: Calculation: HSTS, NPS
Household sewage treatment systems (HSTS)
  Population using HSTS (2010 US Census)
    Estimated using GIS analysis of census information
  Nutrient yield (lb/person/year): from literature (Lowe, 2009)
  Differentiated by regional 2012 survey (ODH, 2013)
    direct discharge vs. onsite
    onsite: working vs. failed
Nonpoint source
  NPS upstream of pour point
    Does not differentiate between types of NPS (e.g., agriculture vs. urban stormwater)
  NPS downstream = Upstream NPS Yield x Downstream Area
    NPS Yield = NPS Load divided by Watershed Area
Notes:   NPS upstream = Pour Point Total Load minus Point Source Load

## Slide 11: Water Yield: Study vs. 20-year History Water Yield = total discharge divided by watershed area
Chart: Water Yield (in/yr)
| Maumee | Portage | Sandusky | Cuyahoga | Great Miami | Scioto | Muskingum
25th pct | 12.1564 | 10.6589 | 11.8654 | 16.5888 | 13.5845 | 12.4772 | 13.8593
50th pct | 1.7847 | 2.8711 | 2.1756 | 5.0304 | 3.7361 | 3.0854 | 1.5756
75th pct | 1.1961 | 3.0812 | 3.9931 | 2.8944 | 3.2394 | 3.6146 | 3.3351
wy13 | 12.0711 | 13.3207 | 18.1317 | 21.2736 | 13.7564 | 14.0076 | 14.8568
wy14 | 14.0419 | 15.6232 | 17.2311 | 22.4448 | 18.4076 | 17.6425 | 18.6602
Water yields for study years (wy13 & wy14) were within typical ranges during past 20 years for all watersheds
___________ * Water Years 1996-2015; (2002-2015 for Muskingum)
Notes: How do our 2 years of load analysis compare with runoff/streamflow over a longer time period?
Define water yield (depth/year) = total discharge (vol/year) divided by watershed area
Explain structure of boxplot: median, 25th/75th pct, extreme high/low.
Generally all watershed for these two application years (wy13 and wy14) within realm of “normal” (i.e., within 25th/75th pct).
Elevated wrt to other watershed: ORB higher than LEB, Cuy high (snowbelt), ORB esp high wy14).

## Slide 12
Total P Load
Chart: Load (mta)
| wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14
NPS upst Pour Point | 1911.7813 | 1673.0305 | 103.1759 | 137.3441 | 583.8141 | 501.3721 | 171.2081 | 227.2952 | 495.9838 | 884.2457 | 791.0608 | 956.3764 | 514.9331 | 871.9196
NPS dst Pour Point | 82.2253 | 71.9567 | 38.1715 | 50.8125 | 79.8331 | 68.5597 | 25.7462 | 34.1806 | 214.7751 | 382.9035 | 547.3765 | 661.767 | 43.6328 | 73.882
Total NPDES | 217.0655 | 232.5042 | 19.1366 | 22.9121 | 32.1768 | 29.6091 | 94.6601 | 104.5804 | 474.4294 | 450.5289 | 616.9811 | 727.687 | 670.4534 | 589.0971
HSTS | 84.2 | 84.2 | 7.6987 | 7.6987 | 15.0371 | 15.0371 | 35.5262 | 35.5262 | 80.7 | 80.7 | 80.0815 | 80.0815 | 131.1976 | 131.1976
Dummy 1 | 0
Dummy 2
Dummy 3 | 0.195 | 0.21441 | 0.21808 | 0.31737 | 0.42266 | 0.50322 | 0.40076 | 0.3411 | 0.0085525 | 0.022088 | 0.0094533 | 0.051749 | 0.0008445 | 0.0024805
Dummy 4 | 0.195 | 0.21441 | 0.21808 | 0.31737 | 0.42266 | 0.50322 | 0.40076 | 0.3411 | 0.0085525 | 0.022088 | 0.0094533 | 0.051749 | 0.0008445 | 0.0024805
Notes: Open…will talk about individual watershed proportions later – this slide is for big picture differences between watersheds – first cover P then cover N
Little bit busy presenting both water years but I don’t find it appropriate to compute an average for the two years – as we get more years of data we can report a ‘normal’
Explain axis – L to R (W to E, LE then OR), load (MTA)
  MTA used by the large loading community (e.g., Annex 4)
  Total load – subdivided into sources (stacked bar) – left axis
Total load: Maumee & Scioto have highest loads
  Muskingum is largest watershed but only the 4th highest load contributor
Proportions: Two red-orange colors are NPS and can be looked at as one; differences are detailed in the report
  Highest proportions of NPS in NW Ohio: Sandusky, Maumee, Portage
  Highest proportions of PS in Ohio River basin; Cuyahoga also high
NPS yield
  Yield: load standardized by area of watershed; grey bar (right axis)
  Highest in NW Ohio
    Maumee has highest total load, BUT… Sandusky and Portage have higher yields
    Lowest NPS yield Muskingum (hypothesize in-stream reservoirs, natural land)
Per capita yields
  NPDES (CSO + final) and HSTS load
  Yield: load standardized by number of people residing in watershed; blue bar (right axis)
  Highest values in Ohio River basin – lack of P limits
  Lowest value in Cuyahoga – lots of NPDES load, but lots of people
Summary
  Maumee loadings are similar to other reports
  Ohio River basin may raise more questions…surprised so high on annual basis

## Slide 13
Total P Yield
Chart: Yield (lb/ac or lb/person)
Dummy 1 | 0
Dummy 2
Dummy 4 | 0.195 | 0.21441 | 0.21808 | 0.31737 | 0.42266 | 0.50322 | 0.40076 | 0.3411 | 0.0085525 | 0.022088 | 0.0094533 | 0.051749 | 0.0008445 | 0.0024805
NPS Yield | 1.0458 | 0.91521 | 0.83231 | 1.1079 | 1.6099 | 1.3825 | 0.83962 | 1.1147 | 0.62953 | 1.1223 | 0.70797 | 0.85592 | 0.23919 | 0.40501
Per Capita Yield | 0.61144 | 0.64278 | 0.88063 | 1.0045 | 0.80014 | 0.75663 | 0.2855 | 0.30725 | 0.90007 | 0.86132 | 0.7925 | 0.91836 | 1.2088 | 1.0861
wy13 wy14
wy13 wy14
wy13 wy14
wy13 wy14
wy13 wy14
wy13 wy14
wy13 wy14
Notes: Open…will talk about individual watershed proportions later – this slide is for big picture differences between watersheds – first cover P then cover N
Explain axis – L to R (W to E, LE then OR), load (MTA)
  MTA used by the large loading community (e.g., Annex 4)
  Total load – subdivided into sources (stacked bar) – left axis
Total load: Maumee & Scioto have highest loads
  Muskingum is largest watershed but only the 4th highest load contributor
Proportions: Two red-orange colors are NPS and can be looked at as one; differences are detailed in the report
  Highest proportions of NPS in NW Ohio: Sandusky, Maumee, Portage
  Highest proportions of PS in Ohio River basin; Cuyahoga also high
NPS yield
  Yield: load standardized by area of watershed; grey bar (right axis)
  Highest in NW Ohio
    Maumee has highest total load, BUT… Sandusky and Portage have higher yields
    Lowest NPS yield Muskingum (hypothesize in-stream reservoirs, natural land)
Per capita yields
  NPDES (CSO + final) and HSTS load
  Yield: load standardized by number of people residing in watershed; blue bar (right axis)
  Highest values in Ohio River basin – lack of P limits
  Lowest value in Cuyahoga – lots of NPDES load, but lots of people
Summary
  Maumee loadings are similar to other reports
  Ohio River basin may raise more questions…surprised so high on annual basis

## Slide 14
Total N Load & Yield
Chart: Load (mta)
| wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14 | wy13 | wy14
NPS upst Pour Point | 37207.0001 | 31304.8939 | 2545.747 | 1919.534 | 9573.7114 | 6897.453 | 1712.0569 | 1910.0472 | 10406.1404 | 11751.7482 | 10969.7262 | 13655.2872 | 12544.8388 | 15741.3284
NPS dst Pour Point | 1600.2653 | 1346.4169 | 941.8368 | 710.1601 | 1309.1484 | 943.1859 | 257.4588 | 287.2326 | 4506.1544 | 5088.8409 | 7590.5296 | 9448.8102 | 1062.9851 | 1333.8392
Total NPDES | 4283.8387 | 4594.2848 | 319.6845 | 363.9954 | 379.1113 | 369.9573 | 3842.4738 | 3422.9977 | 3143.2346 | 3382.1769 | 3599.914 | 4084.696 | 4974.8863 | 4999.6369
HSTS | 607.2 | 607.2 | 74.4701 | 74.4701 | 145.454 | 145.454 | 351.1505 | 351.1505 | 582 | 582 | 782.4704 | 782.4704 | 1380.7166 | 1380.7166
Dummy 1 | 0
Dummy 2
Dummy 3 | 0.30423 | 0.31928 | 0.12064 | 0.18244 | 0.32682 | 0.36761
Dummy 4 | 0.30423 | 0.31928 | 0.12064 | 0.18244 | 0.32682 | 0.36761 | 0.090102 | 0.09516 | 0.011789 | 0.02687 | 0.014796 | 0.084192 | 0.0010394 | 0.0026691
Notes: Very similar to the phosphorus results, but a few key differences:
  Don’t see the same difference between the Ohio River and Lake Erie basin relative to PS proportion
  Point source proportions much higher for Cuyahoga than any other watershed
  Note again, NPS yields in Sandusky were the highest observed

## Slide 15
Total N Load & Yield
Chart: Yield (lb/acre or lb/person)
NPS Yield | 20.3536 | 17.1249 | 20.5364 | 15.4848 | 26.3995 | 19.0197 | 8.3961 | 9.367 | 13.2081 | 14.9161 | 9.8175 | 12.221 | 5.8271 | 7.3119
Per Capita Yield | 9.9268 | 10.5569 | 12.9346 | 14.3887 | 8.8899 | 8.7347 | 9.1966 | 8.2767 | 6.04 | 6.4274 | 4.9824 | 5.5336 | 9.5834 | 9.6207
Dummy 1 | 0
Dummy 2
Dummy 3 | 0.30423 | 0.31928 | 0.12064 | 0.18244 | 0.32682 | 0.36761
Dummy 4 | 0.30423 | 0.31928 | 0.12064 | 0.18244 | 0.32682 | 0.36761 | 0.090102 | 0.09516 | 0.011789 | 0.02687 | 0.014796 | 0.084192 | 0.0010394 | 0.0026691
Notes: Very similar to the phosphorus results, but a few key differences:
  Don’t see the same difference between the Ohio River and Lake Erie basin relative to PS proportion
  Point source proportions much higher for Cuyahoga than any other watershed
  Note again, NPS yields in Sandusky were the highest observed

## Slide 16
Population Density
Notes: We looked at the population density it helps inform why:
Proportion of PS is so high for Cuyahoga (nearly 4x as many people per area)
Also note pop density is elevated for Scioto and GMR
  Proportional loading in these watersheds is confounded by major facilities not being subject to TP limits

## Slide 17
Land Use
Chart: Percent of Total Area
Agricultural | 77.4436 | 81.1484 | 80.3999 | 15.3722 | 68.0477 | 57.7288 | 39.7333
High intensity development | 1.7715 | 1.3767 | 0.91135 | 10.3114 | 2.8215 | 2.96 | 1.4837
Low intensity development | 9.7875 | 8.7052 | 7.8886 | 35.948 | 14.9883 | 10.3535 | 10.7115
Natural | 10.8788 | 8.4652 | 10.517 | 38.2331 | 14.0554 | 28.832 | 47.7734
Notes: We looked at the land use – it helps inform why:
NPS is high in NW Ohio
PS is high in Cuyahoga
NPS is low in Muskingum

## Slide 18
Facility Size Classes
Notes: The next slides show proportional loads
The size classes for NPDES permit holders are used to show how different types of facilities are contributing to those loads

## Slide 19
Maumee Watershed
Located in NW Ohio draining to the Western Lake Erie Basin
77% Agricultural Lands
Major Cities include Toledo and Lima, Ohio and Fort Wayne, Indiana
Notes: This is an example of the type of information included in the report for each watershed. This one is for Maumee in wy13. The non point source loads reduced slightly in wy14 so the relative contribution of NPDES sources and HSTS increased slightly.
Mention that NPDES classes get successively smaller progressing from 2 – 5.
Highlight small proportion of loading that comes from CSOs relative to the final outfalls of the major WWTPs; however several of the largest WWTPs pass there partially treated wet weather flows through the final outfall station.
Small facilities do not constitute a considerable part of the total NPDES.
Proportional loads for TP and TN are similar. Major WWTPs become a larger percentage of the NPDES loads for TN than they are for TP.
These results agree with other analyses that have been completed for the watershed.

## Slide 20
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs | OOS PS | OOS Wet Weather
 | 607.2 | 38807.2654 | 2496.2824 | 48.7776 | 31.3361 | 70.5127 | 35.3033 | 54.5671 | 142.3699 | 1160.8895 | 243.8
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs | OOS PS | OOS Wet Weather
 | 84.2 | 1994.0066 | 101.6506 | 10.3802 | 6.7023 | 4.9203 | 4.5616 | 12.0973 | 15.6271 | 34.4261 | 26.7
wy13 Loading Breakdown - Maumee Watershed
Total N
Non point Source
HSTS
NPDES Sources
  CSO
  Out of State NPDES
  Class 4
  Class 5
  Industrial
  Major WWTP
  Class 2
  Class 3
Total P
Notes: This is an example of the type of information included in the report for each watershed. This one is for Maumee in wy13. The non point source loads reduced slightly in wy14 so the relative contribution of NPDES sources and HSTS increased slightly.
Mention that NPDES classes get successively smaller progressing from 2 – 5.
Highlight small proportion of loading that comes from CSOs relative to the final outfalls of the major WWTPs
Small facilities do not constitute a considerable part of the total NPDES.
Proportional loads for TP and TN are similar. Major WWTPs become a larger percentage of the NPDES loads for TN than they are for TP.
These results agree with other analyses that have been completed for the watershed.

## Slide 21
Portage Watershed
Located in NW Ohio draining to the Western Lake Erie Basin
81% Agricultural Lands
Largest cities are Fostoria and Bowling Green

## Slide 22
wy13 Loading Breakdown - Portage Watershed
Total N
Total P
Non point Source
HSTS
NPDES Sources
  CSO
  Class 4
  Class 5
  Industrial
  Major WWTP
  Class 2
  Class 3
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TP YR'13 | 7.6987 | 141.3474 | 6.4845 | 5.2246 | 2.0286 | 0.49631 | 0.72353 | 0.0056357 | 4.1734
 | 7.6987 | 141.3474 | 6.4845 | 5.2246 | 2.0286 | 0.49631 | 0.72353 | 0.0056357 | 4.1734
TP YR'13 | 7.6987 | 141.3474 | 6.4845 | 5.2246 | 2.0286 | 0.49631 | 0.72353 | 0.0056357 | 4.1734
TP YR'13 | 7.6987 | 141.3474 | 6.4845 | 5.2246 | 2.0286 | 0.49631 | 0.72353 | 0.0056357 | 4.1734
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TN YR'13 | 74.4701 | 3487.5838 | 229.4222 | 31.8198 | 8.9913 | 5.002 | 5.8716 | 0.011583 | 38.566
Notes: This is an example of the type of information included in the report for each watershed. This one is for Maumee and again it agrees with other analyses that have been completed for the watershed.
Mention that NPDES classes get successively smaller progressing from 2 – 5.
Highlight small proportion of loading that comes from CSOs.
Small facilities do not constitute a considerable part of the total NPDES.

## Slide 23
Sandusky Watershed
Located in NW Ohio draining to Sandusky Bay and the Central Lake Erie Basin – sometimes considered a Western Lake Erie Basin Tributary
80% Agricultural Lands
Largest cities are Tiffin and Fremont
Notes: Might note that Tiffin is the home of Heidelberg and NCWQR.

## Slide 24
wy13 Loading Breakdown - Sandusky Watershed
Total N
Total P
Non point Source
HSTS
NPDES Sources
  CSO
  Class 4
  Class 5
  Industrial
  Major WWTP
  Class 2
  Class 3
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TP YR'13 | 15.0371 | 663.6472 | 8.991 | 7.4962 | 0 | 1.3893 | 0.58607 | 0.11418 | 13.6
 | 15.0371 | 663.6472 | 8.991 | 7.4962 | 0 | 1.3893 | 0.58607 | 0.11418 | 13.6
TP YR'13 | 15.0371 | 663.6472 | 8.991 | 7.4962 | 0 | 1.3893 | 0.58607 | 0.11418 | 13.6
TP YR'13 | 15.0371 | 663.6472 | 8.991 | 7.4962 | 0 | 1.3893 | 0.58607 | 0.11418 | 13.6
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TN YR'13 | 145.454 | 10882.8598 | 215.39 | 26.2031 | 0 | 7.5161 | 5.9912 | 0.11098 | 123.9
Notes: This is an example of the type of information included in the report for each watershed. This one is for Maumee and again it agrees with other analyses that have been completed for the watershed.
Mention that NPDES classes get successively smaller progressing from 2 – 5.
Highlight small proportion of loading that comes from CSOs.
Small facilities do not constitute a considerable part of the total NPDES.

## Slide 25
Cuyahoga Watershed
Located in NE Ohio draining to the Central Lake Erie Basin
15% Agricultural Lands
Most developed watershed in the study; Largest cities are Cleveland and Akron
Includes the Cuyahoga Valley National Park and other extensive park systems resulting in 38% natural areas

## Slide 26
wy13 Loading Breakdown - Cuyahoga Watershed
Total N
Total P
Non point Source
HSTS
NPDES Sources
  CSO
  Class 4
  Class 5
  Industrial
  Major WWTP
  Class 2
  Class 3
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TP YR'13 | 35.5262 | 196.9543 | 53.4602 | 0.13186 | 0.8516 | 0.67702 | 1.5892 | 0.014087 | 37.9361
 | 35.5262 | 196.9543 | 53.4602 | 0.13186 | 0.8516 | 0.67702 | 1.5892 | 0.014087 | 37.9361
TP YR'13 | 35.5262 | 196.9543 | 53.4602 | 0.13186 | 0.8516 | 0.67702 | 1.5892 | 0.014087 | 37.9361
TP YR'13 | 35.5262 | 196.9543 | 53.4602 | 0.13186 | 0.8516 | 0.67702 | 1.5892 | 0.014087 | 37.9361
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TN YR'13 | 351.1505 | 1969.5157 | 3376.4676 | 25.499 | 16.507 | 13.0814 | 13.2904 | 51.4121 | 346.2162
Notes: This is an example of the type of information included in the report for each watershed. This one is for Maumee and again it agrees with other analyses that have been completed for the watershed.
Mention that NPDES classes get successively smaller progressing from 2 – 5.
Highlight small proportion of loading that comes from CSOs.
Small facilities do not constitute a considerable part of the total NPDES.

## Slide 27
Great Miami Watershed
Located in SW Ohio draining to the Ohio River
68% Agricultural Lands
Largest cities are Dayton, Middletown and Hamilton

## Slide 28
wy13 Loading Breakdown – Great Miami Watershed
Total N
Total P
Non point Source
HSTS
NPDES Sources
  CSO
  Class 4
  Class 5
  Industrial
  Major WWTP
  Class 2
  Class 3
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TP YR'13 | 80.7 | 710.7589 | 417.6823 | 7.7939 | 6.4847 | 1.9416 | 4.9831 | 31.4862 | 4.0575
 | 80.7 | 710.7589 | 417.6823 | 7.7939 | 6.4847 | 1.9416 | 4.9831 | 31.4862 | 4.0575
TP YR'13 | 80.7 | 710.7589 | 417.6823 | 7.7939 | 6.4847 | 1.9416 | 4.9831 | 31.4862 | 4.0575
TP YR'13 | 80.7 | 710.7589 | 417.6823 | 7.7939 | 6.4847 | 1.9416 | 4.9831 | 31.4862 | 4.0575
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TN YR'13 | 582 | 14912.2948 | 2871.9216 | 44.269 | 43.4691 | 11.2021 | 17.7449 | 117.5727 | 37.0552

## Slide 29
Scioto Watershed
Located in Central and Southern Ohio draining to the Ohio River
58% Agricultural Lands
Large cities include Columbus, Delaware, Marion and Chillicothe
Notes: To contrast the results observed from the Maumee Watershed, a the results from the Scioto River watershed are now shown. wy14 saw similar magnitude increases for both Non point source and NPDES sources so the proportions did not change much. We have results from other watersheds covered in the mass balance but won’t cover them all unless questions arise later in discussion.
>3x of the annual TP loading and ~1.5x the annual TN loading than the Maumee
While the Maumee had higher proportions of the NPDES load attributed to sources other than the Major WWTPs the Majors accounted for >90% of the annual NPDES load in the Maumee
Contrasting the Maumee the TN from NPDES sources was nearly half the contribution of TP when compared to the total annual load
- We have contributed this to TP limits that are standard for Major WWTPs in the Lake Erie Basin but uncommon in the Ohio River Basin

## Slide 30
wy13 Loading Breakdown - Scioto Watershed
Total N
Total P
Non point Source
HSTS
NPDES Sources
  CSO
  Class 4
  Class 5
  Industrial
  Major WWTP
  Class 2
  Class 3
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TP YR'13 | 80.0815 | 1338.4374 | 575.545 | 7.0481 | 4.7523 | 5.4877 | 4.1262 | 14.1894 | 5.8325
 | 80.0815 | 1338.4374 | 575.545 | 7.0481 | 4.7523 | 5.4877 | 4.1262 | 14.1894 | 5.8325
TP YR'13 | 80.0815 | 1338.4374 | 575.545 | 7.0481 | 4.7523 | 5.4877 | 4.1262 | 14.1894 | 5.8325
TP YR'13 | 80.0815 | 1338.4374 | 575.545 | 7.0481 | 4.7523 | 5.4877 | 4.1262 | 14.1894 | 5.8325
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TN YR'13 | 782.4704 | 18560.2558 | 3314.3524 | 103.6612 | 40.8269 | 39.3388 | 41.4563 | 7.0135 | 53.2649
Notes: To contrast the results observed from the Maumee Watershed, a the results from the Scioto River watershed are now shown. wy14 saw similar magnitude increases for both Non point source and NPDES sources so the proportions did not change much. We have results from other watersheds covered in the mass balance but won’t cover them all unless questions arise later in discussion.
>3x of the annual TP loading and ~1.5x the annual TN loading than the Maumee
While the Maumee had higher proportions of the NPDES load attributed to sources other than the Major WWTPs the Majors accounted for >90% of the annual NPDES load in the Maumee
Contrasting the Maumee the TN from NPDES sources was nearly half the contribution of TP when compared to the total annual load
- We have contributed this to TP limits that are standard for Major WWTPs in the Lake Erie Basin but uncommon in the Ohio River Basin

## Slide 31
Muskingum Watershed
Located in SE Ohio draining to the Ohio River
40% Agricultural Lands
Large cities include Canton, Massillon, Dover/New Philadelphia and Zanesville
Notes: To contrast the results observed from the Maumee Watershed, a the results from the Scioto River watershed are now shown. wy14 saw similar magnitude increases for both Non point source and NPDES sources so the proportions did not change much. We have results from other watersheds covered in the mass balance but won’t cover them all unless questions arise later in discussion.
>3x of the annual TP loading and ~1.5x the annual TN loading than the Maumee
While the Maumee had higher proportions of the NPDES load attributed to sources other than the Major WWTPs the Majors accounted for >90% of the annual NPDES load in the Maumee
Contrasting the Maumee the TN from NPDES sources was nearly half the contribution of TP when compared to the total annual load
- We have contributed this to TP limits that are standard for Major WWTPs in the Lake Erie Basin but uncommon in the Ohio River Basin

## Slide 32
wy13 Loading Breakdown – Muskingum Watershed
Total N
Total P
Non point Source
HSTS
NPDES Sources
  CSO
  Class 4
  Class 5
  Industrial
  Major WWTP
  Class 2
  Class 3
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TP YR'13 | 131.1976 | 558.5659 | 563.023 | 21.2598 | 14.0512 | 7.6238 | 6.0656 | 57.864 | 0.5662
 | 131.1976 | 558.5659 | 563.023 | 21.2598 | 14.0512 | 7.6238 | 6.0656 | 57.864 | 0.5662
TP YR'13 | 131.1976 | 558.5659 | 563.023 | 21.2598 | 14.0512 | 7.6238 | 6.0656 | 57.864 | 0.5662
TP YR'13 | 131.1976 | 558.5659 | 563.023 | 21.2598 | 14.0512 | 7.6238 | 6.0656 | 57.864 | 0.5662
Chart: 
| HSTS | NPS | 1 (ADF ≥ 1.0 mgd) | 2 (0.5 mgd ≤ ADF < 1.0 mgd) | 3 (0.25 mgd ≤ ADF < 0.5 mgd) | 4 (0.1 mgd ≤ ADF < 0.25 mgd) | 5 (ADF < 0.1 mgd) | Industrials | CSOs
TN YR'13 | 1380.7166 | 13607.8239 | 3138.2787 | 151.9878 | 100.1475 | 55.1679 | 46.9133 | 1477.2204 | 5.1708

## Slide 33
What’s Next
  Increase the portion of the state covered by mass balance calculations
  Start to establish trends with 5-years of data
  Refine HSTS estimates
    Use county level statistics where needed
    Improve population estimates by refining sewerage areas
  Improve nutrient concentration estimates for CSO discharges
  Refine NPS load estimates
    Separate urban storm water component
    Differentiate agricultural loads by nutrient source
Notes: Lake Erie Priority 1: Vermillion, Huron, Grand – best case would be to start in wy17
Lake Erie Priority 2: Black R, Toussaint Ck, Rocky R, and Chagrin R
Ohio River Priority 1: Hocking R, L Miami R, and Mahoning R
Ohio River Priority 2: Wabash R and Mill Ck (Cincinnati)
Also, with five years of data we can use the 5-year average to present the proportional loading
We will work on developing a protocol to use lower frequency water quality data for annual loads. We may have to consider methods for when there is not water quality data available.

## Slide 34
Closing Note
  While the report was not intended to make recommendations about how to achieve nutrient reductions, the information within could and should inform the Agency and others about the most effective ways of achieving reductions.
Notes: Lake Erie Priority 1: Vermillion, Huron, Grand – best case would be to start in wy17
Lake Erie Priority 2: Black R, Toussaint Ck, Rocky R, and Chagrin R
Ohio River Priority 1: Hocking R, L Miami R, and Mahoning R
Ohio River Priority 2: Wabash R and Mill Ck (Cincinati)
Also, with five years of data we can use the 5-year average to present the proportional loading
We will work on developing a protocol to use lower frequency water quality data for annual loads. We may have to consider methods for when there is not water quality data available.

## Slide 35
Questions
Notes: We are likely to be able to do some of these things but not all. What do our stakeholders feel are the most important; maybe we can focus effort there. We are likely going to be able to make incremental improvements through future iterations that we can prioritize with time.
If they have suggestions make sure we ask if they know of how we can get the support to answer the question. (How do we do it)

## Slide 36: Discussion Slides

## Slide 37
Methods (1 of 4)
Early (technical) stakeholder outreach resulted in feedback from AOMWA (Guy Jamesson), Ohio Farm Bureau (Larry Antosch), TNC (Anthony Sasson), USGS (Dan Button), NCWQR (Rem Confessor), and City of Akron (Kathy Richards).
Loads calculated for ‘water years’ (Oct to Sept basis)
  Named wy13 and wy14
  Matches related efforts in reporting (Annex 4, NCWQR, USGS)
  “Spring” loads compiled for Maumee, Portage and Sandusky
Overall loading equation…for both total P and total N…
Notes: Early technical feedback – encouraged us to consider… orgN inclusion, HSTS inclusion, small WW facility, and industrial inclusion
Define water year –
  Named for September (end) of year – most months (9 vs. 3)
  Snow falling in one calendar year may become runoff (streamflow) in the next calendar year
Spring loads – implications for Annex 4 goals…
Spring = Mar 1 to Jul 31
Maumee NPS best predictor of cyanobacteria bloom severity during these 5 months

## Slide 38
Methods (2 of 4)
Source loads determined from:
  NPDES sources – includes CSOs
  Household sewage treatment systems (HSTS)
  Nonpoint source (total)
Notes: Consider nutrient: total P and total N
Total nitrogen – considers ammonia, nitrite-nitrate, and organic N
Not consider bio-available species (ortho-P, NO23 and NH3) because of the spiraling longitudinally and over an entire year representing load impact from the total (P or N) is most relevant
NPS is the remainder (not actually calculated) once NPDES (final & CSO) and HSTS are accounted for – represents both ag and urban/suburban yields

## Slide 39
Methods (3 of 4)
  NPDES sources
    Municipal NPDES
      Total annual discharge (reported data)
      Median of nutrient concentration, if reported
      Nutrient concentration estimates from similar facilities, if no reporting
    CSOs (all wet weather) includes bypass flows
      Actual reporting data or system characterization Q (LTCP) if under-represented
      Most SSOs do not report volume (only occurrence)
      CSO nutrient concentrations fixed
    Industrial facilities
      Total annual discharge (reported data)
      Nutrient concentration only if there was reported data
      If no nutrient monitoring, assume de minimis contribution
Notes: NPDES from SWIMS download, read by SQL – large datasets then processed in MS Excel
Bypass flows: both raw and secondary
SSOs included when flow volume is reported (e.g., City of Dayton)

## Slide 40
Methods (4 of 4)
  Household sewage treatment systems (HSTS)
    Population using HSTS (2010 US Census)
      Estimated using GIS analysis of census information
    Nutrient yield (lb/person/year): from literature (Lowe 2009)
    Differentiated by regional 2012 survey (ODH 2013)…
      direct discharge vs. onsite
      onsite: working vs. failed
  Nonpoint source (total)
    Determined as the total load minus the point source load
    Does not discriminate between types of NPS (e.g., agriculture vs. urban stormwater)
    Land use/cover characterized upstream/downstream of pour-point
      Unit area loads applied downstream of pour-point
Notes: 2010 US decennial Census
HSTS: 3 delivery ratios assigned:
  TP / TN
    Discharging (both working and failed)= 94% / 100%
    Onsite-failed = 60% / 60%
    Onsite-working = 20% / 60%
HSTS approach better (and different) than U Mich sustainability project

## Slide 41: 20-year Seasonal (Mar-Jul) Discharge 1996-2015 (2002-2015 for Muskingum)
Chart: Water Yield (in)
| Maumee | Portage | Sandusky | Cuyahoga | Great Miami | Scioto | Muskingum
25th pct | 4.4372 | 3.998 | 4.3401 | 6.6164 | 4.9676 | 4.6475 | 6.116
50th pct | 2.2354 | 2.0178 | 3.6037 | 2.9489 | 2.1246 | 1.6428 | 1.6859
75th pct | 1.3322 | 2.1102 | 2.198 | 2.34 | 2.7795 | 3.1928 | 0.9035
wy13 | 6.6258 | 6.4718 | 8.0234 | 10.0361 | 6.0275 | 9.8102 | 8.6938
wy14 | 6.7193 | 4.7914 | 8.7421 | 11.4606 | 9.714 | 9.2573 | 8.7092
Notes: Spring season – March to July, inclusive – adopted by Annex 4 because cyanobacteria bloom
As in annual water yield, seasonal water yield within realm of “normal”
wy 14 elevated for all ORB watersheds and for Cuy
  Scioto & Musk: wy 13 and wy 14 both elevated