## Slide 1: Nutrient Criteria Development 3rd Year Update
Ryan Argo
214th Technical Committee Meeting
Agenda Item 3

## Slide 2
…Selecting appropriate response variables requires further consideration. First, one should identify the designated use that is likely to be sensitive to increased N and P (e.g., aquatic life use support). Second, analysts should select an assessment endpoint that represents the designated use (e.g., health of the benthic macroinvertebrate community). Third, analysts should identify an appropriate measure of effect (US EPA 1998) for the selected assessment endpoint (e.g., a multimetric index value). In general, the most appropriate response variable both measures whether the designated use of the waterbody is supported and responds to changes in N and P concentration.

## Slide 3
…Other factors one might consider in selecting response variables include the inherent variability and signal-to-noise ratio of a particular measurement. An estimate of a stressor-response relationship for a highly variable measurement (e.g., abundance of a particular species) would be imprecise, which affects one’s ability to specify appropriate criteria (see Section 5.2). US EPA has historically recommended particular variables, where appropriate, for criteria (US EPA 2000a, 2000b, 2001). These variables include the “primary causal variables”, which are total nitrogen (TN) and total phosphorus (TP), and the “primary response variables”, which are chlorophyll a (chl a) and clarity. In some cases, selecting several different response variables and conducting stressor-response analyses for each of them may provide useful insights.

## Slide 4
Table 3-1. Examples of measured variables for different concepts shown in conceptual models for lakes and streams. * lakes only; ** streams only. Variables in bold are those that are most often available for stressor-response analysis.
Concept Examples of measured variables
Point Sources Compositions and emission rates from National Pollutant Discharge and Elimination System (NPDES) Permits
Urban Nonpoint Sources Summary statistics from land use / land cover maps
Agricultural Nonpoint Sources Summary statistics from land use / land cover maps
Geology Alkalinity, conductivity
Nutrients Total N, total inorganic N, total organic N, total Kjeldahl N, NO2/NO3, NH4, total P, PO4, N and P loading estimates.
Suspended Sediments Total suspended solids, turbidity
Toxics Metals, PAHs, pesticides
Physical Habitat Quality Qualitative or quantitative visual habitat measures, quantitative geomorphic measures, percent sand/fines.
Lake Depth* Total depth, epilimnion depth
Stratification* Temperature profile
Residence Time* Ratio of lake volume to outflow discharge
Fetch* Lake dimensions
Scour** Shear stress calculations, direct scour measures, stream discharge
Light Secchi depth, photsynthetically active radiation (PAR)
Color In situ measurements (Platinum Cobalt Units, PCU)
Temperature In situ measurements (degrees C)
Primary Production chl a, species, phytoplankton bloom frequency, ash free dry mass (AFDM), metabolism, cell counts, cell biovolume
Organic Matter Total organic carbon, dissolved organic carbon, particulate organic carbon, AFDM
Respiration Biochemical oxygen demand, chemical oxygen demand, metabolism
Nuisance Algae Cyanobacteria, abundance of nuisance algae or macrophytes
Dissolved Oxygen Dissolved oxygen concentration profile
Food Quantity Algal biomass (chl a, AFDM), zooplankton abundance, seston concentration, allochthonous organic matter standing stock (AFDM)
Food Quality Algal composition, C:N:P content, biochemical measures (e.g., protein content)
Algal Toxins Biochemical indicators (e.g., microcystins, anatoxins)
Recreation Clarity, use surveys, fishing permits
Aquatic Life Use Bioindicators (e.g., indices of biological integrity), chl a, fish kills
Drinking Water Supply Taste, odor, turbidity, biochemical measures (e.g., trihalomethane)

## Slide 5: The Current Approach
Nutrient Program – Paired data collections
  nutrients, planktonic algae & chl-a
  failed to develop a cause and effect relationship
ORMIn
  Metrics varied with habitat and showed responsiveness to nutrients
Missing Piece = Continuous DO
  Determine min and daily change
Augmented Macro Sampling
  Began 2014 w/ USACE Louisville co-op
  Continue through 2017
ORSANCO’s conceptual approach to nutrient criteria development modified from Qian & Miltner (2014, in prep)

## Slide 6: Field Activities
Paired Sampling (2-4 rounds)
  Nitrogen – Ammonia, TKN, N-N
  Phosphorus
  Chlorophyll (a,b,c)
  Continuous DO and Temp (30min increments)
  Macroinvertebrates (MH and HD)
Annually
  Sept – Oct in 2014 - macro colonization period
  May – Oct in 2015 – set early to identify low DO period
  July – Oct in 2016 – decided against earlier set
    Repeat for 2017

## Slide 7: Addressing Complications
Deployed
Retrieved
Above Water
Sedimentation
Open Water – Rmi 955.5 RDB

## Slide 8
Belleville Pool – Rmi 199.7 RDB
Belleville Pool – Rmi 172.1 LDB

## Slide 9: Addressing Complications
Cannelton Pool – Rmi 667.3 RDB

## Slide 10: Addressing Complications
Cannelton Pool – Rmi 702.8 RDB
Bio-fouling

## Slide 11: Current Status
Nutrients (TN, TKN, TP)
Productivity (Chl-a, TChl)
Dissolved Oxygen (min, Stds, Δ)
Biology (macros, ORMIn)
Establish Criterion
Breakpoint Analysis
or
Bayesian Hierarchical Model
Linear Regression/Correlation
Linear Regression/Correlation
Linear Regression/CART/Boxplots
Notes: After the QA process, preliminary analyses were conducted on the remaining data

## Slide 12: Nutrient & Chlorophyll Grab Samples
Pool | Year | Avg TN | Avg TP | Avg Chl-a | Avg Total Chl
Montgomery | 2015 | 1.093 | 0.053 | 6.175 | 7.399
Willow Island | 2016 | 1.218 | 0.063 | 4.674 | 5.981
Belleville | 2014 | 1.563 | 0.121 | 3.382 | 4.417
Racine | 2015 | 1.331 | 0.047 | 6.266 | 7.047
Greenup | 2016 | 1.114 | 0.042 | 9.218 | 11.742
Markland | 2014 | 1.450 | 0.102 | 2.682 | 3.660
McAlpine | 2014 | 1.406 | 0.143 | 2.347 | 3.055
Cannelton | 2016 | 1.419 | 0.082 | 8.761 | 
J.T. Myers | 2015 | 1.789 | 0.084 | 16.998 | 17.724
Olmsted | 2014 | 1.585 | 0.168 | 9.540 | 11.643

## Slide 13: Nutrients vs Productivity
Expectation: Vary Directly

## Slide 14: Current Status
Nutrients (TN, TKN, TP)
Productivity (Chl-a, TChl)
Dissolved Oxygen (min, Stds, Δ)
Biology (macros, ORMIn)
Linear Regression/Correlation
Linear Regression/Correlation

## Slide 15: Daily HOBO DO Data
Pool | Year | Avg mg/L | Min mg/L | Max mg/L | Range mg/L
Montgomery | 2015 | 6.92 | 7.12 (0.35) | 8.82 (16.09) | 1.83 (12.36)
Willow Island | 2016 | 6.48 | 5.27 (0.46) | 7.60 (12.35) | 1.23 (6.66)
Belleville | 2014 | 6.42 | 6.07 (0.02) | 7.90 (13.80) | 1.95 (8.54)
Racine | 2015 | 7.14 | 5.95 (0.22) | 7.16 (11.44) | 1.50 (6.89)
Greenup | 2016 | 6.96 | 5.50 (0.49) | 7.45 (13.87) | 1.20 (5.60)
Markland | 2014 | 7.04 | 6.39 (2.16) | 7.59 (10.09) | 1.00 (5.44)
McAlpine | 2014 | 7.99 | 6.61 (2.46) | 7.60 (10.74) | 1.70 (9.38)
Cannelton | 2016 | 7.28 | 5.91 (1.49) | 7.15 (13.88) | 0.86 (3.55)
J.T. Myers | 2015 | 6.55 | 6.36 (0.00) | 7.86 (13.79) | 1.21 (5.53)
Olmsted | 2014 | 6.36 | 6.88 (4.67) | 7.74 (11.45) | 2.32 (6.36)
Values shown are daily averages – values in ( ) are absolute observed per pool

## Slide 16: Productivity vs DO

## Slide 17: Current Status
Nutrients (TN, TKN, TP)
Productivity (Chl-a, TChl)
Dissolved Oxygen (min, Stds, Δ)
Biology (macros, ORMIn)
Linear Regression/Correlation
Linear Regression/CART/Boxplots

## Slide 18: Macro Colonization Period DO Data
Pool | Year | Freq Days Avg <5mg/L | Freq Diel Δ >3mg/L | Freq DO Readings <4mg/L
Montgomery | 2015 | 3.41 | 29.12 | 3.16
Willow Island | 2016 | 2.25 | 17.99 | 1.19
Belleville | 2014 | 5.45 | 19.34 | 3.92
Racine | 2015 | 4.68 | 9.84 | 0.73
Greenup | 2016 | 6.22 | 32.81 | 1.87
Markland | 2014 | 0.00 | 3.36 | 0.28
McAlpine | 2014 | 0.19 | 1.32 | 0.08
Cannelton | 2016 | 3.35 | 5.41 | 0.05
J.T. Myers | 2015 | 0.47 | 21.41 | 0.45
Olmsted | 2014 | 0.00 | 0.92 | 0.00

## Slide 19: Productivity vs DO
ORSANCO Std = Daily Average <5 mg/L
Daily Range >3 mg/L - Found by Other Agencies to be Biologically Relevant

## Slide 20: DO vs Macros (2014 & 2015 only)
2016 macro data received this week

## Slide 21: After 2017 Field Season
Nutrients (TN, TKN, TP)
Productivity (Chl-a, TChl)
Dissolved Oxygen (min, Stds, Δ)
Biology (macros, ORMIn)
Establish Criterion
Breakpoint Analysis
or
Bayesian Hierarchical Model
Linear Regression/CART/Boxplots