## Slide 1: Ohio River and Major Tributary Mercury Load Studies
Results of Tributary Monitoring Study and latest Ohio River Mercury Studies
ORSANCO Technical Committee Meeting 214
June 6-7, 2017
West Baden Springs, Indiana

## Slide 2
Mercury Projects 2010-2017
Tissue Bioaccumulation Studies 2010-2016
Tributary Monitoring 2015-2016
Total Ohio River Load Monitoring 2016-2017
Tissue Bioaccumulation Studies
  Site Specific Methyl Mercury Bioaccumulation Factor Development
  Total Mercury Mass Load Measurement/Estimation
Tributary Monitoring
  Annual Mass Mercury Loads and Yields
  Methylation Efficiency by Tributary
Total Ohio River Load Monitoring
  Lower Ohio River Mercury Mass Load Measurement
  Site Specific Methyl Mercury Bioaccumulation Factor Development

## Slide 3: 19 Mercury Project Locations
15 Major Tributary Sites
3 Completed Ohio River BAF Sites
1 Lower Ohio River “Total Load” Project Underway

## Slide 4: Bioaccumulation Projects -4 Sites
Mile 126 - in response to Axial Corp Variance Request
  Pilot with USGS May-September 2010 3 Events
  Monthly Project July 2012-June 2013 12 Events
Mile 282 – Highest Apparent Tissue Accumulation
  Monthly Project June 2015-May 2016
Mile 782 – Lowest Apparent Tissue Accumulation
    Monthly Project July 2015-June 2016
Mile 912 – Highest Water and Tissue Mercury Concentrations (lower bioaccumulation)
  Monthly Project November 2016 -October 2017

## Slide 5: Tributary Monitoring How much mercury is directly discharged to the Ohio River?
Study Period
November 2015 through October 2016
Number of Events
180 Events: One year, one per month, 15 Locations

## Slide 6: Bioaccumulation and Tributary Methods Used
Ohio River: Isokinetic, depth-integrated, Equal Discharge Increment (EDI) Composite
Trib Project: Discharge-Weighted Single Vertical (VCF) sampling

## Slide 7: Bioaccumulation and Tributary Methods Used
Ohio River Bioaccumulation Studies: 7 analyses
  Total Mercury and Methyl Mercury (Filtered and Unfiltered)
  Selenium, Total Organic Carbon, Total Suspended Solids (Unfiltered Only)
Tributary Study: 4 analyses
  Total Mercury and Methyl Mercury (Unfiltered only)
  Total Organic Carbon, Total Suspended Solids
All Sites:
  Multiparameter Datasonde variously YSI or Hydrolab
    pH, SpCond, DO, Temp, Turbidity, Chlorophyll-a, Phycocyanin

## Slide 8: Mercury Load Models
Clean Metals Program Total Mercury Detection Rate (UTHg) 2000-2017 (N-90) | 
Ohio River Location | % Detections
New Cumberland | 97%
Pike Island | 98%
Hannibal | 95%
Willow Island | 99%
Belleville | 99%
R.C. Byrd | 100%
Greenup | 98%
Meldahl | 98%
Anderson Ferry | 95%
Markland | 99%
Louisville | 98%
McAlpine | 100%
West Point | 100%
Cannelton | 99%
Newburgh | 99%
J.T. Myers | 100%
Smithland | 99%
L&D 52 | 100%

## Slide 9: Calculation Method for Load Models
Ohio River Mile 782 has the strongest model
12 Measured Total Mercury Results
  QA Dups and Blanks not incl.
ADCP Measured Flow
Test Regression
  Residual Variance is constant, independent and normally distributed
Strongest Trib model (Monongahela R. ) low p-value (<0.000) but

## Slide 10: Tributary Loads: Period of Interest Nov 2015 to Oct 2016 (Trib. Mont. and DMR data)

## Slide 11: Tributary vs Ohio Estimated Load
11 Major Tributaries are above Ohio River Mile 782
  Newburgh, Indiana immediately above the Green River
Model shows ~40 lbs THg from non-major tribs and discharges

## Slide 12: Ohio River Load Remainder after Estimated Tributary Loads
Chart: Tributary Estimated Load vs Ohio River Load (lbs THg)
| Allegheny | Monongahela | Beaver | Muskingum | Kanawha | Big Sandy | Scioto | Little Miami | Licking | Great Miami | Kentucky | Ohio River
Trib Load (lbs THg) | 71.95 | 76.31 | 25.25 | 86.38 | 162.87 | 68.96 | 94.63 | 22.5 | 17.35 | 34.1 | 123.5 | 39.1
Ohio River Load (lbs THg) | 822.9