## Slide 1: Interstate Spill Notification and Response Plan
2014th Technical Committee Meeting
June 6-7, 2017
West Baden Springs, IN

## Slide 2: Plan Purpose
Memorializes what ORSANCO does for spills Notification & Response.
Ensures that all of our customers have a common understanding of what we promise to do.
Provides a vehicle for additional input for continuous improvement.

## Slide 3: Plan Scope
ORSANCO provides notification and response to spills deemed to impact the Ohio River.
ORSANCO receives NRC notification of spills for all counties adjacent to the Ohio River plus 2 counties up the Kanawha River (Charleston).
Vast majority of spill reports ORSANCO receives are from the NRC. Occasional report from state, water utility, citizen, or unusual ODS detection.
11 OSANCO technical staff that provide
24-hour spills coverage on a weekly basis.

## Slide 4: Plan Contents
What conditions ORSANCO wants to know about.
How ODS monitoring will be used in spills detection.
ORSANCO’s Notification and Response procedures.

## Slide 5: ODS Detections
“Unusual” detections reported as a spill.
“Unusual” generally defined as:
detection > 2ppb which has been confirmed to be the result of instream conditions.

## Slide 6: ORSANCO’s Procedures
ORSANCO receives report.
Determine by best professional judgment that there is an impact to the Ohio River.
Report to state and federal emergency response agencies where lacking.

## Slide 7: 4. Drinking Water Utility Notification
When spill determined to be “significant and imminent”, utilities will be called.
“Significant and imminent” is determined by best professional judgment.
It means the utilities needs to know about it, and it needs to know quickly.
II. When spill determined to be “possible threat”:
Call water utilities within 10 miles of spill.
This includes all unknown sheens of unknown size.
III. All spills determined to impact Ohio River are
emailed to entire spills distribution list.

## Slide 8: Response
ORSANCO will provide response activities such as on-river monitoring and time-of-travel modeling when requested by state or federal agencies, or water utilities, or when ORSANCO deems it appropriate.

## Slide 9: Spill Notification Resources
ORSANCO maintains a Spill Response Directory which is updated annually which provies all contact info.
ORSANCO maintains email distribution list for spills notification.

## Slide 10: Input
Spill plan has been provided to Water Users for their input.
Will be bringing plan to ORSANCO’s Emergency Response Workgroup for input.
TEC input.

## Slide 11: Questions/Comments?
Thank You.