## Slide 1: Water Quality Observations 2009 Algae Blooms

## Slide 2: Upper River Taste and Odor Reports
Initial report to ORSANCO on June 1, 2009
  Complaints from:
    Toronto, OH (ORM 59.2)
    Weirton, WV (ORM 65.2)
    Steubenville, OH (ORM 65.3)
    Wheeling, WV (ORM 86.8)
    Later confirmed at East Liverpool (ORM 40.2) and Midland (ORM 36)
  T&O problems started on May 28.
  Weirton reported clear water on June 1.
Beaver Falls, PA water plant reported T&O problems on May 26
Conference call with PA DEP on June 5

## Slide 3: Sampling Locations
Samples collected on June 8, 2009
  Nutrients (TP, TKN, Nitrate/Nitrite, Ammonia)
  Algae community
Dashields L&D (ORM 13.3)
Beaver River (Confluence at ORM 25.4)
Montgomery L&D (ORM 31.3)
New Cumberland L&D (ORM 54.4)
Pike Island L&D (ORM 84.2)
Wheeling Water Plant (ORM 86.8)

## Slide 4: Nutrients Sample Results

## Slide 5: Algae Sample Results

## Slide 6: Lessons Learned and Future Planning
Algae issues are usually very short lived
  Response time important
Second time in 3 years we have seen spring time algae issues on the upper river
Preparation for 2010
  Sampling kits for water treatment plants
  Discussed Hydrolab placement with L&Ds

## Slide 7: Microcystis Bloom Middle River
Cincinnati Area (ORM 451-470)
  September 22- October 5
  Contacted Louisville and Huntington Water Plants
  Visual observation of near shore Microcystis in Louisville
No reports of T&O problems
Concentration greater near-shore
  Avg. near shore 1,243 colonies/ml
  Avg. mid river 247 colonies/ml
Toxicity testing not yet available

## Slide 8: Nutrients Analysis 2009

## Slide 9: Algae Analysis 2009 (Near shore vs Mid River)

## Slide 10: Flow Comparison 2008-2009

## Slide 11: Temperature Comparison 2008-2009

## Slide 12: TP at ORM 463 Comparison 2008-2009

## Slide 13: Conclusions from 2 years of blooms
Literature suggests temperatures greater than 25 C needed for Microcystis to bloom
Light penetration needed to start recruitment of spores from sediment
Water column nutrients not a limiting factor – sediment nutrients sufficient
We could have a Microcystis bloom any time the temperature and clarity coincide.